## Slide 1: Some QoS Aspects of Data via MME
Vodafone
S2-161085
3GPP TSG SA WG2 #113 ad hoc
ETSI, Sophia Antipolis, France 23-26 Feb 2016
Agenda item 5.6

## Slide 2: NB-IoT data rates
Minimum about 300 bit/s -> 40 secs for 1500 byte packet
Maximum about 120 kbit/s -> 0.1 seconds for 1500 bytes
Much less than WB-E-UTRAN
Data in “coverage extension” is very resource consuming for the VPLMN -> lower AMBR

## Slide 3: How to avoid GBR and Dedicated bearers on NB-IoT
Assume that the PDN GW/PCRF should/shall take the RAT Type into account - assume other cases are ‘abnormal’
 update Attach and PDN Connectivity procedures

## Slide 4: Policing of AMBR value
HSS “should” set a low AMBR for NB-IoT-only devices. - However, this is not guaranteed (it has implications on O&M/admin tools & processes behind the HSS – e.g. some operators might have control of AMBR from PCRF/PDN GW) - NB-IoT has quite a large data rate range (300 bps to 120 kbit/s -> factor 500) - VPLMN will want to be local master:  MME should implement local policing of AMBR VALUE for NB-IoT RAT (and not rely on HSS/PDN GW)
AMBR also applies to SCEF data

## Slide 5: Enforce AMBR in MME or eNB?
For IoT, MME could be optimised differently to a smartphone MME.
Providing AMBR enforcement in MME avoids changing the eNB to segregate siganlling and “data via MME”
For SCEF connections on WB-E-UTRAN, eNB enforcement of AMBR might be difficult / is not easily supported by S1 AP signalling if SCEF connection is in parallel to default bearers.
enforce “data via MME” data rate in MME?
Or
assume signalling volumes are small and police “MME-AMBR” for whole SRB in eNB?

## Slide 6: QoS Profiles
TS 23.203’s QCI profiles need adjusting for NB-IoT - primarily with regard to their Packet Delay Budget targets.

## Slide 7: Background information

## Slide 8: (APN) AMBR granularity
Section 9.9.4.2 of TS 24.301
APN-AMBR for downlink, octet 3
0 0 0 0 0 0 0 0 Reserved
0 0 0 0 0 0 0 1 The APN-AMBR is binary coded in 8 bits, using a granularity of 1 kbps giving a range of values from 1 kbps to 63 kbps in 1 kbps increments. 0 0 1 1 1 1 1 1
0 1 0 0 0 0 0 0 The APN-AMBR is has a range of values from 64 kbps to 568 kbps in 8 kbps steps 0 1 1 1 1 1 1 1
/…/
APN-AMBR for uplink, octet 4: Coding is identical to that of APN-AMBR for downlink.
On S1 interface 36.413 section 9.2.1.19 allocates UE AMBR to granularity of 1 bit/s (up to 10 Gbit/s) but section 9.2.1.20 also refers to TS 23.401.
 Minimum AMBR is 1 kbit/s