## Slide 1: CIoT Drafting Jan-27, 2016 (6:30 – 8:15PM) Puneet Jain
SA WG2 Meeting #113
S2-160523

## Slide 2: Agreements from Drafting session
UE requests “Non-IP” ESM session w/ PDN type = “Non-IP”
MME creates a PDN connection depending on APN and/or HSS information. MME selects SCEF or P-GW based on APN information.
UE is informed by MME which transmission method (CP and/or UP) it shall use
  If MME determines that PDN connection via SCEF shall be used, “CP only” is indicated to the UE in the ESM response.
MME will grant EBI (present range 5-15) to PDN connections via SCEF as well

## Slide 3: For further discussion offline
APN related stuff
  NB-IoT UE need not provide APN information in PDN CONNECTIVITY REQUEST
     For such UEs wanting Non-IP support, APN corresponding to Non-IP has to be the default APN in HSS
     The HSS has one default APN for PDN Type = “Non-IP”. It may point to SCEF or PDN
  Same handling for NB-IOT UE, eMTC UE and multimode NB-IOT+eMTC UE
  To allow MME to distinguish which selection procedure (S/PGW or SCEF) to invoke, a well known APN partial APN string (eg SCEF*) is used for “Non-IP” APNs
     To ensure consistent service behaviour whilst roaming, GSMA agreement might have to be obtained?
  SCEF selected by MME must be the same as SCEF selected by SCS/AS (see S2-160276)
     APN-based address resolution (scefabc.mccX.mncY.3gpp.org) can’t guarantee this
    Proposal: HSS needs to be configured w/ either hostname (scef.vf.com) OR IP address of SCEF. Similar config will be on SCS/AS.
      For SCEF hostnames which resolve to multiple SCEF IP addresses it must be ensured that those SCEF which share the hostname can share the SCEF contexts

## Slide 4: Header Compression CRs
Header compression updates to Attach procedure
  S2-160322
  It was agreed that changes should be in ESM signalling
  No need to transfer header compression context during inter node change. Header compression configuration parameters would be transferred.
  S2-160322 will be revised to S2-160516
Header compression updates to CP optimization procedure
  S2-160314
  Changes should be merged with CR in S2-160422
  S2-160422 will be revised to S2-160517