## Slide 1: RAN-CN Interface, Functional Split and Access Independence
AT&T
S2-162322

## Slide 2: Overview
RAN-CN Interface, Functional Split and impacts of minimizing access dependencies in the CN on this work have been discussed in SA2 as part of NextGen study
The key objective of this presentation is to
  Apprise RAN WGs on the work done so far in SA2 WG on the topic
  To stimulate discussion between the WGs on these topics
  To help in alignment of WGs in their work goals and timelines with respect to this topic

## Slide 3: Relevant Architectural Assumptions, Requirements and Definitions
Architectural Requirements
The architecture of the "Next Gen" network shall:
  Support the new RAT(s), the evolved LTE, and non-3GPP access types. GERAN and UTRAN is not supported:
  As part of non 3GPP access types, WLAN access and Fixed access shall be supported. Support for satellite access is FFS.
  Allow independent evolutions of core network and RAN, and minimize access dependencies.
Architectural Assumptions
The functional split between NextGen core and access network shall be defined with support for the new RAT(s), the Evolved LTE and non-3GPP access types.
A NextGen Core-NextGen RAN interface supporting new RAT(s) and the evolved LTE shall be specified.
Definitions
Evolved LTE: In the context of this document Evolved LTE is E-UTRAN upgraded to interface with the Next Generation Core.
NextGen RAN (NG RAN): In the context of this document, it refers to a radio access network that supports Evolved LTE and/or New RAT and interfaces with the Next Generation Core.
NextGen System (NG System): It refers to NextGen System including NG RAN and NextGen Core.
(from NextGen TR 23.799)

## Slide 4: Key issue 8: Next Generation core and access - functional division and interface
This key issue will address the following general aspects:
analyze in detail the functionality for the Next Generation Core and for the interface between the access networks and the Next Generation Core to support the LTE radio access network, the new, expected 5G radio access network (depending on information available from RAN design and the SMARTER requirements), and for non-3GPP access networks, in order to identify the functional split between AN and Core Network, and to identify if a single AN-CN interface can be specified which can be used across many different access networks. In particular, the functionality should be decomposed between:
access-specific functionality: such functionality applies only to a specific (set of) AN(s)
access-independent functionality: such functionality applies to all ANs, though the set of information/parameters/policies used for the functionality may be dependent on the specific AN
identify how the various functionality correlate to each other and identify interdependencies – i.e. impacting Next Generation Core, AN and UE
(from NextGen TR 23.799)

## Slide 5: Key issue 8: Next Generation core and access - functional division and interface
identify how the functionality can be modularized for the definition of a modular Next Generation Core -ANs interface that minimizes access dependencies and applies to any access networks
identify how to decouple the access network and the core network, and identify its effects and implications to the Next Generation Core. Such decoupling shall allow for parallel and independent design and evolution of access networks and core networks
Solutions and agreements for 3GPP RAN specific aspects should be prioritized in order to facilitate cooperation with 3GPP RAN. Aspects to consider for such solutions include e.g. functions which have impact to both CN and RAN, desired NextGen Core - RAN functional split and interface. The new RAT(s) and the evolved LTE should be taken into considerations.
NOTE: This key issue has dependencies on the solutions specified for other key issues such as QoS framework, Mobility framework, Session Management.
(from NextGen TR 23.799)

## Slide 6: Implications of Access Independence on RAN-CN Interface and Functional Split
High level principles to interpret the requirements of minimizing access dependencies for key core network functionalities
Captures RAN-CN interface aspects as well from the perspective of making it non access specific.
QoS
QoS related parameters and QoS related signalling between the core network and access network is non access specific. For example QoS needs on a per IP flow basis are signalled to the access network via non access specific signalling using non access specific QoS parameters. Within the access network the conversion to access specific QoS parameters and signalling can occur as needed.
Authentication
Authentication framework used between the core network and access network is non access specific. The security methods (e.g. EAP AKA) used for authentication can however be access specific if needed.
Charging Framework
Charging Framework that includes functions responsible for charging data collection and communication will be non-access specific. The actual charging data collected maybe access specific however. This functionality is contained within the CN and has no implications for RAN-CN functional split.
(from Annex F of NextGen TR 23.799)

## Slide 7: Implications of Access Independence on RAN-CN Interface and Functional Split
Policy Framework
The policy framework that includes for example a concept of a policy controller, policy enforcement points, etc. will be non-access specific. There will however be access specific policies that may require for example access specific additional policy decision, communication and enforcement. This functionality is contained within the CN and has no implications for RAN-CN functional split.
Session Continuity
Sessions continuity functions in the core network will be non-access specific. The access network may have access specific session continuity mechanisms that are not visible to the core network.
Session Management
Session management functions such as techniques for allocation of IP address will be non-access specific. For any access specific session management functionality that is identified, the transport (e.g. IP) for carrying access specific session management signalling over RAN-CN interface will be non-access specific.
Mobility Management
Mobility management functions will be access specific. However the transport (e.g. IP) for carrying access specific mobility management signalling over RAN-CN interface will be non-access specific.
(from Annex F of NextGen TR 23.799)

## Slide 8: Implications of Access Independence on RAN-CN Interface and Functional Split
Minimization of Access dependencies and CP/UP functional split
It is likely that there will be some access specific functional entity(ies) left in the CN for example to handle mobility management. This will result in possible communication between both access specific and non-access specific functional entities in the control plane and user plane.
CP/UP communication functionality between non access specific functional entities in CP and UP will also be non-access specific.
CP/UP communication functionality where at least one of the functional entities is access specific will also be access specific but it can possibly use an existing CP/UP interface with access specific extensions.
Carrying of Access Specific information over AN-CN
Access specific functionalities in the network should be isolated from non-access specific functions. When access specific entity(ies) exist in the core network and they have to communicate over RAN-CN interface it is possible to consider taking the following actions;
Use a non-access specific transport (e.g. IP) to carry traffic to a core network functional node specific to that access technology.
Possibly use a transport header extension to identify an access technology and based on that route the packet to right control plane entity.
(from Annex F of NextGen TR 23.799)

## Slide 9: Next Gen System, CN and Standardization Timelines
Development of a new system architecture including a new core network is a significant standardization effort. Completion of this task will take multiple 3GPP releases. A timely completion of this work that meets various deadlines for anticipated technology trials and deployments can be achieved with the help of proper planning. The goals of the planning include;
    An early availability of basic system for trials and limited deployments that fulfils the goals and expectations set about for Next Generation of System including the Core Network.
    Building of a complete and feature rich system using the basic system defined in step 1 as a foundation thereby ensuring backwards compatibility within Next Gen Ecosystem.
    (from Annex C in NextGen TR 23.799)

## Slide 10: Preferred areas of contributions for R-14 (to help specify basic NG system in R-15)
Functionality needed
  QoS
  Charging
  Policy
  Authentication
  Mobility management
  Session continuity
  Session management
  (from Annex C in NextGen TR 23.799)
Architectural enablers to be addressed
  Minimizing access dependencies (incl. non-3GPP access integration aspects).
  Shared network and roaming scenarios
  CP/UP separation
  RAN-CN functional split
  Architectural impacts of scaling
  Network slicing
  Co-existence, migration and interworking
  Network functions granularity and interaction between them
These lists are a work in progress and can get updated as work progresses e.g. based on new key issues introduced into the TR and feedback from RAN WGs.

## Slide 11: 3GPP Timeline for Next Gen (NG)
A phased NG approach needs to address NG system architecture and NG CN in the initial phase
  Work on NG System Architecture and NG CN needs to be aligned with NG radio work for timing and content
  We believe a baseline NG System Architecture and CN work can be completed in Release 15. Its features can further be enhanced in Release 16
  Launching of a NG RAT without a NG System / CN will impact target timelines for a deployment of a NG System / CN
    Increases dependency of new NG RAT on legacy EPC and creates complex roaming scenarios for NG
A phased approach that results in fragmentation of 5G ecosystem should be avoided
  A phased approach towards NG work should not result in non-compatible NG UEs and base stations for different phases of NG
Operator expectations for the launch of NG networks are:
  UE’s and NG RAN will be compatible for different NG phases
  A solution that allows independent evolution of core network and RAN, and minimizes access dependencies