## Slide 1
NextGen System Migration Scenario and Roaming
China Mobile, ???
2016-8
SA WG2 Meeting #116bis S2-164658
29 August – 02 September 2016, Sanya, China
NOTE: this contribution generated based on S2-164017, the SA2 email discussion, and offline discussion among some operators.

## Slide 2: 1. Migration and Roaming Principles
The deployment of NextGen System without interworking between EPC and NG-Core is the long time final goal after migration (under the assumption the EPC may still last for a long time to provide legacy or roaming UE support).
NextGen System’s requirements therefore should not be compromised to improve interworking between EPC and NG-Core or to fit a specific migration path
Any interworking functionality between EPC and NG-Core shall be developed in a manner that
  Minimizes impacts to EPC as well as to the NextGen core
  Does not create any permanent dependencies for NG-Core on interworking to EPC even after the migration is completed
To avoid market fragmentation, UE forward compatibility shall be achieved

## Slide 3: 2. Assumptions on UE Capability
Assumption C0: A UE that supports any NG RAN also has LTE/EPC capability
Assumption C1: the NG CP stack can only be used by one RAT at any instance (either NR or eLTE) and cannot be used by both RATs at the same time.
Assumption C2: the NG CP stack can be used by either NR or eLTE within a UE based on the network deployment
Observations:
  If C1 host, there will have different categories of UE with variant capabilities and UE with multiple capabilities, e.g., Opt 3+7, Opt 3+7+2
  If C2 is true, the UE on the Option 2/4/7/5 are essentially the same
Note: whether C1 or C2 is true needs to discuss with RAN TSG.

## Slide 4: 3. Interworking and Migration scenarios within an operator
LTE/EPC -> Option 2/Option 4
LTE/EPC -> (Option 3) -> Option 7 -> Option 2/Option 4
Any alternative combinations or sequence of deployment and/or transition flows involving options 3, 7, 2/4 would similarly need to be supported. For example, two of the migration paths are illustrated as:
NOTE1: Option 7 and Option 3 can coexist in the same PLMN at the same stage
NOTE2: the support of Option 7 implies that Option 5 will also be supported.
Recommendation:
  Under Assumption C2, from SA2 perspective the interworking scenario generated from the migration paths can possibly be simplified as: LTE/EPC and NG System
Notes: 增加AT&T；很多场景
Docomo: deployment scenario

## Slide 5: 4. Interworking scenarios on roaming
Roaming Scenarios should be considered in R14:
  Option 2/ Option 4 <-> Option 7/5
  Option 2 / Option 4 <-> Option 3
  Option 2 / Option 4 <-> LTE/EPC
  LTE/EPC <-> Option 7/5
  Option 3 <-> Option 7 /5
  LTE/EPC <-> Option 3
  (1: means VPLMN is Option 2/4, HPLMN is Option 7/5; or HPLMN is Option 2/4, VPLMN is Option 7/5)
  Recommendation
  Under Assumption C0, a NextGen UE will get at least LTE/EPC service where LTE/EPC exists. On top of that, it will be able to use any NG RAN in the VPLMN that it supports and that the roaming agreement allows.
  Rather than the roaming interface, it worth investigating whether the different Options of the NextGen system lead to impact and requirement in the roaming
  Under Assumption C2, the roaming scenarios are simplified to the following cases:
    EPC in VPLMN, NG Core in HPLMN
    NG Core in VPLMN, EPC in HPLMN,

## Slide 6: 5. Forward Compatibility
Forward compatibility requirement is based on operators deploying either Option 3 and/or Option 7. Option 7 should be backwards compatible to Option 3. This translates into two main requirements/goals:
  (a) UE supporting Option 7 should also support Option 3
  (b) Network supporting Option 7 should also provide Option 3 service to UEs supporting Option 3.

## Slide 7: 6. Proposed Way Forward
Discuss the UE capability assumption on P3 and determine whether a Draft LS to RAN is needed
Capture Section 1-5 in the TR 23.799

## Slide 8: Annex 1: Type of connectivity for different UE types under different serving networks
 | Serving Networks |  |  |  | 
UE Types | Legacy LTE | Option 2/4 | Option 3 | Option 7 | Option 5
Legacy LTE UE | LTE/EPC Connectivity | LTE/EPC Connectivity | LTE/EPC Connectivity | LTE/EPC Connectivity | LTE/EPC Connectivity
Option 2/4 UE | LTE/EPC Connectivity | Option 2/4 Connectivity | LTE/EPC Connectivity | LTE/EPC Connectivity | LTE/EPC Connectivity
Option 3 UE | LTE/EPC Connectivity | LTE/EPC Connectivity | Option 3 Connectivity | LTE/EPC Connectivity Option 3 Connectivity is required | LTE/EPC Connectivity
Option 7 UE | LTE/EPC Connectivity | LTE/EPC Connectivity | LTE/EPC Connectivity Option 3 connectivity is required | Option 7 Connectivity | Option 5 Connectivity
Option 5 UE | LTE/EPC Connectivity | LTE/EPC Connectivity | LTE/EPC Connectivity | Option 5 Connectivity | Option 5 Connectivity
Option 3+7 UE | LTE/EPC Connectivity | LTE/EPC Connectivity | Option 3 Connectivity | Option 7 Connectivity | Option 5 Connectivity
Option 3+7/5+2/4 UE | LTE/EPC Connectivity | Option 2/4 Connectivity | Option 3 Connectivity | Option 7 Connectivity | Option 5 Connectivity
  The following table is obtained based on Assumption C1 (UE types indicate the HPLMN deployment).
  If the Assumption C2 holds, there will be no different types of UE. The Connection will collapse to the last row

## Slide 9: Annex 2: Deployment Options
Option 2
Option 3
Option 5
Option 7
Option 4