## Slide 1
Network sharing for flexible and cost-efficient
5G coverage in residential, commercial, and industrial properties
NICT, ATR
2016-10
SA WG2 Meeting #117 S2-165542
17 – 21 October 2016, Kaohsiung City, Taiwan

## Slide 2: Background
As stated in [22.864-e00]:
  “5G network deployments are expected to range from large-scale macro networks to small-scale residential deployments, including medium-scale networks covering industrial and commercial properties. These networks will need to be identified is such a way as to enable an operator to define policy enabling roaming/redirection onto specific networks for enhanced user services and operator traffic management.”
Corresponding potential requirement [PR 5.7.2.1-003]:
  “The 3GPP system shall provide a mechanism for a network operator to direct a UE to onto a partnership Mobile Network for the purposes of data offload.”
This contribution aims at providing a flexible and cost-efficient 5G coverage in residential, commercial, and industrial properties.

## Slide 3: Scenario and Assumptions
Micro cells of Local Area Operator X may have better coverage inside this specific local area than micro cells of Large Area Operator A
AND/OR
Micro cells of Local Area Operator X are capable of supporting one or several sets of QoS requirements tailored for specific classes of applications compared to micro cells of Large Are Operator A (for example, tailored for high data rate or low latency applications)
Operator A is large-area network operator
Operator X is local area network operator (for example, inside residential, commercial, or industrial property)
F1 is lower frequency allocation
F2 is new higher frequency allocation used for micro cells

## Slide 4: Options to Provide Connection to an Application
Option 1
Large Area Operator A macro cell is used for control information
Large Area Operator A micro cell or Local Area Operator X micro cell is used for data (selection is based, for example, on coverage, required QoS requirements)
Option 2
Local Area Operator X micro cell is used for data
Large Area Operator A macro cell or Local Area Operator X micro cell is used for control information (selection is based, for example, on required CN functionality)

## Slide 5: Proposal
Related key issues from [23.799-102] (most relevant first):
  Key issue 17: 3GPP architecture impacts to support network discovery and selection
  Also, key issues 10, 3, 4, and 6 may be related
Proposed update to TR [23.799-102] for network sharing for flexible and cost-efficient 5G coverage in residential, commercial, and industrial properties is described in S2-165543
  The contribution S2-165543 is proposing additional solution to the key issue 17 that will enable scenario described in this presentation