## Slide 1
Observations on Network Slicing Approaches
Qualcomm Inc.
3GPP TSG SA WG2#117, Oct 17 – 21, 2016, Kaohsiung City, Taiwan
S2-166055

## Slide 2: Network slicing and background
Network slicing requirements:
  CN related:
    Selection of a CN node which enables particular slice(s).
    Selection of a particular Service Slice based on e.g. SLA
  RAN related:
    Selection of RAN resources with specific characteristics (i.e. RAN slice)
Related previous 3GPP work
  Rel-13: DECOR was built specifically for dedicated CN node reselection at the CN
  Rel-14: eDECOR was built specifically for UE assisted dedicated CN node selection at the RAN
  Let’s build on it to enable network slicing!!
Network Slicing requirements and DECOR/eDECOR support:
  CN related:
    Selection of a CN node which enables particular slice(s) -> Supported by DECOR/eDECOR
    Selection of a particular Service Slice based on e.g. SLA -> Extension needed
  RAN related:
    Selection of RAN resources with specific characteristics (i.e. RAN slice) -> Extension needed
In the next slides we study:
  Existing 3GPP work: eDECOR
  Existing proposals: MDD, eDECOR extension
  Proposed way forward

## Slide 3: eDECOR Overview
eDECOR: UE assisted DCN selection performed at the RAN.
  Introduces concept of DCN ID:
    UE provides a DCN ID in RRC signaling, eNB selects MME based on that DCN ID.
    Two types of DCN IDs:
      PLMN specific DCN ID -> Provided by the visited PLMN to be used by UE in subsequent procedures.
      Default standardized DCN ID -> To be used by UE if no PLMN specific is stored.
    An MME may serve more than one DCN ID.

## Slide 4: Extend DCN ID (eDCN ID) Approach
Several solutions where NSSAI is a signle dimensional parameter (similar to DCN ID)
  In some solutions it’s used in conjunction with APN for slice selection
Discussion has taken place on extending DCN ID to an “eDCN ID” to include concept of eDECOR DCN ID plus specific customer identification

## Slide 5: MDD Approach (sol. 6.1.2)
UE provides set of Multi-Dimensional Descripto (MDD) vectors = “Slice Type” + Tenant ID
  “Slice type” is equivalent to the usage of DCN ID
    Can be standardized or not, and can be VPLMN-specific
    Identifies a NST
  Augmented with an identification of the slice customer (Tenant ID) to identify a specific SLA
    Identifies specific CN resources for the customer
    Identifies RAN resources enabling RAN Slicing
    Specifically identifies the RAN part of an SLA plus network part of an SLA and the specific customer

## Slide 6: Qualcomm Proposed Compromise
Not a NEW solution, just clarifications on use multidimensional slice information

## Slide 7: Qualcomm Observations
Ability to identify specific customer and specific SLA for an NST is important to provide better granularity than eDECOR and enable RAN slicing
A single parameter for identifying all the information (slice type and SLAs) is not sufficient
  DCN ID/”Slice Type”/NST ID shall identify only an NST, not the customer also
  Specifically, when VPLMN returns VPLMN-specific values, it should only modify the DCN ID part of a multidimensional NSSAI to enable correct identification of CN resources for a specific customer
    Expecting VPLMN to understand the HPLMN-specific aspects is unrealistic
Suggested way forward:
  NSSAI provided by UE in RRC and in NAS
  NSSAI is multi-dimensional (let’s call it MDD as an example)
  MDD = slice type (functionally equivalent to DCN ID) + “customer ID”
    DCN ID to identify NST
    Customer ID: Tenant ID (either single value or split in RAN and CN component is FFS)
  VPLMN returning VPLMN-specific DNN means returning VPLMN-<specific DCN ID + unmodified customer ID>

## Slide 8
UE
HSS
DNS
RAN
CN-CP
GW
VPLMN
HPLMN
Standard DCN-ID (X bits)
UE Usage Type (8 bits)
CN-CP
GW
DCN-ID
Select CN node based on DCN-ID
NAS
DCN-ID
DNS
DNS req (APN+UE Usage Type)
DNS req (APN+UE Usage Type)
Select GW
DÉCOR/eDECOR
1 DCN per UE
No support for RAN slicing

## Slide 9
Multiple slices per UE
UE
HSS
DNS
RAN
GW
VPLMN
HPLMN
Standard DCN-ID(s)+tenant-id(s)
UE Usage Type(s)+Tenant(s)
CN-CP
GW
Select CN node based on DCN-ID and tenant
NAS
DCN-ID+
Tenant-ids
DNS
DNS req (APN+UE Usage Type+tenant)
DNS req (APN+UE Usage Type+tenant)
Select GW
NW slicing
CN-CP
DCN-ID(s)
+Tenant ID(s)
Possible support for RAN slicing

## Slide 10
UE
HSS
DNS
NSSAI-v=SST(s)+tenant-id(s)
RAN
GW
VPLMN
HPLMN
NSSAI-v(s)
NSSAI(s)
GW
Select CN node based on DCN-ID and tenant
NAS
NSSAI-vs
DNS
DNS req (APN+NSSAI-v)
DNS req (APN+NSSAI-v)
Select GW
NW slicing (cont.)
CCNF
Multiple slices per UE
Possible support for RAN slicing