## Slide 1: RAN impact due to: 5G System Features
Devaki Chandramouli (Nokia)

## Slide 2
Objective
Objective of this document is to collect and track all the open items in SA2 that are pending resolution due to dependency on RAN.
Note: In some cases, the same open item may also impact on other WGs however focus of this slide-set is to collect the items that are pending RAN impact.

## Slide 3
Impacts to RAN due to Network Slicing
To be discussed in RAN based on SA2 considerations:
  Whether NSSAI in RAN and NAS are exactly the same.
  How to provide policies for the limitation of UP resources assigned to a tenant.
  Ensuring uniform service within a given registration area
SA2 FFS with RAN impact:
  How to support initial access (i.e. RRC connection establishment) policies that are aware of the slices used by the UE, thus allowing allocation of different C-plane resources per tenant or have some different priority level per slice. This should work irrespective of dedicated resource allocation at physical layer.
RAN specific discussion items:
  How to guarantee a minimum level of UP resources to a tenant?
  Discuss whether some slices could have dedicated phy layer resources and if so how would that work.
  Impact on Random access channel and whether there could be dedicated resources for certain slices.
  Consider the case of cells dedicated to certain slices and therefore imply that some restrictions to use these apply (end the impact on Idle mode procedures)
  Impact on RAN Slicing due to Connected mode HO
  Impact on RAN slicing due to idle mode mobility

## Slide 4
Impacts on RAN due to QoS
It is up to RAN WGs to decide whether RAN needs to be aware which QoS rule is the Default QoS rule.
NG2 signalling related to QoS, outside of PDU Session establishment, corresponding to a pre-authorised QoS rule should be minimised for initiation, modification or termination of SDFs with no GBR requirements. This is target for SA WG2, but the feasibility needs to be confirmed by RAN WG.
How RAN maps QoS flows onto access-specific resources based on the NG3 marking is up to RAN WGs to decide.
Need for U-plane marking from RAN to the UE for reflective QoS is up to RAN WG2 decision.
It is up to RAN to define the AS-level QoS of DRBs and how uplink and downlink packets (with the associated QoS profile (A- or B-type) and the associated PDU Session information) are mapped to DRBs.
it is up to RAN to ensure that UL traffic is sent to Core with a Flow Id that maps to the QoS of the UL radio resource used to send this traffic

## Slide 5
Impacts to RAN due to Mobility Management
Paging/reachability detection, UL/DL transport, UE capability exchange, access priority etc.
Details of CN assistance for RAN paging will be developed in coordination with the RAN WGs.
  For RAN paging CN may provide assistance information to AN. The necessity and the detailed procedure of RAN paging is RAN WG decision.
Need for RAN level tracking to be decided by RAN; How to do the RAN level reachability detection and notify to the CN in case UE is unreachable is to be decided by the RAN WG.
  Notification of CN if the UE is unreachable in the RAN paging area is TBD by RAN WG
  Fall back to CN paging after RAN paging failure (or loss of coverage) is foreseen
For UE in “MO only” mode, the CN needs to inform RAN that the UE will not listen to paging
  e.g. RAN may decide to never keep an inactive “MO only” mode UE in RRC Inactive state.
SA2 agreed whether to define procedures to support the Close Subscriber Group (CSG), including the hybrid access mode, is to be determined during normative phase.
Network control of UE mobility via handover or cell re-selection

## Slide 6
Session Management
Support of WLAN integrated at RAN level is under RAN responsibility, and CN related aspects will be considered as needed based on RAN decision.

## Slide 7
Congestion and Overload functionality
SA2 expects to support congestion and overload control to prevent MM and SM signaling requests from UEs
Interaction with Access control (e.g. ACB) functionality needs to be determined with RAN

## Slide 8
Interworking and migration
5GS-EPS handover
  Measurements on other RAT & target selection (both)
    RAN impact due to measurements on other RATs
    RAN impact due to Inter RAT HO triggers:
      Due to S1AP/NGAP message (single-registered); due to RRC message (dual-registered)
  Use of transparent containers for context transfer (single-registered only)
    Whether transparent containers for intra-5G System but inter-RAT HO can be reused is FFS.
  PDU forwarding (single-registered only)
    Bearer-QoS flow mapping, in-sequence delivery, direct/indirect PDU forwarding, etc.
    Whether PDU forwarding mechanism for intra-5GS inter-RAT HO can be reused is FFS.
Migration
  Indication of support for connectivity to NGC by eNB
  CN selection in the eNB based on input from the UE

## Slide 9
Network Discovery and selection
SA2 assumes that Rel-14 network discovery and selection mechanism will be the basis of the work in the normative phase.
Whether network selection or PLMN selection is impacted due to 5G system features will be decided in normative phase.

## Slide 10
Policy Framework
SA2 expects support for RFSP index also with NR

## Slide 11
NextGen Core support for IMS
SA2 agreed that NGS can support IMS multimedia services, including emergency call.
If there are scenarios where NR cannot support IMS multimedia services, it is expected to be identified by RAN WG(s). If such a scenario is identified, intra-NGS RAT/frequency change and/or inter-system mobility procedures to EPS (LTE) defined for EPS-NGS interworking are needed.
Support for emergency services entails RAN impact for support of “unauthenticated emergency session”, location services (positioning) over 5G RAN.

## Slide 12
RAN – CN Functional split
Location: | 5G RAN | NextGen CN
Function: |  | 
Key issue #1 Network Slicing |  | 
CN instance selection when UE attach to a CN network slice | FFS | FFS (X)
Key issue #3 Mobility Management |  | 
Mobility management control, (Subscription and Policies) |  | X
Determination of mobility restriction |  | X
Roaming restrictions execution |  | X
Mobility restrictions execution, [CN Connected] | X | 
Mobility restrictions execution, [CN Idle] |  | X
Red text shows resolution proposal for items that are marked as FFS in the TR 23.799

## Slide 13
RAN – CN Functional split
UE registration |  | X
Area tracking | FFS (The need for RAN level area tracking is for RAN WGs to determine). | X
UE unreachability detection |  | X
RAN UE unreachability detection | X | 
NAS state transitions |  | X
RRC state transitions | X | 
Paging initiation and control in RAN Inactive state | X | 
Paging initiation in CN Idle state |  | X
Access Stratum UE Context storage in RAN Inactive state | X | 
Control of connected state mobility | X | X
Red text shows resolution proposal for items that are marked as FFS in the TR 23.799

## Slide 14
RAN – CN Functional split
UP buffer for UE in CN Idle state |  | X
UP buffer for UE in RAN Inactive state | X | 
Session Management |  | 
PDU Session address allocation |  | X
PDU Session Termination Point |  | X
KI#4 Session Management |  | X
Termination of UP security | FFS (X) | FFS (ongoing discussion in SA3)
Subscription Data Handling (incl. default QoS profile) |  | X
Authentication and Key Agreement |  | X
UP buffer for UE in CN Idle state |  | X
Red text shows resolution proposal for items that are marked as FFS in the TR 23.799

## Slide 15
RAN – CN Functional split
QoS |  | 
Radio Resource Admission Control | X | 
Radio Resource management (QoS attributes) | X | 
Max rate control | X | X
QoS Policy Control |  | X
Transport marking | X | X
Charging Data Collection |  | X
Packet classification of DL packets for QoS differentiation on the Radio | FFS | FFS X
QoS differentiation and verification for UL packets | FFS X (QoS Flow -> DRB) | FFS X (SDF -> QoS flow)
QoS |  | 
Red text shows resolution proposal for items that are marked as FFS in the TR 23.799