## Slide 1: Discussion on CCNF relocation
Samsung
3GPP SA WG 2 Meeting#118bis
16 – 20 January, Spokane, Washington, USA
S2-170279

## Slide 2: CCNF relocation during initial attach
SA2 TR conclusion
Scenarios
  Scenario 1: UE did not provide any NSSAI in the Initial Attach message
    initial CCNF = default CCNF
    The initial CCNF may create a new NSSAI based on e.g. operator policy, subscription info, etc. and include the new NSSAI in the redirection message.
    No NSSAI ≠ new NSSAI
    CCNF relocation occurs due to the change of NSSAI.
  Scenario 2: RAN selects a CCNF using NSSAI, but the initial CCNF updates the NSSAI
    initial CCNF ≠ default CCNF
    The initial CCNF updates the NSSAI based on e.g. operator policy, subscription info, etc. and includes the updated NSSAI in the redirection message.
    NSSAI ≠ updated NSSAI
    CCNF relocation occurs due to the change of NSSAI.
  Scenario 3: RAN is not able to select a proper CCNF
    initial CCNF = default CCNF
    The initial CCNF includes the same NSSAI sent by the UE in the redirection message.
    NSSAI = NSSAI
    CCNF relocation occurs due to the wrong decision by RAN. Routing information at RAN may need to be updated.
  Scenario 4: RAN selects a CCNF, but the CCNF is not a proper CCNF
    initial CCNF ≠ default CCNF
    The initial CCNF includes the same NSSAI sent by the UE in the redirection message.
    NSSAI = NSSAI
    CCNF relocation occurs due to the wrong decision by RAN. Routing information at RAN may need to be updated.
During the initial Attach procedure, in case the CCNF to serve the UE is to be redirected, the CCNF, which first receives the initial Attach request, shall be able to redirect the initial Attach request to another CCNF via the RAN or via direct signalling between the initial CCNF and the target CCNF. The redirection message sent by the CCNF may include an information about the new CCNF to serve the UE.
S2-170279

## Slide 3: How to find another CCNF
Opt1 : CCNF by itself
  CCNFs have direct or indirect connection with neighbor CCNFs and exchange their capabilities.
  Each CCNF maintains network topology information including neighbor CCNF’s capabilities.
  The initial CCNF selects the target CCNF based on the topology information.
Opt2 : via NF repository
  Use NF selection and discovery function (KI#7)
    CCNFs register at the NF Repository. The NF repository maintains profile of each CCNF including CCNF’s capabilities.
    The initial CCNF asks NF repository to find a proper CCNF which has required capabilities.
    The NF repository selects the target CCNF based on the NF profile and responds to the initial CCNF with the target CCNF information.
Proposal
  Opt1 requires connection between each CCNFs and whenever any of those CCNFs changes its capabilities, then the other CCNFs which are connected to the CCNF also need to update the information.
  Therefore, we propose to choose Opt2.
<Opt1 >
<Opt2 >
S2-170279

## Slide 4: How to redirect the request
Opt1 : via RAN
  Initial CCNF sends redirection message to RAN.
    The redirection message includes the target CCNF information, the original NAS request(Initial Attach) and the new NSSAI if the NSSAI is changed(scenario 1 & 2).
  RAN reroutes the initial attach request.
Opt2 : via direct signalling-1
  Initial CCNF sends redirection message to the target CCNF.
    The redirection message includes the RAN terminating point, the original NAS request(Initial Attach) and the new NSSAI if the NSSAI is changed(scenario 1 & 2).
  The target CCNF sends the initial attach response to the UE via RAN directly.
Opt3 : via direct signalling-2
  Initial CCNF sends redirection message to the target CCNF.
    The redirection message includes the original NAS request(Initial Attach) and the new NSSAI if the NSSAI is changed(scenario 1 & 2).
  The target CCNF sends redirection response to the UE via the initial CCNF.
    The redirection response message includes the NAS response(Initial Attach response).
  The initial CCNF forwards the NAS response and redirection information to RAN.
Proposal
  Opt3 requires initial CCNF to be involved to complete CCNF relocation while Op1 and Opt2 doesn’t. Opt3 requires additional procedure to setup initial context between RAN and the target CCNF.
  Therefore, we propose to choose Opt1 and Opt2.
<Opt1 >
<Opt2 >
<Opt3 >
S2-170279

## Slide 5: Thanks!
S2-170279