## Slide 1: Local Area Data Network Discussion, Solution Update, Evaluation
Jicheol Lee
2016. 11. 08
Samsung Electronics

## Slide 2
Concept of Local Area Data Network
Technical Issues
Proposed Solution Update
Solution Evaluation

## Slide 3: Concept of Local Area Data Network
Definition
  A Local Area Data Network is a new type of Data Network which the UE can connect to with Local Area PDU session only where the UE is located in a certain area (i.e. list of Tracking Areas)
Operation
  The available DN configuration information is initially configured to the network (i.e. MM) and informed to the UE during attachment or tracking area update procedure.
  The UE may initiate the PDU session within the DN allowed area when it is needed or initiate the PDU session immediately after the UE detects that it enters the DN allowed area.
Use cases
  the enterprise network, stadium, special event or concert as well as IoT service.

## Slide 4: Technical Issues
Solution 4.25: Local Area Data Network (current solution accepted at Sanya meeting)
  The network may indicate to the UE the availability of the Data Network and the allowed area of the Data Network.
  Editor’s Note: it is FFS how the allowed area is defined
  Editor’s Note: it is FFS whether network triggers PDU session establishment when the UE enters the allowed area.
  If the UE receives the information of the available Data Network, the UE may initiate the PDU session establishment procedure when it is needed.
  Editor’s Note: It is FFS how the network provides the information to the UE of the available DNs.
  Once the UE and the network established the PDU session, the PDU session is maintained while the UE moves within the area. The established PDU session is disconnected or becomes invalid when UE leaves the area.
  Editor’s Note: it is FFS whether and how the PDU session should be terminated when the UE leaves the area
  Editor’s Note: it is FFS how to minimize signalling when the UE moves repeatedly between an area where the local area data network and one where the local area data network is not allowed.
Next slides resolves the technical issues addressed as the “Editor’s Note”s during the meeting one by one.

## Slide 5: 1. How the DN allowed area is defined
Technical Issue 1. How the allowed area is defined
  As a finest granularity of the allowed area for the Data Network, we have considered four possibilities as described in the table below.
  Based on the above analysis, it is proposed to re-use a tracking area as a finest granularity of the DN allowed area.
Proposal 1. It is proposed to define DN allowed area as a list of tracking areas per UE’s PDU session. It is configured based on the operator’s policy.
  The UE is able to detect the entrance and the exit of the DN allowed area by checking tracking area.
  When the UE detects the entrance or exit of the DN allowed area, the UE may perform the tracking area update procedure in order to indicate whether the PDU session is enabled or not.
Granularity of DN allowed area | Advantage | Disadvantage
A. Tracking Area | Re-using the tracking area | Dependency with TA.
B. Newly defined area | Clear | RAN change is required
C. Cell id | Fine granularity | Not flexible
D. RAN paging area | Suitable for the small area | Only works for CN active state.

## Slide 6: [Annex] Example configuration of LADN
a. Adjacent allowed DN areas without overlapping area
b. Adjacent allowed DN areas with overlapping area(s)
TAI list = { TA1, TA2, TA3, TA4, TA5, TA6, TA7, TA8, TA9 }
DN allowed area A = { TA1, TA2, TA3, TA4 }
DN allowed area B = { TA5, TA6, TA7 }
TAI list = { TA5, TA6, TA7, TA8, TA9, TA10 }
DN allowed area A = { TA5, TA6, TA7 }
DN allowed area B = { TA7, TA8, TA9, TA10 }

## Slide 7: 2. Network trigger vs. UE requested PDU session
Technical Issue 2. Whether network triggers PDU session establishment when the UE enters the allowed area.
  We don’t find a critical application which inevitably requires the network triggered PDU session establishment. In case of the application which requires the notification service when the UE enters the area, it can be implemented by UE requested PDU session establishment immediately after the UE enter the allowed area. So instead of the network triggered PDU session establishment, we propose to add a PDU session type which requires the immediate PDU session establishment when the UE enters the DN allowed area.
Proposal 2. It is proposed to add a PDU session type which indicates whether the immediate PDU session establishment is required when the UE enters the allowed area.
  The UE receives the information that PDU session(s) is/are available in certain tracking area(s) among the TA list received during the attachment or tracking area update. The information may include an immediate setup indicator for each PDU session to be established immediately after the UE enter the DN allowed area. If there is no such indicator (i.e. default), the UE initiates PDU session establishment when the UE decides it is needed.

## Slide 8: 3. How the network provide the information
Technical Issue 3. How the network provides the information to the UE of the available DNs
  We have considers three options as described in the table below.
Granularity of DN allowed area | Advantage | Disadvantage
A. Broadcast allowed area to the UE (together with the newly defined area) | Per-UE provisioning or indication is not needed | - Overhead Broadcast message overhead - Per-UE configuration is not possible - RAN impact to change and configure the area.
B. Provisioning the allowed area to the UE | Per-UE configuration is possible | Unnecessary information is provisioned when the UE is located far away from the configured area
C. Per-UE indication of the allowed area | Per-UE configuration is possible | 
Proposal 3. Per-UE indication of the allowed area is proposed. The availability of the DN allowed area is informed to the UE during the attachment procedure, tracking update procedure or a separate DN allowed area indication procedure.

## Slide 9: 4. PDU session is suspended when the UE leaves the area
Technical Issue 4. Whether and how the PDU session should be terminated when the UE leaves the area
  Based on the UE movement, it is preferred not to terminate the PDU session immediate after the UE leaves the area because it can moves back to the allowed area soon. If the PDU session is terminated and established again, all the process including IP address assignment and NG3 session establishment is required, which increases complexity.
Proposal 4. It is proposed to introduce the PDU session suspended state for the PDU session.
    Instead of terminating the PDU session, we may disable (or suspend) the PDU session where the UE is located out of DN allowed area. When the PDU session is suspended, the UE and the network drops the traffic.
    When the UE comes back to the DN allowed area, the PDU session is resumed. The UE updates the UE location by performing tracking area update procedure for the network to update the PDU session status.

## Slide 10: 5. Signaling when UE moves across the allowed area
Technical Issue 5. How to minimize signaling when the UE moves repeatedly across the allowed area boundary.
  In the scenario where the UE moves in and out the DN allowed area, it causes significant signaling overhead if we synchronize the states between the network and the UE.
  When those happen in active mode, change of the tracking area also incurs the handover across boundary, those signaling can be performed during the handover procedure.
  When those happen in idle mode, the signaling overhead is significant and it wakes up the UE frequently. In particular, even when the UE does not have any data to send, it doesn’t have to waste the resources. In order to solve this problem, we may design lazy update of the status in idle mode. Since the UE doesn’t have to update the network status, if it does not use.
Proposal 5. It is proposed to introduce a lazy status update mode for the PDU session together while the PDU session is suspended.
  In this mode, the UE doesn’t perform the tracking area update procedure even when the UE moves in or out of the DN allowed area in idle mode. When the UE has a data to send while the PDU session is suspended where the UE is located in the DN allowed area, the UE performs the tracking area update to resume the PDU session.
  When the downlink traffic comes to the User Plane Function while the UE is located out of the DN allowed area, the network pages the UE. The UE responds the paging with sending service request. During this procedure, the network checks whether the UE is allowed to use PDU session in the location, the network may reject the UE’s service request by checking whether the PDU session is allowed where the UE is located. During this procedure, the PDU session state is changed to the suspended state.
Detailed solution is for further study

## Slide 11: Proposed Function (1/2)
1. Discovery of the available Data Network with the allowed area (DN allowed area)
  When the UE attaches or update tracking area, MM of the core network may informs the UE of the availability of the Data Network and the allowed area of the Data Network.
  The information may include an immediate setup indicator for each PDU session to be established immediately after the UE enter the DN allowed area. If there is no such indicator (i.e. default), the UE initiates the PDU session establishment procedure when it is needed.
2. Establishment of PDU session within DN allowed area
  If the current tracking area which the UE is camping on is within the allowed area of the PDU session (i.e. the PDU session is available), the UE may initiate the PDU session establishment procedure when it is needed.
  During the PDU session establishment, the UE is informed the full list of DN allowed for the PDU session. If the PDU session is established while the UE is in the allowed area.
3. Maintaining the PDU session while the UE moves within the DN allowed area
  Once the UE and the network established the PDU session, the PDU session is maintained while the UE moves within the area. During the PDU session establishment, the NG-CP (i.e. SM) sends PDU session information including the DN allowed area for the UE’s PDU session to the NG-RAN. The NG-RAN manages the PDU session context including the DN allowed area.

## Slide 12: Proposed Function (2/2)
4. Suspending the PDU session when the UE moves out of the DN allowed area
  When the UE moves out of the DN allowed area in active mode after the PDU session is established, the NG-RAN informs the NG-CP that the UE moves out of the DN allowed area in order to suspend the PDU session. In the suspended state, the User Plane Function drops the downlink traffic toward to the UE and the UE drops the uplink traffic.
  When the UE moves out of the DN allowed area in idle mode after the PDU session is established, the UE informs the SM of the current location by using tracking area update procedure via MM to suspend the PDU session.
  The figure 6.4.25.1-2 shows the diagram of PDU session status based on the UE’s location across the DN allowed area.
5. Resuming the PDU session when the UE moves in the DN allowed area
  When the UE moves in the DN allowed area while PDU session is suspended, the UE informs the SM of the current location by using tracking area update procedure via MM to resume the PDU session state.

## Slide 13: Solution Evaluation
Introduction of the Data Network Allowed Area (DN allowed area) for the PDU session
  DN allowed area is equivalent with the white list of tracking areas where the PDU session is allowed to be established. After the UE discovers information of DN allowed area for the PDU session, it may initiate the PDU session where it is allowed to establish the PDU session.
  In addition to other PDU session establishment solutions, it only added the allowed area for the PDU session.
  Compared to the mobility restriction solutions, this solution allows the transmitting and receiving the PDU data for the allowed area for the specific DN.
Network triggered PDU session establishment vs. UE requested PDU session establishment
  Network triggered PDU session establishment is not main part of this solution. However, it is required to describe the use case when the UE enters a DN allowed area. This solution does not propose “network triggered PDU session establishment”. Instead, this solution proposes a new PDU session type which requires the immediate PDU session establishment.
Suspending and resuming PDU session based on the UE location
  In order to avoid the frequent terminating and re-establishing the PDU session, it is proposed to suspend (or disable) the PDU session where the UE is located out of DN allowed area. When the PDU session is suspended, the UE and the network drop the traffic. When the UE comes back to the DN allowed area, the PDU session is resumed (or enabled). The UE updates the UE location by performing tracking area update procedure for the network to resume the PDU session. To do this, the PDU session is not terminated and re-established frequently. But it requires a new state so called “PDU session suspended state” which is changed based on the UE location.
  In order to realize the PDU session service which is only allowed in a certain area such as enterprise network and amusement park, it is necessary to signal when the UE moves in and out the area, which is inevitable for the service.