## Slide 1: Proposal on Interim agreement for multiple PDU sessions via different accesses LG Electronics
3GPP SA WG 2 Meeting#118
14 – 18 November, Reno, Nevada, USA
Agenda item: 10.6.4
Document for: Discussion and approval
S2-166548

## Slide 2
SM Work Task#5
Solutions of TR 23.799
  6.4.20: Session Management on the PDU session(s) via different accesses
  6.4.24: Session Management with individual CP function per access network
S2-166548
Background
1
Work Task ID | Work Task(s) | Work Task Description
SM_WT_#5 | PDU sessions via different accesses | UE connected via multiple accesses, including non-3GPP Identify the architecture options for the following cases; - Multiple PDU sessions via different accesses - A single PDU session via different accesses (a.k.a. multi-access PDU session) (NOTE: the way to move IP flows between AN1 and AN2 depends on Key issue#20.)
Notes: 1

## Slide 3: Based on current interim agreements (1/2)
8.6.4 Interim agreements on Session Management and Service Continuity
  The NextGen system shall support an UE establishing multiple separate PDU sessions, to the same data network or to different data networks, via 3GPP and Non-3GPP access networks at the same time. In this case each PDU session is routed over only a single access network. The choice of the access to use for a PDU session is based at least on network policy, service requirements and user subscription
    NOTE 1: Support of WLAN integrated at RAN level is under RAN responsibility, and CN related aspects will be considered as needed based on RAN decision.
    NOTE 2: The definition of policy for selecting the access to route the PDU Sessions (e.g. service requirements, user subscription, etc ) and how it is used are FFS.
 Two solutions (6.4.20 and 6.4.24) are aligned with this interim agreement.
S2-166548
2
Notes: 2

## Slide 4: Based on current interim agreements (2/2)
8.6.4 Interim agreements on Session Management and Service Continuity
  Interim agreements for MM and SM interaction
  A single NG1 NAS connection is used for both MM and SM-related messages and procedures for a UE. The single NG1 termination point is located in MM.
  Editor notes: This is applied for UE only registered via 3GPP access. The case of UE registered via non-3GPP is FFS.
  NG2 signalling related with UE is terminated in the MMF i.e. there is an unique NG2 termination for a given UE regardless of the number of PDU sessions (possibly zero) of a UE.
 We need to decide if above interim agreements are applied in case of attaching both via 3GPP access and via non-3GPP access.
S2-166548
3
Notes: 3

## Slide 5
The ways to route over multiple accesses to the same CP function
  Option 1: The information identifying the serving CP function is sent to the UE, and UE uses it when attaching via additional access. The access network directs the UE to the same CP function.
  Option 2: The information identifying the serving CP function is stored to the CP management function (e.g. HSS). The CP function may be re-allocated when attaching via additional access.
   This additional procedure is need to be defined. The procedure to keep the same CP function may be often performed due to the mobility in 3GPP access or AP change in non-3GPP access.
S2-166548
6.4.20 Common MM CP solution (1/2)
4
Figure 6.4.20.1-1: Multiple PDU sessions via different accesses
to the different data networks
Figure 6.4.20.1-2: Multiple PDU sessions via different accesses
to the same network
Notes: 4

## Slide 6: 6.4.20 Common MM CP solution (2/2)
S2-166548
5
VPLMN
HPLMN
common
MMF
3GPP access
Non-3GPP access
ngPDG
MMF
HSS
IPsec tunnel
SMF
SMF
In case of untrusted non-3GPP access, how to use ngPDG of HPLMN ?
  Assuming initial attach via 3GPP access in VPLMN, and the serving MMF in VPLMN can be common MMF for the attach via non-3GPP access later.
  When attaching via non-3GPP access, if the authentication is performed via ngPDG of HPLMN and the reallocation from MMF of HPLMN to common MMF of VPLMN is performed, the NAS signaling is routed in the inefficient manner.
Notes: 5

## Slide 7
The individual MM CP function per access network handles the signalling related to session managements via NG1 and it is similar to the existing EPS system (i.e. MME for 3GPP access and P-GW for non-3GPP access).
   No specific issues comparing to common CP solution.
S2-166548
6.4.24 Individual MM CP solution
6
Figure 6.4.24.1-1: Multiple PDU sessions via different accesses
to the different data networks
Figure 6.4.24.1-2: Multiple PDU sessions via different accesses
to the same network
Notes: 6

## Slide 8
S2-166548
Proposal
We propose to select the individual MM CP function per access network.
We propose to update the interim agreements as follows;
8.6.4 Interim agreements on Session Management and Service Continuity
  Interim agreements for MM and SM interaction
  A single NG1 NAS connection is used for both MM and SM-related messages and procedures per access network for a UE. The single NG1 termination point is located in MM per access network.
  Editor notes: This is applied for UE only registered via 3GPP access. The case of UE registered via non-3GPP is FFS.
  …..
  NG2 signalling related with UE is terminated in the MMF per access network i.e. there is an unique NG2 termination per access network for a given UE regardless of the number of PDU sessions (possibly zero) of a UE.
7
Notes: 7