## Slide 1: Feedback on S2-166721
Nokia
S2-166782

## Slide 2: Note: Contents of S2-166721 and S2-166782 are differentiated with an appropriate header for S2-166782 in the right top corner.

## Slide 3: Data layer solution contradicts industry’s best practices for service-based architectures
SA2 has agreed to evaluate service-based architecture (*) for NGCN
  network functions “provide a service based interface to other NFs.”; [TR 23.799, section 8.7 “Interim agreements on Key Issue 7]
Industry’s best practices for (micro) service architectures (see backup for more material and references)
  “Monolithic applications prefer a single logical database for persistent data”; “micro-services prefer letting each service manage its own database”
  “Create a separate data store for each micro-service”
  “Keep each micro-service’s persistent data private to that service and accessible only via its API.”
Data Layer solution proposes the opposite (quotes from TR 23.799, solution 7.5)
  “UE context and session context is stored across network functions”
  “Context shar[ing] across network functions”
  “Data sharing between same type of Core Network Functions […] and different type of Core network functions”
(*) expected to be a complement (not a replacement) for point-to-point interfaces for basic network procedures.
S2-166721

## Slide 4: Response to the arguments in slide #3
The well-known argument applies to micro-services that do not need to access the same data, i.e. where each service has a truly isolated context they operate on. In some/many cases such services are stateless by nature and only few of the services even have any real state data. Often in these cases the amount of state data is very small compared to telco domain. Solutions where there is a lot of state data are not following the model they promote.
Slide #3 is very vague in terms of assumed service granularity. What is the service granularity considered here? Can S2-166721 source companies clarify how exactly the outlined principles are adopted for NGC without sharing the same UE context for supporting service based architecture?
In telco domain, NGC in particular, that approach would lead to mega-services instead of micro-services as the number of services that can be implemented with the isolated data principle is very small / close to zero. In NGC micro-services require access to the same context data (e.g. authentication run is dependent on MM events thus MM related contexts) of a particular UE. Encapsulating the data inside each service could lead to mega services. Adding new micro-services in an agile way is possible only if this data is available to them.
Thus in order to reach the agility targets promised by service based architecture, supported services need to be able to share context.
DL solution states deployments should have the option to use a single logical DL to store contexts shared by 2 AMFs, AMF-SMF-PCF etc. Rather 3GPP solution should not preclude any of these deployment options.
S2-166782

## Slide 5: Problems claimed to be solved by the Data Layer solution (*)
Support common interface to a common database (avoid need for different databases for state from different NFs)
Increase NF resiliency by separating state from network functions and enabling any network function instance to finish a transaction if a first network function instance crashes
Reduce network function resource usage for long-term Idle UEs
Sharing context information via a data layer instead of via direct messaging (e.g. from MM to SM)
Support exposure of information to other MNO network functions or 3rd party functions (e.g. ULI)
Support of analytics/big data on top of UE context information in the data layer
(*) Summary based on Data Layer solution as per TR 23.799, section 6.7.5
S2-166721

## Slide 6: Support common interface to a common database (avoid need for different databases for state from different NFs)
Background
NF implementations on virtualized platforms may decide to separate context (state) information into a separate state DB
Operators may want to avoid having to deploy different databases for different network functions
Key idea: define a common interface to a common state database for all network functions
Analysis
Typically databases are often bundled with network functions (in which case there may not be an issue)
However, it may be worth analyzing if this is a valid issue from deployment perspective (e.g. to ensure low CAPEX/OPEN for network functions from different vendors)
Analysis cont’d
If so, it could be solved by defining optional interfaces from network functions to storage services (databases)
Whether one type of storage service is sufficient or not (“polyglot persistence” principle) and whether those should be defined by 3GPP or re-used from other fora is FFS
  Virtualization platforms like OpenStack already provide such service (e.g. OpenStack Swift -- a highly available, distributed, eventually consistent object/blob store)
No need for a common data model for solving this issue
  Data is not shared by different network functions.
Conclusion
Underlying issue needs to be better understood
Issue could be solved by defining interface(s) from network functions to storage services/databases for opaque data
  Type of storage services required and where to specify those is FFS.
S2-166721

## Slide 7: Response to the arguments in slide #6
Open stack does not define the database access interface
Trove provides database as a service on Openstack where different DBs can be plugged in: Cassandra, CouchBase, CouchDB, DataStax Enterprise, DB2, MariaDB, MongoDB, MySQL, Oracle, Percona Server, PostgreSQL, Redis, Vertica and probably more to come.
However, publishing APIs means every vendor’s NF needs to be customized to support every other vendor’s DL, i.e. requires a specific integration project. And does not allow data sharing between different vendor’s NFs.
Slide 6 states – “Data is not shared by different network functions” – This statement is not true based on current outcome of NextGen TR (e.g. MM parameters might be needed for authentication decision; SM state might be needed for MM state transition etc)
S2-166782

## Slide 8: Increase NF resiliency by separating state from network functions and enabling any network function instance to finish a transaction in case of NF failure (1/2)
Key idea
Network functions store their state into a state database after completing a transaction and become stateless
NFs are stateless; at a new transaction, a serving NF gets selected, pulls state from the DB, executes the transaction and writes the state back to the repository
If a serving function crashes, a different serving function can continue
Analysis
As per the Data layer solution description, a network function decides on its own when to sync the state back to the state DB and it may even cash state for some time
However, a network function may crash at an arbitrary point in time, i.e. quite a lot of state will get lost before the function can synchronized it with the state DB
Analysis cont’d
Given this, it is not obvious how fail-over across network function can work unless the synchronization algorithm was fully standardized
But: Using a state DB across different network functions violates a key principle of service architectures
Therefore, separating state into a state DB as a basis for failover and recovery is a potential solution that can work within(!) a specific network function implementation
  Can be done today, i.e. does not require standards work
S2-166721

## Slide 9: Increase NF resiliency by separating state from network functions and enabling any network function instance to finish a transaction in case of NF failure (2/2)
Analysis cont’d
Also, even in multi-vendor deployments, no obvious need for fail-over across between functions from different vendors
  By definition fail-over across vendors will always be worse compared to intra-vendor since the target function does not understand the source function’s proprietary state
  Typically multiple instances of a function from one vendor would be active (even in a multi-vendor deployment), so fail-over can be supported easily across those
  Hence, not clear why an operator would require inter-vendor fail-over support
Conclusion
Not obvious that the data layer solution solves all fail-over and recovery scenarios (e.g. how to handle NF failure while an NF holds state)
Fail-over between network functions from different vendors will not work as well as intra-vendor and it is not obvious why an operator would need support for inter-vendor fail-over
Fail-over based on a separate state DB is an intra-vendor implementation option
Similarly as for the previous issue, it may be worth looking into defining common interface(s) from network functions to storage services/databases for opaque data to foster this
S2-166721

## Slide 10: Response to the arguments in Slide, #8, #9
If a network function fails during a certain procedure, some data created in the middle of a transaction may be lost.
This is true with or without the Data Layer. But the Data Layer allows the service/UE context to be restored from the last stable state.
This is similar to the existing EPC restoration procedure, which also relies on storing state information in a centralized repository, and for which a failure may also happen in the middle of a transaction.
The Data Layer provides a framework that inherently supports the restoration feature.
S2-166782

## Slide 11: Reduce network function resource usage for Idle UEs
Key idea
NW functions store context information of UEs that are in long term Idle state (large number of IoT devices/sensors) into a state database to reduce memory demand for the actual network functions
Analysis
Outsourcing state information from serving network functions (e.g. from memory into a different storage service (e.g. even disk based)) for UEs that remain in very long Idle state may or may not be useful
  Memory demand for IoT device session state (the typical long time Idle mode case) is typically low (i.e. small benefit)
  Memory demand is higher for smart phone sessions (up to 100s of KBs), however those are typically not Idle for long
Analysis cont’d
Implementations can do this today (e.g. for EPC), i.e. a standardized state DB is not a prerequisite for reducing network function resources
A common storage service across different implementations could simplify deployments
Conclusion
Benefits of outsourcing state may need to be better understood
Standardized state DB is not a prerequisite for outsourcing state for long time Idle UEs
Similarly as for the previous issue, it may be worth looking into defining common interface(s) from network functions to storage services/databases for opaque data to foster this
S2-166721

## Slide 12: Sharing context information via a data layer instead of via direct messaging (e.g. from MM to SM)
Key idea
Different network functions (e.g. MM and SM) access a common view of the session state for a given subscriber
As a result, subscriber state needed by e.g. the SM function does not have to be passed as direct messaging from MM to SM
Analysis
If network functions exchange direct messages anyway (as Data layer solution assumes) no signaling is saved (instead, additional signaling for sync with the data layer and from there to the target function is needed)
Passing information directly via a database instead of an API violates key industry principles for service architectures
Analysis
Open technical issues: How can synchronization between direct messages and state transfer via data layer be ensured:
  How can it be ensured that the data exchanged via data layer reaches the target function before the direct message?
How can it be avoided that multiple network functions overwrite the same data field in the shared session state database?
Conclusion
Too early to agree this as the way forward for the 5G architecture (synchronization issues and access control to shared session state has not been described yet)
Generally not promising due to
  Lack of benefits if also direct messaging is used
  Violation of industry principles for service architectures
S2-166721

## Slide 13: Response to arguments in slide #12 (1/4)
Question from slide #12 - How can synchronization between direct messages and state transfer via data layer be ensured:
  How can it be ensured that the data exchanged via data layer reaches the target function before the direct message?
  Answer - Depending on the type of procedure, Network Function 1 can store the data and request for acknowledgement prior to sending a message to NF2. This ensures that NF2 has the data available from DL for processing the message from NF1.
Question from slide #12 - How can it be avoided that multiple network functions overwrite the same data field in the shared session state database?
Answer: The DB maintains one owner for the session data. Only one NF has write permission for certain UE context.
If 3GPP defines a clear trigger for NF to store UE contexts in the SDL and the new NF reads the UE contexts from the SDL, this approach is as reliable as message centric context transfer.
S2-166782

## Slide 14: Response to arguments in slide #12 (2/4)
Two trigger options:
  NF updates the contexts at the end of the procedure as shown in the call flows in solution 7.5 (or)
  NF updates the contexts at the time of NG2 release and during HO.
S2-166782

## Slide 15: Response to arguments in slide #12 (3/4)
With Trigger option 1:
This guarantees data in cache and in DL are in synch upon completion of the procedure.
AMF updates the DL with UE contexts at the end of an atomic procedure (e.g. attach, SR, NG2 connection release, TAU etc).
This will ensure that for subsequent transactions –
  When HO happens, new AMF will have updated state in the DL
  When UE performs, new AMF will have updated state in the DL
  If there is a failure, new AMF will have updated state in the DL
If the NF fails in the middle of a procedure, then the DL will have last known stable state. This is still better than “no state”. The new NF should have enough information to restore connection. Upon restoration, new NF can update the DL.
S2-166782

## Slide 16: Response to arguments in slide #12 (4/4)
With Trigger option 2:
This guarantees data in cache and in DL are in synch when NG2 is released.
If UE is in connected state and a HO is triggered by the RAN, the AMF updates the DL before proceeding with the HO if DL needs to be updated
If UE is in idle state and triggers a TAU, DL should have the latest data.
If UE is in idle state and NF fails, then DL has latest Context Data.
If UE is in connected state and NF fails, then new assigned NF will retrieve context from DL. If we assume DL has not been updated before the NF failure, the new NF will use stored data to restore connection (there should be enough data to restore connection) and new NF can then update DL. Worst case UE will have to re-attach which would normally be the case if there is no multi-vendor network resiliency.
S2-166782

## Slide 17: Exposure of information to other MNO network functions or 3rd party functions
Key idea
Network functions expose a subset of their context information (e.g. ULI)
Other network functions or 3rd party functions subscribe to changes of e.g. ULI
Avoids the need to pass this information via potentially multiple nodes on the path as today
Analysis
Exposure of information such as ULI to 3rd party functions (and other network functions) is useful
But: issue has already been solved by the agreement to follow a service-based approach (capability exposure) in R15
  ULI reporting can be defined as a service offered for multiple consumers (3rd parties and other NFs)
  Multiple functions can subscribe to receiving ULI updates
  No need for an additional data layer for storing ULI
  As an optimization (to reduce load on NFs), an intermediate Network Exposure Function (NEF) may be considered
Conclusion
Issue has already been solved by the agreed principle of exposing capabilities (e.g. ULI reporting) as a service
No need for an additional data layer (but data layer could be an implementation option on top of capability exposure; see next slide)
…
ULI
S2-166721

## Slide 18: Support of analytics/big data on top of UE context information in the data layer
Key Idea
If UE context information is exposed to a data layer, then this enables analytics solution on top of this data
Analysis
Exposing standardized state information (e.g. information sent via 3GPP interfaces today) is not helpful for analytics beyond some simple cases like ULI
Other information (bulk statistics, counters) are typically much more useful for analytics (but are not part of the standardized UE state)
Conclusion
Just exposing 3GPP state information not useful for analytics
Conclusion cont’d
A more thorough study should be done to determine information (statistics/counters) to be standardized and exposed in addition for analytics
No need for an additional solution: Information can already be exposed to e.g. an analytics solution using the service-based architecture notion (capabilities exposed as a service)
  Analytics solution can simply subscribe to exposed capabilities
  Nothing prevents implementations (e.g. analytics function using capabilities from other NFs or the NEF) to store data
Capability A
Capability B
S2-166721

## Slide 19: Response to API based exposure slides #17, #18
Drawback of #17, #18:
The data exposure capability is not centered around just one parameter ULI which is only one of parameters to be considered.
API exposure intra PLMN for data sharing is a bit too heavy. All NFs (consumers/producers) have to implement additional APIs. Application level knowledge (functional requirement) is required while filtering is much easier in a DB schema.
Requires subscription to multiple network functions (= m NFs) depending on the contexts needed. Consumers needs to determine the right producers for the context information. Assumes network capability is tied 1-1 with data object exposed.
Analytics – will need all the data. No characterization on the type of data possible ahead of time. Thus constant replication of data will be necessary. Analytics might need to subscribe towards multiple source, keep track of the latest serving node information and be notified whenever there is a relocation unlike Analytics depending on one source.
Data exposure via API will require similar or even more standardization. Every data object needs to map to NF capability. Then every NF capability mapped to Service ID will require standardization. Then inter-PLMN scenarios will require service ID to be maintained in a central repository, registry etc.
With just a pure DB based approach, only the standardized context needs to be specified (i.e. data model standards for UE context).
In short, using API model is not simplifying anything over standardizing UE contexts. Only makes it worse.
Selection of correct NF instance upon UE relocation needs to be resolved - Every Client would have to know that the correct NF instance information is maintained even as part of relocation.
S2-166782

## Slide 20: Conclusion
State information to remain part of the network function itself (as per industry’s best practices for service architectures)
NF implementations can decide to internally separate state (into their own data store)
3GPP may support this by defining or recommending optional interfaces from network functions to storage services (databases) for opaque data
A single type of storage service may be insufficient (different storage technologies may be needed -- “polyglot persistence” principle as per industry’s best practices for service architectures)
Types of storage services needed and who should define those (3GPP or re-used from other fora) needs to be studied
Exposure of information (and analytics) are already supported by the agreed principle of exposing capabilities as a service (e.g. ULI reporting) to multiple consumers.
  No need for an additional data layer for storing e.g. ULI (but: nothing prevents e.g. an NEF implementation from storing data, i.e. Data layer is a potential implementation option on top of capability exposure).
S2-166721

## Slide 21: Proposed way forward (conclusion for KI#7)
3GPP should recommend or specify an optional interface from network functions to a storage service that network functions may use to store selected state as opaque data.
NOTE: Recommendation may for instance be by reference to an existing industry standard from an SDO other than 3GPP. The details of this, including whether a single storage service (interface) is sufficient or if multiple storage service types need to be supported is up to Stage 3.

## Slide 22: Proposed update to questions for show of hands
Question #7/2a: Should Rel-15 support a standardized, capability, that may be used by any Network Function to export some or all of its opaque data to a state repository? Should 3GPP recommend or specify optional interfaces from network functions to storage services (information repositories) that network functions may use to store selected state as opaque (=vendor specific) data?
  NOTE: Recommendation may for instance be by reference to an existing industry standard from an SDO other than 3GPP. The details of this, including whether a single storage service (interface) is sufficient or if multiple storage service types need to be supported is up to Stage 3.
Question #7/2a-bis: Should selected information like ULI be exposed in a standardized manner to other network functions as a capability (ULI reporting), in line with the existing interim agreement (KI#7) (“the capability (s) of NFs are exposed as a service to other NF”)?
  NOTE: Information to be exposed to be decided on a case by case basis.
  NOTE: As an optimization (to reduce load on NFs if needed), an intermediate Network Exposure Function (NEF) may be considered.
  NOTE: Nothing prevents implementations to also cache/store data (e.g. by an analytics solution subscribing to exposed capabilities).

## Slide 23: Backup

## Slide 24: Industry’s best practices for designing service architectures

## Slide 25: Best practices in micro-service architectures: “In the micro-services approach, each service manages and stores its own state.“
Source: https://azure.microsoft.com/en-us/documentation/articles/service-fabric-overview-microservices/

## Slide 26: Best practices in micro-service architectures: “Micro-services prefer letting each service manage its own database.”
“Monolithic applications prefer a single logical database for persistent data, […] many of these decisions driven through vendor's commercial models around licensing.
“Microservices prefer letting each service manage its own database…”
“…either different instances of the same database technology, or entirely different database systems - an approach called Polyglot Persistence. “
Source: http://www.martinfowler.com/articles/microservices.html

## Slide 27: Best practices in micro-service architectures: “Keep each microservice’s persistent data private to that service and accessible only via its API”
Problem
What’s the database architecture in a micro-services application?
Forces
Services must be loosely coupled so that they can be developed, deployed and scaled independently
Different services have different data storage requirements.
Forces cont’d
For some services, a relational database is the best choice. Other services might need a NoSQL database such as MongoDB, which is good at storing complex, unstructured data, or Neo4J, which is designed to efficiently store and query graph data.
Solution
Keep each micro-service’s persistent data private to that service and accessible only via its API.
Source: Chris Richardson: Pattern: Database per service. http://microservices.io/patterns/data/database-per-service.html

## Slide 28: Best practices in micro-service architectures: “Create a Separate Data Store for Each Microservice”
“Create a Separate Data Store for Each Microservice
Do not use the same backend data store across microservices.
You want the team for each microservice to choose the database that best suits the service.
Moreover, with a single data store it’s too easy for microservices written by different teams to share database structures, perhaps in the name of reducing duplication of work. You end up with the situation where if one team updates a database structure, other services that also use that structure have to be changed too.”
Tony Mauro: Adopting Microservices at Netflix: Lessons for Architectural Design.
https://www.nginx.com/blog/microservices-at-netflix-architectural-best-practices/

## Slide 29: Summary: Key attributes of micro service architectures
“A micro-service is a minimal independent process interacting via messages. […]
Micro-services are independent components conceptually deployed in isolation and equipped with dedicated memory persistence tools (e.g. databases)”.
  Dragoni et. al: micro-services: yesterday, today, and tomorrow, 2016. https://arxiv.org/pdf/1606.04036v1.pdf]
“Micro-services are small, autonomous services that work together”:
  “All communication between the services themselves are via network calls, to enforce separation between the services and avoid the perils of tight coupling.”
  Strong cohesion and loose coupling—with database integration, we lose both things.
  “Avoid database integration at all costs.”
  Sam Newman: Building Microservices. Designing Fine-Grained Systems. O'Reilly Media, 2015.