## Slide 1
Discussion guide for slicing
Based on S2-166055 picture (courtesy Qualcomm)
EDITOR (NOKIA)
3GPP TSG SA WG2#118, November 14-18, Reno, Nevada. S2-16xxxx

## Slide 2: What is NSSAI?
A slice is identified by two pieces of info: Slice/Service type (SST) and complementary info that we can call Tenant ID, or client ID, or SLA ID
  We refer to this as Individual Network Slice Selection Information, or I-NSSAI
A NSSAI (Network Slice Selection Information) is a collection of >1 I-NSSAIs

## Slide 3: Which procedures use what
MM procedures should include NSSAI (they affect all slices)
SM procedures should include the I-NSSAI of the affected slice.

## Slide 4: What does HSS store
The HSS stores the I-NSSAIs of the slices the UE subscribes to

## Slide 5: HOW is CCNF selected by RAN
By Temp ID (if available)
By NSSAI based routing in RAN

## Slide 6: HOW is SMF selected by CCNF
By I-NSSAI . If more than 1 SMF is allowed in a slice the DNN or other info also is used.

## Slide 7
UE
HSS
DNS
NSSAI=SST(s)+tenant-id(s)
RAN
SMF
NSSAI
NSSAI
SMF
Select CN node based on SST and tenant
NAS
NSSAI
DNS
DNS req (DNN+ I-NSSAI)
DNS req (DNN+I-NSSAI)
Select GW
NW slicing in 8.1
CCNF
Multiple slices per UE
Possible support for RAN slicing
Based on RRC NSSAI inspection
I-NSSAI + DNN
Selected by Temp ID or NSSAI in NAS
Selected by I-NSSAI + DNN
In SM message

## Slide 8: Some terminology
In section 8.1. these terms are used:
  Configured NSSAI: a NSSAI configured by default on a UE to be used in a PLMN before any interaction with the PLMN ever took place
  Accepted NSSAI: the NSSAI used by the UE AFTER the PLMN has accepted an attach request including THIS NSSAI.