## Slide 1: Service Based Architecture for the Control Plane of 5G Core
AT&T
S2-170810
Agenda Item: 6.5.1

## Slide 2: The Traditional Way Specifying Interactions between Logical Functions via Stage 2 Call Flows
Traditionally, interactions between 3GPP defined logical elements of a telecom network are specified as a call flow showing a sequence of interactions amongst two or more network elements
These call flows only provide a very specific set of interactions with individual interaction between two functions only meaningful within the context of a larger and particular procedure / call flow
  Makes the system inflexible to future uses
  Increases time to market as new features need additional standardization to specify changes to the external behavior of network functions and standardization

## Slide 3: 5G Mobile Core Control Plane Architecture
Based on 3GPP SA2 TR 23.799 agreements the Control Plane of a 5G core will be modular, comprising of several Network Functions (e.g. AMF, SMF, PCF, UDM etc.) that interact with each other as well as with other entities outside of the Control Plane
This modularized approach towards defining a Control Plane architecture is aligned with industry drive towards “softwarization” of telecom networks
It is important during the specification phase of the network functions that the interactions of Network Functions within the Control Plane are specified in a manner that would help adopt this concept of multi vendor software modules that are easy to interact with and maintain in a virtualized environment.
  This has been a key driver towards the requirement for consideration of service based architecture within the control plane for many operators

## Slide 4: Network Function as a Software Module
A Network Function, like traditional 3GPP logical function, can be considered to be self contained and interchangeable in the sense that
  its functionality is described in specifications via how it interacts with other Network Functions
  its internal working is implementation specific and not part of the standards specifications
In a “softwarized” or virtualized telecom network, a 3GPP Control Plane Network Function in its implementation can be considered a software module that is
  self contained in its functionality and interacting with other software modules through interfaces that should follow software industry trends e.g. use of APIs
  seamlessly interchangeable with similar software modules from other vendors in a virtual environment

## Slide 5: Network Function Interactions Areas Requiring Common Understanding
For a “softwarized”/virtualized environment what is the best way to represent interactions between network functions implemented as software modules?
  In some instances interactions between network elements is confined to only two elements
  In many other instances interaction between two network elements results in triggering interaction with other network elements
    In some instances a response from one or more additional network functions maybe needed before responding – is that because we have been thinking about these transactions in a point to point manner and perhaps these interactions can be asynchronous and not nested?
--------------------------------------------------
In our view event driven model that uses external triggers (e.g. incoming request on an interface) / internal timers (e.g. periodic timer) etc. should be considered as a basis for interactions between modules.
  The initial proposals for service based architecture already point to such an approach and we propose to use this as the basis for developing. Two service types should be considered: Request/Response and Subscribe/Notify
  High level software concepts similar to “semaphore” can be used to provide control over common resources across network functions / software modules

## Slide 6: Network Function Interactions Areas Requiring Common Understanding
What is the criteria for having a service based architecture type interactions between control plane entities?
  Is there a need to show the transactions under discussion are reusable as part of justification for service based architecture?
Do we need to consider two types of interactions between control plane network functions / software modules i.e. service based and traditional point to point. OR can we have ONLY service based architecture for all interactions amongst control plane modules?
  Would having to support two types of interactions (Service based and point to point) for control plane functions complicate the architecture?
----------------------------------------------------
In our view, in addition to reusability, simplification of the system is an additional criteria while considering support for two interface types on control plane entity. Therefore effort should be made to avoid network functions having to support two types of interfaces for communication within CP (service based and point to point based).
  Exceptions can however be made where it is justified and unavoidable

## Slide 7: Network Function Interactions Areas Requiring Common Understanding
How should we document interactions between network functions (to be implemented as software modules) at stage 2 level?
Two tables per NF (one for Request/Response and one for Subscribe/Notify) with various interactions/services tabulated and perhaps their invocation indicated through a parameter. Additional information such as which network function has control over shared resources during transaction can also be added
  For example first parameter of the table indicates the service and the remaining parameters are interpreted based on the first parameter
One per Service with several interactions/services separately documented per NF
---------------------------------------------------
In our view either of the two approaches can work. However use of first approach can result in a more compact and easier to maintain document. Current tables may have to be moved from TS 23.501 to TS 23.502
While the details on how stage 2 information like a table gets translated into for example an API is a stage 3 issue, stage 2 information should be provided in a manner that would facilitate such stage 3 work

## Slide 8: Conclusion
It is proposed that SA2 discuss the questions on slide #5, #6 and #7 and endorse the agreements so that normative work can progress smoothly in an efficient manner