## Slide 1: Discussion on Service Based PCF
Oracle
3GPP SA WG 2 Meeting#120
27 – 31 March, Busan, Korea
S2-172033

## Slide 2: Introduction
This discussion paper evaluates various service based PCF architectures as follows:
  Services are first determined by grouping cohesive functionality
  Grouping can be done at various granularity levels resulting in multiple alternatives
  Architecture alternatives are expanded and validated based on call flows
  Alternatives are compared based on various criteria

## Slide 3: Approaches
Approach #1: PCF exposing a service per interface, as follows:
  AM service, SM service, AF service, RCAF service, etc.
Approach #2: PCF exposing high level functional services
  Policy Decision Service (e.g. used by SM, AM to get policy decisions from the PCF)
  Decision Publish Service (e.g. policy rules published by PCF)
Approach #3: PCF exposing low level functional services, as follows:
  QoS, Charging, Application Detection, Usage Management, Mobility, Traffic Steering, etc.

## Slide 4: Approaches’ evaluation criteria
Efficiency
Extensibility
  Easily extending existing functionality (e.g. adding new QoS functionality)
  Introducing new services (e.g. traffic steering) with minimal impact to existing services
  Backward/forward compatibility
Simplicity

## Slide 5: Evaluated Call flows
PDU session establishment
PDU client initiated session update
PDU server initiated session update
Stateful application service authorization (e.g. equivalent to Rx AAR)
Application notification (e.g. equivalent to Rx RAR)

## Slide 6: Approach #1 Interface based services

## Slide 7: Approach#1 - Architecture
PCF
AF
SMF
AMF
AF Policy Service
SM Policy Listener
AM Policy Listener
SM Policy Publisher
SM Policy
Client
AF Policy
Client
AF Notification
Consumer
SM Enforcement Service
SM Policy Service
AM Policy Service
AF Notification Publisher
AM Enforcement Service
AM Policy
Client
AM Policy
Publisher
PCF provides interface specific services (policy pull)
PCF publishes interface specific policies (policy push)
PCF publishes interface specific notifications (e.g. similar to Rx RAR)
Clients requests policies from PCF based on interface specific service
Clients (AM/SM) listen to interface specific policy pushes
Clients subscribe and get notified based on interface specific events

## Slide 8: PDU session establishment (approach 1)
SMF
PCF
SM Service
SM Policy
Client
PDU session establishment request
GetSMPolicies (User Id, RAN/PDU context)
SMPoliciesResponse
(context id, list of decisions, event triggers)
PDU answer
SM Policy Context
SaveSMPolicyContext ()
SM Policy Context
Save SM Policy context
(context id, decision info)
Eval policies
SM Policy Listener
SM Policy Publisher

## Slide 9: PDU client initiated update (approach 1)
SMF
PCF
SM Service
SM Policy
Client
SM Policy Context
SM Policy Context
SM Policy Listener
SM Policy Publisher
PDU session update
GetUpdatedSMPolicies()
(context id, RAN/PDU data, event triggers)
PDU answer
GetSMPolicyContext
(context id)
GetSMPolicyContext ()
Eval policies
SaveSMPolicyContext ()
SMPoliciesResponse
(context id, list of decisions, event triggers)
SaveSMPolicyContext
(context id, decision info)

## Slide 10: PDU server initiated update (approach 1)
SMF
PCF
SM
Service
SM Policy
Client
SMPolicyProvisionRequest
(context id, list of decisions, event triggers)
SM Policy Contexts
SM Policy Contexts
SM Policy Listener
SM Policy Publisher
Session update
SaveSMPolicyContext
(context id, decision info)
SMPolicyProvisionResp(success)
SaveSMPolicyContext()
Update PDU

## Slide 11: Stateful application service authorization (approach 1)
AF
PCF
AF Policy
Service
AF Policy
Client
AF service procedure
AFPolicyRequest
(User Id, IP addresses, AF service info, Subscribed events)
AFPolicyResp(AF policy context id, PDU/RAN info)
AF Policy Contexts
SaveAFPolicyContext()
AF Policy Contexts
SaveAFPolicyContext (context id, PDU/RAN info)
Eval policies
Bind and publish SM policy updates
Continue AF service procedure

## Slide 12: Application notification (approach 1)
AF
PCF
AF Service
AF Policy Client
AFApplicationNotification
(context id, event info (e.g. deactivated SDF)
AF Policy Contexts
AF Policy Contexts
AF Notification
Consumer
AF Notification Publisher
Application notification (ex: SDF Deactivation)
SaveAFPolicyContext(Context id, updated PDU/RAN info)
AFAppNotificationResp()
SaveAFPolicyContext(context id)

## Slide 13: Summary approach #1 vs criteria
Efficiency: Good on runtime, Fair on design time
  Runtime:
    Efficient APIs as policy decisions can be retrieved/pushed in one API call
    Subscriptions to events can be combined with policy decision request
  Design time:
    Cannot re-use common aspects across interfaces
Extensibility: Fair
  Changes required for a new interface will be mostly confined to one service
Simplicity: Fair

## Slide 14: Approach #2 High level functional services

## Slide 15: Approach #2 - Architecture
PCF
AF
SMF
Decision Service
Decision Listener
Decision Publisher
Decision
Client
Decision
Client
Notification
Consumer
Enforcement Service
Notification Publisher
AMF
Decision Listener
Decision
Client
Enforcement Service
PCF provides generic decision service
PCF publishes/pushes decisions to generic decision listeners
PCF publishes notifications based on clients’ subscriptions to events
Decision clients request specific decision info from generic PCF service (e.g. AMF requests mobility policies whereas SMF requests QoS, Charging, etc)
Decision listeners receive decisions pushed by PCFC

## Slide 16: PDU session establishment (approach 2)
SMF
PCF
Decision Service
Decision
Client
PDU session request
GetDecision(User Id, RAN/PDU context,
Requested Decisions: QoS, Charging, AppDetection, …)
DecisionResp(acknowledge,
decision context id, list of decisions, event triggers)
PDU answer
Decision Contexts
SaveDecision()
Client Decision Contexts
SaveDecision(context id, decision info)
Eval policies

## Slide 17: Stateful application service authorization (approach 2)
Continue AF service procedure
AF
PCF
Decision Service
Decision
Client
AF session request
GetDecision(User Id, IP addresses, Service info, Requested Decisions: Service QoS, Sponsored Data, Subscriptions…)
DecisionResp(acknowledge,
decision context id, AF decision, information of events)
Decision Contexts
SaveDecision()
Client Decision Contexts
SaveDecision(context id, decision info)
Eval policies
Bind and publish SM policy updates
Decision Publisher

## Slide 18: Application notification (approach 2)
AF
PCF
Decision Service
… Service
Client
DecisionUpdate[AF](
decision context id, information of the events[Ex: deactivated SDF])
Decision Contexts
Client Decision Contexts
Notification
Consumer
Decision Publisher
Application notification (ex: SDF Deactivation)
SaveDecision(context id, decision info)
DecisionUpdateResp(acknowledge)
SaveDecision()

## Slide 19: Summary approach #2 vs criteria
Efficiency: Good on runtime, Good on design time
  Runtime:
    Efficient APIs as policy decisions can be retrieved/pushed in one API call
    Subscriptions to events can be combined with policy decision request
  Design time:
    Can re-use common aspects across interfaces into the generic services
Extensibility: Good
  Policy decisions can be grouped into sub-category (e.g. QoS, Charging, etc) and clients can request specific decision categories
  No need to introduce new services every time a new interface is added. Instead, we can leverage existing generic services
Simplicity: Fair

## Slide 20: Approach #3 Low level functional services

## Slide 21: Approach #3 - Architecture
PCF
AF
SMF
AMF
QoS Service
QoS
Listener
Mobility Listener
TS
Publisher
QoS Service
Client
AF Notification
Consumer
Traffic Steering
Charging Service
…
QoS
Publisher
Charging
Publisher
…
…
SM Enforcement Service
QoS Service
Client
…
Mobility
Policy Client
AM Enforcement Service
PCF provides a service per functional construct (QoS, Charging, Usage Monitoring, etc)
PCF publishes/pushes decisions per specific service
PCF publishes notifications based on clients’ subscriptions to specific service
Clients of the PCF have to request each service by interacting with each PCF service endpoint separately

## Slide 22: PDU session establishment (approach 3)
SMF
PCF
PDU session request
GetQoSDecision
(User Id, RAN/PDU context)
QoSDecisionResp(context id, list of QoS decisions, event triggers)
PDU answer
Decision Context
SaveQoSDecision()
Client Decision Context
SaveQoSDecision (context id, decision info)
Eval policies
GetChargingDecision(…)
QoS Service
Client
QoS Service
…
GetTrafficSteeringDecision(…)
Eval policies
SaveChargingDecision()

## Slide 23: PDU client initiated update (approach 3)
SMF
PCF
PDU session update
GetUpdatedQoSDecision(context id, event triggers/data)
QoSDecisionResp (decision context id, list of decisions)
PDU answer
Decision
Context
GetQoSDecision
(context id)
Client Decision Context
SaveQoSDecision
(context id, decision info)
GetQoSDecision()
Eval policies
SaveQoSDecision ()
QoS Service
Client
QoS
Service
GetUpdatedChargingDecision(…)
…
GetUpdatedTrafficSteeringDecision(…)

## Slide 24: PDU server initiated update (approach 3)
SMF
PCF
… Service
… Service
Client
QoSDecisionUpdate (
decision context id, list of decisions, event triggers)
Decision Contexts
Client Decision Contexts
Decision update
SaveQoSDecision(context id, decision info)
QoSDecisionUpdateResp(acknowledge,
event triggers/data)
SaveQoSDecision()
QoS Listener
ChargingDecisionUpdate(…)
…
TrafficSteeringDecisionUpdate(…)
QoS Publisher

## Slide 25: Stateful application service authorization (approach 3)
AF
PCF
GetQoSDecision(User Id, IP addresses, AF context, Requested Decisions: QoS, Subscription)
DecisionQoSResp(acknowledge,
decision context id, AF QoS decision, information of events)
Decision Contexts
SaveQoSDecision()
Client Decision Contexts
SaveQoSDecision(context id, decision info)
Eval policies
QoS Service
Client
QoS Service
GetSponsorDataDecision(…)
…
Continue AF service procedure
AF session request

## Slide 26: Application notification (approach 3)
AF
PCF
QoS Service
… Service
Client
QoSDecisionUpdate(
decision context id, information of the events[Ex: deactivated SDF])
Decision Contexts
Client Decision Contexts
AF Notification
Consumer
Application notification (ex: SDF Deactivation)
SaveQoSDecision(context id, decision info)
QoSDecisionUpdateResp(acknowledge)
SaveQoSDecision()
OoS Publisher
SponsorDataDecisionUpdate(…)
…

## Slide 27: Summary approach #3 vs criteria
Efficiency: Poor on runtime, Fair on design time
  Runtime:
  Too many API calls to get one procedure to complete
  Design time:
  Separation of concerns is a positive. At the same time, the granularity of services is too fine
Extensibility: Good
  Changes to a functional area can be confined to a specific service
Simplicity: Poor

## Slide 28: Conclusion
Approach #2 is the recommended approach
  It enables re-use of common functionality across various policy decision clients and reduces duplication
  It allows separation of concerns across functional areas by utilizing decision categories/sub-categories
  It’s runtime and design time efficient
 | Approach 1 | Approach 2 | Approach 3
Efficiency (runtime) | Good | Good | Poor
Efficiency (design) | Fair | Good | Fair
Extensibility | Fair | Good | Good
Simplicity | Fair | Fair | Poor