## Slide 1: 5GS_Ph1: AMF-N2 Stickiness Drafting session Solutions Comparison
Devaki Chandramouli

## Slide 2: Transport Network Links
More than one TNL associations between an AMF/xNB pair should be allowed.

## Slide 3: Objective
Identifies the list of items, commonalities and differences between S2-173151 and S2-173528 (papers opened)
List of items considered:
  Handling CONNECTED Mode
  Handling IDLE to CONNECTED transition
  AMF Planned Maintenance/Out of Service
    Handling CONNECTED mode UE(s)
    Handling IDLE to CONNECTED mode UE(s)
  Failed AMF (Consequence)
  5G Temporary ID definition

## Slide 4: Handling CONNECTED mode UE(s)
A 5G-RAN node shall be able to support one or multiple TNL associations per GUAMI. An AMF shall be able to request the 5G-RAN node to add or remove TNL associations to a GUAMI. (Common for the 2 proposals)
Different solution options for changing AMFs when UE is in long CONNECTED mode:
  Source AMF provides TNL association of target AMF - AMF can ask RAN to use a different TNL association including the one for a different AMF (Cisco et al proposal, present in S2-173528 (but allowing AMF change not present in S2-173530))
  Source AMF deactivates N2AP association - AMF can perform hybrid deactivation of N2AP association on a per UE basis with the RAN:
    Subsequent MO transaction - the RAN selects an AMF, activates N2AP association with the new AMF and forwards N1/N2 transaction;
    Subsequent MT transaction - the AMF activates N2AP association and forwards N1/N2 message.
  (Nokia et al proposal in S2-173151)
Terminology:
The N2AP UE association is defined as the logical per UE association between a gNB and an AMF.
The N2AP UE-TNLA-binding is defined as the binding between a N2AP UE association and a specific TNL association.

## Slide 5: Solution Options - Differences
Source AMF
1. Use TNL-y of AMF2 for a given UE
Assumptions:
Require all AMFs (source and target) maintain other AMFs TNL association information.
Consequences:
RAN actions –
  Deactivate N2AP-TNL-x binding with TNL-x of AMF-1
  Deactivate N2AP association with AMF1
  Activate N2AP association with AMF2
  Activate N2AP-AMF2-TNL binding.
Open/Unclear – When should RAN perform take actions above?
Assumptions:
Each AMF maintains its own set of TNL associations.
Consequence:
Immediate RAN actions:
  Deactivate N2AP-TNL binding with AMF1.
  Deactivate N2AP association with AMF1.
Subsequent MT / MO transaction – RAN/AMF actions:
  MO - RAN selects an AMF
  MO/MT - Activate N2AP association.
  MO/MT - Activate N2AP-AMF2-TNL binding.
Target
AMF
RAN
Source AMF
1. Deactivate N2AP association for a given UE
Target
AMF
RAN
RAN impact almost the same for the 2 options
Trigger - Per UE Dissociation needed
Trigger - Per UE Dissociation needed

## Slide 6: Handling Connected mode UE(s) – Way forward
Source AMF provides TNL association of target AMF - Source AMF provides TNL association of target AMF. – Cisco et al proposal
Solution option Hybrid deactivation – Source AMF can perform hybrid deactivation of N2AP association on a per UE basis with the RAN. – Nokia et al proposal
Revision of Cisco proposal – Source AMF can perform hybrid deactivation of N2AP-TNL binding on a per UE basis with the RAN.
Huawei proposal – Change of AMF by remapping the AMF ID to another instance in the RAN.
Agreed Way forward:
Source AMF can perform hybrid deactivation of N2AP-TNL binding on a per UE basis with the (R)AN. For subsequent MO transaction, AN goes to the same AMF denoted by the AMF ID.
Editor’s note: Whether there is a need to change AMF in the Connected and transition from IDLE to CONNECTED mode scenario is FFS. Whether this is for a single UE or a group of UE(s) is FFS.

## Slide 7: IDLE to CONNECTED mode
RAN behavior for forwarding N1/N2 messages and/or selecting an AMF
Solution Option 1 (Cisco et al proposal):
  RAN uses the AMF Group and AMF ID in the temp ID to forward the N1/N2 message
  No Option for AMF not to disassociate itself for a given UE.
Solution Option 2 (Nokia et al proposal):
  If AMF decides to disassociate itself from IDLE UE(s), then it can do one of the 2 things:
    5G-GUTI allocated for the UE contains a fixed value for AMF ID (per UE)
    AMF requests RAN (per AMF message) to select an AMF from the AMF group for UE(s) providing a temporary ID that contains the corresponding AMF. (per node)
    For subsequent MO transactions:
    RAN can select any AMF from AMF Group. For the selected AMF, the RAN reactivates an N2AP association for the UE for the selected AMF and it forwards the N1/N2 message.
  If AMF has not taken any of the above 2 actions, RAN uses the AMF Group and AMF ID in the temp ID to forward the N1/N2 message.

## Slide 8: Slides beyond this not discussed

## Slide 9: Way forward
Solution Option 1 or Solution Option 2?

## Slide 10: AMF Planned maintenance
Solution Option 1 (Cisco et al proposal)
  Connected mode UE(s) – AMF initiates N14 relocation on a per UE basis by transferring UE context. Target AMF notifies RAN and all other CP NFs with the update.
  IDLE mode UE(s):
    AMF can page the UE(s) to update the temp ID with target AMF ID.
    Alternatively, RAN configuration updated by taking AMF out of service. Subsequent MO transaction, RAN selects an AMF from the AMF Group and forwards it to the AMF. RAN tries to select an AMF from the same AMF Group. Otherwise, it may select an AMF from a different AMF Group.
Solution Option 2 (Nokia et al proposal)
  An AMF shall be able to instruct the RAN to not consider itself anymore when selecting AMFs from the AMF Group. Upon receipt of this indication from the AMF:
  For UE(s) in IDLE mode, RAN should perform AMF reselection if the UE provided temporary ID indicates the AMF ID of an AMF that indicated planned maintenance.
  For UE(s) in CONNECTED mode, RAN should select a new AMF and create the N2AP association with a newly selected AMF when the subsequent N2 transaction occurs.
  RAN can select an AMF from the same AMF Group. Otherwise, it may select an AMF from a different AMF Group.

## Slide 11: Way forward
Solution option 1 or Solution option 2?

## Slide 12: Other interfaces
Solution Option 1 (Cisco et al proposal):
  Target AMF informs other CP NFs (e.g. SMF, PCF) immediately about a change of the termination point of the related interfaces (e.g. N11, N15, etc.) for a given UE (per UE).
Solution Option 2 (Nokia et al proposal):
  When an AMF decides to dissociate itself from per UE association - Serving AMF may decide not to update other CN CP NFs immediately. In this case, other CP NFs (e.g. UDM, AUSF, PCF) consequently send the AMF terminated UE specific requests to AMF known to have previously served the UE, and that results in:
  Redirection from the AMF that has previously served the UE to AMF actually serving the UE (triangular re-routing or re-route via RAN as described in 3GPP TS 3.502 clause 4.2.2.2.3), when the AMF serving the UE has changed; or
  the AMF that previously served the UE resuming service, when no (other) AMF is actually serving the UE.
  AMF Planned maintenance – In case other CP NFs are subscribed for such a notification, AMF can notify other CP NFs to not consider itself anymore when forwarding MT transaction.
    In this case, the other CP NFs shall reselect an AMF from an AMF group at the next UE terminated transaction. Other CP NFs should select an AMF from the same AMF Group.

## Slide 13: Way forward
Solution option 1 or Solution option 2?

## Slide 14: AMF Failure
Failure can be at AMF level. An AMF can fail in cloud environment.
When AMF fails some other AMF(s) within “AMF Group" is expected to take over and serve those UEs. This is not a planned activity.
MO transaction - RAN should select a different AMF from an AMF Group for a UE that was associated with failed AMF.
MT transaction - Other CP NFs – Should be also able to select a different AMF from an AMF Group instance to recreate/own UE state.
Check pointed/backed up "State" may be available for other AMFs within the "Group" to recover/reconstruct UE state.
Assumption - failures are expected to be common in cloud environments and we have to design to address these failures.