## Slide 1: Options for EPC Handling Non-IMS Exempt Services
S2-175377 Ericsson

## Slide 2: SA1 Requirement TS 22.011
3GPP PS Data Off Exempt Services:
  MMTel Voice;
  SMS over IMS;
  USSD over IMS (USSI);
  MMTel Video;
  Particular particular IMS services not defined by 3GPP, where each such IMS service is identified by an IMS communication service identifier;
  Device Management over PS
  Management of USIM files over PS (e.g. via Bearer Independent Protocol); and
  IMS Supplementary Service configuration via the Ut interface using XCAP.
IMS APN
Home Operator Service APNs
DL services are controlled in IMS core network
DL services are controlled in EPC

## Slide 3: SA1 Requirement During SA2#121 (May 15-19, 2017)
LS S1-172233 received (together with 22.011 CR S1-172208)
Reason for change: | The requirement for VPLMN-specific 3GPP PS Data Off Exempt Services was not part of the original GSMA requirement but it was inadvertently added to TS 22.011 by SA1. Also, the functionality has been excluded from stage 2 and 3 in Rel-14. This CR removes the requirement, but adds two separate sets of 3GPP PS Data Off Exempt services, one for home and another for roaming operation. The CR also makes some editorial corrections
Summary of change: | Removal of VPLMN-specific 3GPP PS Data Off Exempt services, adding two separate sets of 3GPP PS Data Off Exempt services, one for home and another for roaming, and some editorial corrections
Consequences if not approved: | Unnecessarily complex 3GPP PS Data Off service, and some typos
Title: | Removal of VPLMN-specific 3GPP PS Data Off Exempt services |  |  |  |  | 
Source to WG: | Nokia, Alcatel-Lucent Shanghai Bell, Deutsche Telekom, Telecom Italia, KPN |  |  |  |  | 
Source to TSG: | S1 |  |  |  |  | 
Work item code: | PS_Data_Off |  |  |  | Date: | 2017-05-08
Category: | F |  |  |  | Release: | Rel-14
Remove requirement of per PLMN list
New text:
3GPP PS Data Off may be activated based on roaming status, and the HPLMN may configure up to two sets of 3GPP PS Data Off Exempt Services for its subscribers: one is used when in HPLMN and another when roaming.
NOTE 2: The updating to the sets of configured 3GPP Data Off Exempt Services in the VPLMNs and HPLMN is not guaranteed to take effect in real time. The updating to the sets of configured 3GPP Data Off Exempt Services in the UEs is not guaranteed take effect in real time.

## Slide 4: Two main solutions discussed
Solution-2 PCRF/PCEF configuration, + HSS Configuration (HSS configuration intended for LBO only)
  List configured also in HSS
  List sent to PCEF/PCRF during
    Initial Attach,
    UE requested PDN connectivity,
    HSS initiated Subscribed QoS modification-like procedure…
  PCRF/PCEF configuration needed anyway because the visiting network may not be upgraded
Pros
  Supports dynamic update of list of DL filters in LBO
Cons
  Only needed for LBO but LBO is not suitable for any SA1 required non-IMS services.
  Require support of visiting network
  Impact on all CN nodes (i.e. HSS, MME, SGW, PGW and PCRF) in a number of procedures
  Impact on CN nodes for 2G/3G (i.e. HLR, SGSN & GGSN).
Solution-1 PCRF/PCEF Configuration
  List configured in PCRF or PCEF if no PCRF
Pros
  Simple solution requiring no additional impact if PCRF is deployed
  Small impact on PCEF if PCRF is not deployed
  No impact on the visiting network
  Same solution works for 2G/3G and 4G
Cons
  If LBO is needed, it can be difficult to re-configure the PCRF or PCEF in the roaming partner’s network.

## Slide 5: Proposed way foRward
Accept Solution-1 PCRF/PCEF Configuration for Data Off Phase 2
If there are new services required in the future, similar analysis is needed whether LBO can be adopted for those services.