## Slide 1: Intermediate SMF/UPF selection and the architecture
Huawei, HiSilicon

## Slide 2: Deployment assumption for SMF/UPF
Option 1: The SMF within a region serves all UPFs
  All UPFs are controlled by the same group of SMF, regardless whether UPF is deployed at edge office or at CO.
Option 2: Hierarchical deployment of SMF
  Two different sets of SMFs exists:
    SMFs that controls local UPF (e.g. located at edge)
    SMFs that controls UPFs that are more generic (e.g. located in CO)
  Intermediate SMFs are inserted due to the UPF at edge may be controlled by only one SMF.

## Slide 3: Additional SMF Insertion for Option 2
Before UE moves to an area served by local SMF
After UE moves to an area served by local SMF:
  Original UPF can still serve the UE.
  Additional SMF is inserted to support access to local DN for some specific traffic, i.e. not only due to the connection issue.

## Slide 4: Scenario for SMF Selection
Deployment Option 1
  The selection of SMF is dependent on the region the UE camped, within one region, only one SMF is needed.
    In initial PDU session establishment, only one SMF within the region is selected
    When ULCL/BP is inserted, if the UE still within the region, no additional SMF is needed
  If UE moves into another region, an additional SMF is inserted together with an intermediate UPF which terminates the N3 reference point.
Deployment Option2
  The selection of SMF is dependent on UE location and whether ULCL/BPF is needed, i.e. MM/SM procedure.
  If UL-CL/BPF is needed, additional SMF that controls the ULCL/BPF may need to be inserted, during PDU session establishment or at a later stage.
Conclusion: Additional SMF selection due to the: location and/or UL-CL/BPF are needed

## Slide 5: Selection of intermediate SMF that controls N3 UPF
This corresponds to deployment option 1
The intermediate SMF controls UPF that connects to RAN the UE is currently camping
Selection of this intermediate SMF does not need to consider PDU session requirements, e.g. whether ULCL is needed at that location
AMF has enough information to select the intermediate SMF
Observation: The intermediate SMF that controls UPF that connects to RAN may be selected by AMF

## Slide 6: Selection of intermediate SMF that controls ULCL/BP
In deployment option 2, an intermediate SMF may be inserted due to the insertion of ULCL/BP
AMF is not aware of PDU session information, e.g. whether ULCL/BP is needed, hence AMF does not have enough information to select the intermediate SMF that controls ULCL/BP.
It is better that this kind intermediate SMF is selected by Anchor SMF.
Observation: Anchor SMF selects the intermediate SMF that controls ULCL/BP

## Slide 7: Insertion of SMF that controls ULCL/BP during mobility
During mobility related procedure, it is possible both intermediate SMF that controls N3 UPF and intermediate SMF that controls ULCL/BP need to be selected:
  It is preferred that this 2 intermediate SMFs are collocated, hence, intermediate SMF controls both N3 UPF and ULCL/BP (or N3 UPF and ULCL/BP are collocated).
  AMF does not have enough information to select such intermediate SMF
  It is proposed that Anchor SMF selects intermediate SMF
Proposal: Anchor SMF selects the intermediate SMF.

## Slide 8: Function of Additional SMF
Option A
  N1 signaling termination
  N2 signaling termination
  Event handling, e.g. SR, location reporting
  UPF selection
  N4 session management
  Possible local charging and QoS enforcement
Option B
  UPF selection
  N4 session management
  Possible local charging and QoS enforcement
  N1 signaling termination in Anchor SMF
  N2 signaling termination in Anchor SMF
  Event handling in Anchor SMF, e.g. SR, location reporting

## Slide 9: The Architecture Option A
The additional SMF interfaces with both AMF and SMF via N11 and Nxy respectively

## Slide 10: The Architecture Option B
The additional SMF interfaces only with SMF via Nxy

## Slide 11: Comparison of Option A/B
Option A
  Pros:
    DDN is sent from additional SMF directly to AMF.
  Cons:
    Couples SM with MM (in step 5 & 6), AMF has to be involved for SM management. Or, AMF needs to have message relay function between anchor SMF and additional SMF (step 5 & 6).
    More messages needed during additional SMF insertion/relocation.
Option B
  Pros:
    Clean SM/MM separation.
    Fewer messages during additional SMF insertion/relocation
  Cons:
    DDN has to be sent via anchor SMF.
Proposal: Option B is selected, that is, additional SMF interfaces with anchor SMF via Nxy reference point.