## Slide 1: QCI-5QI for URLLC
3GPP SA WG#122, 26 – 30 June, 2017, San Jose Del Cabo, Mexico
S2-174348

## Slide 2: content
Background
Discussion – proposals on the specification new QCIs and 5QIs
New definition of the Packet Error Loss Ration (PELR) for URLLC
Proposal on the new parameter values

## Slide 3: Background
URLLC requirements as documented in TS 22.26 are considered in Rel-15 LTE and NR RAN WIs:
  Work Item on shortened TTI and processing time for LTE (RP-171468)
  Work item on Ultra Reliable Low Latency Communication for LTE (RP-171489)
  Work Item on New Radio (RP-171485)
SA#76 updated the SA2 WID EDCE5 adding a new objective:
  Mechanism to inform RAN on a per bearer level whether the traffic requires low latency e.g. by making use of the low latency features being defined by TSG RAN
In the QoS framework a mechanism to inform RAN about QoS characteristics is based on QCIs specifying certain QoS characteristics signalled to RAN.
Consequently, following the legacy approach, it is proposed to introduce new QCIs providing characteristics addressing the URLLC use case.

## Slide 4: discussion (1)
There are two LTE RAN work items in Release 15 introducing support for low latency and high reliability.
The work Item on shortened TTI and processing time for LTE (RP-171468) is improving latency only and is close to completion. For EDCE5 only support for low latency is included in the objectives.
Proposal 1: To enable the possibility of selective support for the low latency, a single additional QCI indicating low latency only, i.e. not combined with high reliability, shall be specified.

## Slide 5: Discussion (2)
The work item on Ultra Reliable Low Latency Communication for LTE (RP-171489) starts in October ‘17 and will introduce support for high reliability in LTE RAN. Given new QCIs as wrt RP-171468 concerning latency improvements are needed rather soon and very soon thereafter wrt RP-171489 new QCIs to capture new reliability characteristics are needed as well, we propose:
Proposal 2: New QCIs that capture both, i.e. combined low latency and high reliability requirements, shall be specified.

## Slide 6: Discussion (3)
Release15 RAN WI on New Radio (NR) (RP-171485) addresses support for high reliability and low latency requirements as documented for URLLC in TS 22.261 and hence new 5QIs are needed to describe these requirements.
Proposal 3: New 5QIs capturing both, low latency and high reliability requirements, shall be specified.
Given that, based on the URLLC use cases, same requirements are going to be addressed by the respective LTE RAN and NR Rel-15 functionalities, the following is proposed:
Proposal 4: The URLLC requirements shall be described by
  the same QoS characteristics specified for NR and LTE;
  the same parameter values shall be specified for the 5QIs and QCIs respectively.

## Slide 7: Proposals summary
Proposal 1: To enable the possibility of selective support for the low latency, a single additional QCI indicating low latency only, i.e. not combined with high reliability, shall be specified.
Proposal 2: New QCIs that capture both, i.e. combined low latency and high reliability requirements, shall be specified.
Proposal 3: New 5QIs capturing both, low latency and high reliability requirements, shall be specified.
Proposal 4: The URLLC requirements shall be described by
  the same QoS characteristics specified for NR and LTE;
  the same parameter values shall be specified for the 5QIs and QCIs respectively.

## Slide 8: New peLr definition for urllc
In TS 23.203 it is defined that the PDB should be fulfilled with a confidence level of 98%. This is sufficient for most GBR applications, but not for URLLC services. In order to cater for the more stringent requirements of URLLC, the definition must be improved.
In R2-1704377, RAN2 fed back that the definition of PDB and PELR need to be improved to be suitable for URLLC services.
Proposal: A new resource type ‘delay critical GBR’ is introduced for delay critical services that require higher confidence level than 98% for the PDB, see S2-174350 (CR to TS 23.203)&S2-174349 (pCR to TS 23.501). For delay critical GBR bearers/flows, a packet which is delayed more than PDB shall be included in the PELR target.

## Slide 9: PDB consideration
UE
RAN
UPF
DN
RAN latency
PDB for 5QI
End-to-end latency (TS 22.261, Table 7.2.2-1)
TS 22.261, Table 7.2.2-1 provides relevant performance requirements for URLLC that are taken as input. The end-to-end latency can be larger than PDB in some deployments, and PDB larger than RAN latency, but for URLLC use cases can be assumed to be the same. Therefore, expected RAN latency can be the basis of the PDB values.

## Slide 10: Use Case - Power grid: substation protection
This case takes one of the examples for critical communications presented in TR 22.862 [1].
The general description consists of a case to automate the fault detection and isolation in the power grid to avoid large-scale power outages; this is increasingly important with the energy grid with the increased integration of renewable power sources and energy storage.
Nowadays, these systems either do not yet exist or are built around dedicated optical networks [2]. However, there is an existing large interest in utilizing flexible wireless systems to support the protection of substations.
Substations communicate in pairs, and there is a geographical correlation between the location of the substations and cellular base stations; with an average of one substation per base station.
1ms
2ms
2ms

## Slide 11: Use Case – Factory automation
This case considers an indoor factory environment with different objects, such as robotic units and self-driving machines performing dedicated production tasks, which are centrally controlled by a production center.
A static deployment with near-static channel is expected [3]. Even if some terminals are mobile, their speed can be expected to be limited, and variations will mostly be related to people and machinery in the environment [3].

## Slide 12: use case – Haptic remote control
The previous use cases consider at most moderate mobility. A further use case may be considered for outdoor wide-area which includes mobility.
For example, the remote control of an unmanned vehicle such as unmanned aerial vehicle (UAV), or a vehicle that needs remote operation like an unmanned taxi or a truck in a construction site.

## Slide 13: QCI values for URLLC cases
QCI Value | Resource Type | Priority Level | Packet Delay Budget | Packet Error Rate | Example Services
 | Delay critical GBR | 3 | 20 ms | 10-2 | Similar to ”Process automation” in TS 22.261, Table 7.2.2-1
 |  | 3 | 1 ms | 10-5 | Factory automation. Similar to “Discrete automation – motion control” in TS 22.261, Table 7.2.2-1
 |  | 3 | 5 ms | 10-5 | Power grid sub-station. Similar to “Electricity distribution – high voltage” in TS 22.261, Table 7.2.2-1 PDB: ~2 ms RAN latency, ~1ms CN
 |  | 3 | 10 ms | 10-5 | Haptic remote control. Similar to ”Remote control” in TS 22.261, Table 7.2.2-1
P. Schulz et al., "Latency Critical IoT Applications in 5G: Perspective on the Design of Radio Interface and Network Architecture," in IEEE Communications Magazine, vol. 55, no. 2, pp. 70-78, February 2017 [link]
3GPP TS 22.261 V15.0.0

## Slide 14: 5QI values for URLLC cases
5QI Value | Resource Type | Priority Level | Packet Delay Budget | Packet Error Rate | Example Services
 | Delay critical GBR | 3 | 20 ms | 10-2 | Similar to ”Process automation” in TS 22.261, Table 7.2.2-1
 |  | 3 | 1 ms | 10-5 | Factory automation. Similar to “Discrete automation – motion control” in TS 22.261, Table 7.2.2-1
 |  | 3 | 5 ms | 10-5 | Power grid sub-station. Similar to “Electricity distribution – high voltage” in TS 22.261, Table 7.2.2-1 PDB: ~2 ms RAN latency, ~1ms CN
 |  | 3 | 10 ms | 10-5 | Haptic remote control. Similar to ”Remote control” in TS 22.261, Table 7.2.2-1
P. Schulz et al., "Latency Critical IoT Applications in 5G: Perspective on the Design of Radio Interface and Network Architecture," in IEEE Communications Magazine, vol. 55, no. 2, pp. 70-78, February 2017 [link]
3GPP TS 22.261 V15.0.0

## Slide 15: References
[1] 3GPP TR 22.862 Feasibility study on new services and markets technology enablers for critical communications; Stage 1
[2] 5GPPP White paper on Energy Vertical Sector. “5G and Energy”.
[3] M. Luvisotto; Z. Pang; D. Dzung, "Ultra High Performance Wireless Control for Critical Applications: Challenges and Directions," in IEEE Transactions on Industrial Informatics, vol.PP, no.99, pp.1-1