## Slide 1: Selecting a set of slices instances serving a UE
Huawei Technologies

## Slide 2: Outline
Intention
Network slice instance selection
  consideration on slice instances
  selecting a set of slice instances
  routing to a set of slice instances
  selecting a slice instance for a session
Considerations
  early binding or late binding
  Allowed S-NSSAI and returned S-NSSAI values
  1-step or 2-step serving AMF discovery
Proposals
  Decision points
  Information flow details
Information flows
  Registration
  Session setup (incl. roaming)

## Slide 3: Intention
This contribution intends to resolve the following questions:
  What is the role of the newly introduced NSSF ?
  Where is the Allowed NSSAI computed ?
  Does the NSSF perform the role of a global NRF and performs the selection of the AMF candidate list itself ? If it does not, does it contact the NRF itself, or does it return sufficient information to the querying AMF to query the NRF ?
  Does the NSSF already associate slice instances to S-NSSAI at registration (early vs late binding) ?
  Does the NSSF already associate HPLMN slice instances to S-NSSAI at registration (early vs late binding) in case of roaming users ?
  What information is used at RRC layer to allow to route to the right serving AMF, when the Temporary identifier is not available ? Where does this information come from ? Shall this information be unique ?
  Does the AMF have to select the same slice instance for a secondary PDU session using the same S-NSSAI ?

## Slide 4: Network slice instance selection: consideration on slice instances (1)
Functional dimension
  A network slice instance (NSi) is end-to-end: it includes all functions necessary to serve a UE
  Functions are grouped into 3+1 parts:
    an access part
    a common part
    a specific part
    (a roaming part) – the roaming part in the HPLMN is a separate slice instance
Access part
Common part
Specific part
(Roaming part)
Structure of RAN part of the slice instance to be defined by RAN WGs
Roaming slice instance is
a separate slice instance in
the HPLMN. Roaming slice instances only have "specific parts".

## Slide 5: Network slice instance selection: consideration on slice instances (2)
Service dimension
  Slice instances are grouped into sets of one or more slice instances: a set of Slice instances
  Each slice instance within the set supports one or more S-NSSAI (there can be full or partial overlaps)
  Each UE is initially associated to one set of slice instances at registration.
    The individual slice instances represent the sum of the potential slice instances the UE can be connected to while registered.
    It does not mean that the UE will actually «use» each and every slice instance in the set.
  Each service (represented by an S-NSSAI) the UE uses is associated to one slice instance within the set. One slice instance can serve all or some of the services used by the UE. Some slice instances might never been used while the UE is registered.
  In roaming scenario, additionally, a roaming slice instance is associated to each home routed service the UE uses.
    Whether all these roaming slice instances belong to a set of slices is academic (as they are only "slice specific" parts – no common parts)
S1, S3, S4
S2, S3, S5
S6
S1, S3
S2, S4, S5
S6
HPLMN (in case of roaming)
S-NSSAIs supported by the network slice instance
There are multiple sets of slice instances in the network (PLMN) (note that all these sets of slice instances likely share (a part of) the RAN part of the slices, which is something not represented visually here

## Slide 6: Network slice instance selection: selecting a set of slice instances (1)
Selecting a set of slice instances:
  When the UE attaches to the network, it needs to be associated to a set of slice instances.
  It is routed to an AMF (see next slide).
  The AMF contacts some NF (let's call it XYZ for now).
  XYZ selects a set of slice instances for the UE, based on a set of criteria [INPUT] and returns information [OUTPUT] to the AMF to be able to identify whether it can serve the UE itself or if it reroutes (see next slide) to another AMF.
AMF
XYZ
?
This is a set of slice instances able to serve a certain list of S-NSSAIs. The box represents the AMF(s) serving the set of slice instances

## Slide 7: Network slice instance selection: selecting a set of slice instances (2)
Input information for the purpose of selecting a set of slice instances:
  requested S-NSSAIs
  subscribed S-NSSAIs
  other subscription information, that can help XYZ to discriminate between multiple sets of slice instances (SoSis) that could serve the UE
Output information for the purpose of selecting a set of slice instances:
  Information that can allow point to a specific set of slice instances (i.e. point to one common part of the set of slice instances)
  Identification information that can help pointing to a serving AMF in the registration area for that set of slice instance (it can be the same information as the previous bullet)
  NOTE: XYZ can do more than just selecting the set of slice instances (e.g. selecting the list of candidate AMFs itself – see next slides), in which case more input and/or output is required
AMF
XYZ
INPUT
Requested S-NSSAI(s) (if any, from the UE)
Subscribed S-NSSAI(s) (from the UE subscription info)
other subscription information (if necessary)
OUTPUT
Information to point to a specific set of slice instances
Information helping pointing to a serving AMF within that set of slice instances

## Slide 8: Network slice instance selection: routing to a set of slice instances
At initial registration (and in subsequent signalling where the Temp ID is not usable):
  the RAN needs to be able to route the UE to an AMF.
  the RAN makes use of the information it has received (from UE and/or from the network). There might be no information.
  based on internal heuristics (configured), the RAN analyses the information available and selects a target AMF. If no information is available, an AMF "by default" is selected.
  In many cases, information provided should be sufficient to route to a proper serving AMF. In some cases, it might require the target AMF to reroute to another serving AMF.
  It is useful for the RAN to have information [ROUTING INFO] that allows to route to a serving AMF within the set of slices to which the UE is associated.
  Possibly, ROUTING INFO should just be sufficient to single out the set of slice instances to which the UE is associated, among all the sets of slice instances in the PLMN
    it can be a single value or composed value, as long as it uniquely points to a given set of slices within the network)
AMF
?

## Slide 9: Network slice instance selection: selecting a slice instance for a session
When an incoming request comes for a new (SM) session:
  The request may be associated with an S-NSSAI (not mandatory)
  In fine, a set of network functions belonging to one of the slice instances of the SoSi, capable of supporting the S-NSSAI (and the required service, e.g. DNN for SM sessions), need to be selected.
  The selection of the slice instance itself could be separate from the selection of the function, or combined. In any case, at least the S-NSSAI and other specific service information (such as DNN for SM) needs to be provided as INPUT.
  In some cases (e.g. HR roaming scenario), additionally, a "specific" slice instance in the HPLMN needs to be selected (see slide on slice binding for discussion on how to select that slice instance).
AMF
NRF
NRF returns a list of SMFs suitable for S-NSSAI "S3", it could down select the list based on configuration or leave the choice to the AMF (e.g. AMF may select based on other PDU sessions already established)
SMF
S1, S3, S4
S2, S3, S5
S6
SMF
SMF
S3
S3?
{Red SMF,Green SMF}

## Slide 10: Consideration: early or late binding
Early binding:
  during the assignment of the UE to a set of slice instances, each S-NSSAI is mapped to a specific slice instance within the set. This assignment is returned to the AMF an stored in its UE context.
  roaming: during the assignment of the UE to a set of slice instances, the HPLMN is also contacted to assign for the UE a specific slice instance for each of the S-NSSAI.
Late binding:
  during the assignment of the UE to a set of slice instances, XYZ only verifies that the slice instances within the set collectively support all Allowed S-NSSAI, but do not assign yet a specific slice instance for each S-NSSAI. Assignment of a specific slice instance for the S-NSSAI is only performed when the UE requests a session for this S-NSSAI.
  roaming: during the assignment of the UE to a set of slice instances, the HPLMN is not contacted for any assignment. Assignment of a specific slice instance in the HPLMN is only performed when the UE requests a HR session for this S-NSSAI.
    NOTE: in the roaming case, each slice instance could be fully independent, i.e. there is no need that they all belong to a single SoSi, since there are no identified required common NFs, compared to the serving PLMN.
  Additionally: when the UE requests additional sessions for the same S-NSSAI, it is possible to allow that new sessions are associated with a different slice instance (e.g. in order to perform "soft relocation")

## Slide 11: Consideration: Allowed S-NSSAI and returned S-NSSAI
Allowed S-NSSAI value can be computed based on:
  Requested S-NSSAI (when present)
  Subscribed S-NSSAI of the UE
  availability of the S-NSSAI within a "most compatible" set of slice instances: i.e. when assigning a UE to a set of slice instances, the set of slice instances should cover most S-NSSAI. When there is no best choice, the selection of one set of slice instances versus another should be based on operator deployment choices.
  Computation of the Allowed S-NSSAI could be done at the (querying or serving) AMF before/after allocation to a set of slice instances, or by XYZ. In any case, XYZ should tailor the set based on the support of S-NSSAIs by the selected set of slice instances. Also, XYZ could use subscribed S-NSSAIs to "understand" priorities for the UE (e.g. subscribed S-NSSAI could be ordered by priority).
Returned S-NSSAI values
  The network should return the list of Allowed S-NSSAI to the UE.
  Question: what does it return if the UE did not provide any S-NSSAI ?
  Question: what if the S-NSSAI used by the network is different from the one requested by the UE and needs to be mapped (e.g. UE requests "V2x/Cars" or "V2X", and subscription says it's a Hyunta car, and assigns the V2x to "V2x/Hyunta")
  The network could use the returned S-NSSAI to provide sufficiently unique information so that the set of slice instances serving the UE can be uniquely identified

## Slide 12: Consideration: 1-step or 2-step serving AMF discovery
When the UE registers, XYZ is queried by the querying AMF to get the UE assigned to a set of slice instances. Once this assignment is done, a serving AMF belonging to that set of slice instances, in the location where the UE is, needs to be selected.
Selection of the set of slice instances is done at the XYZ.
Selection of the individual AMF instance is done at the AMF.
Between the two steps, however, there are several steps that need to be performed:
  (A) Identification of a group of AMFs within the set of slice instances, based on location, etc.
  (B) Identification of a list of candidate AMF within that group of AMFs
Multiple proposals on the table:
  (1) XYZ performs (A) and (B) and returns the list of candidate AMFs to the querying AMF. In that case, XYZ has also the role of an global NRF for the purpose of AMF selection.
  (2) XYZ performs (A) and queries a global NRF. The NRF performs (B) and returns the list of candidate AMFs to XYZ. XYZ then returns the list of candidate AMFs to the querying AMF.
  (3) XYZ performs (A) and returns the identification of a group of AMFs to the querying AMF. The querying AMF queries a global NRF. The NRF performs (B) and returns the list of candidate AMFs to the querying AMF.
    NOTE: in that case, the querying AMF could identify it could be the serving AMF before sending the request to the NRF.

## Slide 13: Proposals
We propose the following:
  This is based on the assumptions on deployment and the considerations listed in the previous slides
  The choices imply that the integrator will properly configure the sets of slice instances available in the network to provide services to the its UEs (own and roaming).
(1) At registration, late binding (serving and roaming)
  Rationale: early binding is not required. While it is not anticipated to have the slice instances change very dynamically within a "SoSi", it is not as static as a physical configuration, and there is no advantage associated with early selection of slice instances, provided the SoSi maintains a number of slice instances capable of fulfilling all the Allowed S-NSSAIs of the UEs it is serving.
(2) At session setup, late binding (serving and roaming), only S-NSSAI is used
  Rationale: same consideration as above. It is expected that the operator (both serving and roaming) will ensure that there is a set of slice instances (resp. roaming slice instances) that can provide all services that a UE should expect simultaneously anyway. There is no need for network slice instance identification in the information flow.
(3) At subsequent session setup, late binding as well
  Rationale: there is no technical need identified to have two independent sessions using the same S-NSSAI to be imperatively served by the same slice instance. This also allows for soft migration to a new serving slice and as well as dynamic load balancing between slices.
(4) XYZ is NSSF, i.e. identification of a list of candidate AMFs is performed by a global NRF. To allow both separate and combined deployments, it is proposed that the NSSF queries itself the global NRF. This way, they can be combined without affecting the signalling.
  Rationale: the role of the NSSF (selecting the best set of slice instances for the UE) is different from the role of the global NRF (identifying the list of candidate NFs within a specific location, based on the life cycle management of the NFs). There is a slight optimisation possibly in having the querying AMF being able to decide before the NRF query whether it can serve the UE itself. However, having the NRF queried by the NSSF could allow the combination of the NSSF and global NRF in certain deployments.
(5) In roaming scenario, NSSF does not need to contact the HPLMN at registration.
  Rationale: Interaction with HPLMN happens at subscription information retrieval from hUDM. Subscribed S-NSSAI should be sufficient information from the HPLMN. Any mapping or further adaptation can be done in the vNSSF based on roaming agreements.
(6) Returned S-NSSAIs can be different from Requested S-NSSAIs
  Rationale: Not only the network should be able to take out certain S-NSSAIs, but it should also be able to "remap" S-NSSAIs. This allows to cover the case where the UE did not provide any S-NSSAI in the first place. Additionally, this allows to ensure that the NSSAI used in RRC (provided it is decided it is a collection of S-NSSAI) is sufficiently unique to identify with certainty the set of slice instances serving the UE. Alternatively, a separate value is required for RRC-NSSAI.

## Slide 14: Answers to the questions (1)
What is the role of the newly introduced NSSF ?
  NSSF selects a set of slices instances for serving a UE
  and possibly: NSSF computes the Allowed NSSAI from the provided input
  and possibly: NSSF assigns individual slices instances within this set for each S-NSSAI in the Allowed NSSAI
  and possibly: NSSF queries an NRF to find a list of serving AMFs within the set of slice instances selected to serve the UE
  or possibly: NSSF selects a list of candidate AMFs within the set of slices instances selected to serve the UE
Where is the Allowed NSSAI computed ?
  Querying AMF computes the NSSAI from the Requested NSSAI and the Subscribed NSSAI
  Querying AMF forwards the Requested NSSAI and the Subscribed NSSAI to the NSSF, NSSF computes the Allowed NSSAI, using the input and slice information (e.g. what set of slices supports best the combination requested by the UE)
Does the NSSF perform the role of a global NRF and performs the selection of the AMF candidate list itself ? If it does not, does it contact the NRF itself, or does it return sufficient information to the querying AMF to query the NRF ?
  To allow more flexibility, it is better if the NRF is defined separately from the NSSF, but that the NSSF does the query to the NRF. Then, it is easier for a deployment to combine NSSF & NRF, as it would look the same from the Querying AMF
  Alternatively: always combine the NSSF & the global NRF
  Alternatively: always split the NSSF & the global NRF. The Querying AMF queries the NRF in a second separate step

## Slide 15: Answers to the questions (2)
Does the NSSF already associate slice instances to S-NSSAI at registration (early vs late binding) ?
  The NSSF does not need to associate the individual slice instances to the S-NSSAIs at registration
  Alternatively: the NSSF may associate or shall associate the individual slice instances to the S-NSSAIs at registration
Does the NSSF already associate HPLMN slice instances to S-NSSAI at registration (early vs late binding) in case of roaming users ?
  The NSSF does not need to associate the individual HPLMN slice instances to the S-NSSAIs at registration (does not need a roaming interface between vNSSF and hNSSF)
  Alternatively: the NSSF may associate or shall associate the individual HPLMN slice instances to the S-NSSAIs at registration (requires a roaming interface between vNSSF and hNSSF)
What information is used at RRC layer to allow to route to the right serving AMF, when the Temporary identifier is not available ? Where does this information come from ? Shall this information be unique ?
  The information can be the Allowed S-NSSAI – it is unlikely to be unique
  Alternatively: The information can be the Allowed S-NSSAI, modified so that it can be unique
  Alternatively: The information can be a routing RRC NSSAI, sufficiently unique to point to a specific set of slice instances from anywhere within the PLMN. This can resolve to a properly serving AMF within the registration area
Does the AMF have to select the same slice instance for a secondary PDU session using the same S-NSSAI ?
  It is not necessary to select the same slice instance for a secondary PDU session using the same S-NSSAI – consequently, it is probably not necessary to use NSi-IDs at the AMF-NRF interaction
  Alternatively: it is possible/required to select the same slice instance, in which case, some sort of identification of the serving slice instance (NSi-ID) is required in the AMF-NRF interaction

## Slide 16: Proposals: information flow details
Input from querying AMF to NSSF:
  Requested S-NSSAIs (if provided)
  Subscribed S-NSSAIs
    Subscribed S-NSSAIs can contain S-NSSAIs that allow NSSF to allocate the UE to certain specific sets of slice instances
Output of NSSF:
  Allowed S-NSSAIs
    index matching requested S-NSSAIs. Values can be different from either Requested S-NSSAIs and Subscribed S-NSSAIs
  "AMF group"
    this information is sufficient to point to all the AMF that serve the selected set of slice instances, regardless of UE location
Routing information (information used for the RRC)
  Allowed S-NSSAIs
  If Allowed S-NSSAIs needs to be a strict replica of Requested S-NSSAIs, then any value provided alongside Allowed S-NSSAIs that can uniquely point to the set of slice instances (SoSi) serving the UE in the PLMN
Input to NRF (either from querying AMF or from NSSF) for AMF selection
  "AMF group" (see above)
  UE location (which information elements TBD, e.g. TAI, registration area, etc)
Output from NRF
  list of candidate serving AMFs in the location of the UE

## Slide 17: Information flow: registration

## Slide 18: Information flow: session setup (incl. roaming)

## Slide 19: Annex: highlight of differences with other proposals
Similarities with (N)
  Late binding in HR session setup
  No interaction with HPLMN at registration
  Allow for 1-step selection of set of slice instances and serving AMF candidate list
Differences with (N)
  Late binding in non-roaming and LBO session setup
  Late binding for subsequent session setup
  No NSi-ID
  Allowed S-NSSAIs is computed in NSSF
Similarities with (Z)
  Allowed S-NSSAIs is computed in NSSF
  Allow for 2-step selection of set of slice instances and serving AMF candidate list
Differences with (Z)
  Late binding of S-NSSAIs to network slice instance used for session
  No NSi-ID
  No interaction with hNSSF
  UE location information is used for AMF selection, not for slice instance selection