## Slide 1
Network Slice Instance selection
Agenda Item: 6.5.1
WI/Release: 5GS-Ph1/Rel-15
Supporting companies: Nokia, Alcatel-Lucent Shanghai Bell, Sprint, T-Mobile USA,NEC
San Jose Del Cabo, Mexico; 26-30 June 2017
Tdoc# S2-174538

## Slide 2: NSI selection architectures and relationship to Architecture without slicing
Slicing architecture options with separate NSSF: NSI selection belongs to separate function, separate NSI selection and Function discovery except for AMF selection in some proposals (The NRF for AMF is NSSF in some proposals). NSI Selection roaming interface needed. Message count increases
NSI Selection with Augmented NRF
NSI selection with standalone NSSF
RAN
AMF
V
-
NRF
V
-
SMF
H
-
SMF
H
-
NRF
V
-
PLMN
/
S
-
PLMN
H
-
PLMN
No slicing architecture

## Slide 3: Augmented NRF: Registration
VPLMN
HPLMN

## Slide 4: AUGMENTED NRF: SM PDU session creation

## Slide 5: Standalone NSSF: Registration
VPLMN
HPLMN

## Slide 6: Standalone NSSF: PDU session creation no early binding

## Slide 7: Standalone NSSF: PDU session creation with early binding

## Slide 8: Side by side comparison
 | Augmented NRF | Standalone NSSF | Standalone NSSF with early binding | comments
Decision on allowed NSSAI at every registration time | AMF | V-NSSF | V-NSSF + H-NSSF | Exporting from AMF the decision adds load on the AMF signalling interface (subs data, UE capabilities need to go to NSSF). For Nokia solution, Allowed NSSAI is permission to use slice not guaranteed of slice instances availability.
Decision on NSI selection | NRFs | NSSFs | NSSFs | AUG.NRF: NRF selects NSIs for NSSAI at AMF discovery time in V-PLMN, at PDU establishment for HPLMN NSI IDs for SMF in HPLMN. Standalone NSSF: NSSF with no early binding selects NSIs associated to NSSAI and the AMF in V-PLMN. The H-NSSF selects at PDU establishment for HPLMN NSI IDs for SMF in HPLMN. With early binding: the NSSF also gets NSI-IDs for the NSSAI from HPLMN for Slices with DNN in HPLMN Both NSSF based solutions require an extra trip to NSSF In HPLMN (whether at early, or late binding)
AMF selection | AMF | V-NSSF | V-NSSF | In Ericsson standalone NSSF solution the NRF is invoked for FQDN of AMF resolution after NSSF returns the FQDN of AMF
SMF selection | AMF | AMF | AMF | 
AMF discovery | NRF | N/A | N/A | In network where NRF is configured to return just one function instance address, then NRF also performs selection.
SMF discovery | NRF | NRF + NSSF | NRF | SMF discovery without early binding requires a NSSF query first if SMF is in HPLMN
Caching of Function selection rules | YES | NO for AMF | NO for AMF | The results of NRF queries can provide list of candidate functions and rules for e.g. load balancing among these. This is not possible if NSSF does AMF selection all the time.
New roaming i/f required | No | Yes | Yes | V-NSSF to H-NSSF interface
Need to pass subscription data, UE capabilities from AMF to NSSF | No | YES | YES | Allowed NSSAI selection is done outside AMF in several standalone NSSF in solutions. this requires passing info from AMF to the NSSF.

## Slide 9: Conclusions on comparing solutions
We prefer a single function discovery service provided by an augmented NRF that offers also the NSI selection option versus two separate service based interfaces (one for NRF and one for NSSF) that cannot live independently – one for function discovery and one for NSI selection – as
  this leads to two separate transactions needlessly, when we need to discover a function, and
  the NSI selection function is not something that can be used atomically and independently for other reason to then discover network functions in the slice – so this does not really qualify for an independent API that can be reused for other reasons than Function discovery.
Side effect of 1) is that we can keep same architecture for Slicing and non slicing scenarios and a single API
In Augmented NRF solution we need no new interdomain interface between new peering functions, unlike for the case of Standalone NSSF (V-NSSF / H-NSSF i/f)
In Augmented NRF solution we do not need at registration time to interact with HPLMN for early binding (we connect to HPLMNs only upon SM events)
In Augmented NRF solution we do not need to export subscription data and other UE context info to NSSF for Allowed NSSAI selection: clear separation between ALLOWED NSSAI determination and NSI selection. Allowed NSSAI is a “permission concept” which determines which mutually compatible set of slices a UE can use in the current Registration area, and not a resource allocation concept. NSI selection needs not any subscription info, all is based on picking a NSI suitable to serve a S-NSSAI in a UE independent fashion (i.e. based on load balancing rules).
NRF can also perform function selection if it is configured to just returns a single IP address
NRF can pass to requesting functions a list of candidate functions and criteria for selection for caching subsequently and avoid subsequent queries.
One NRF (and possibly a failover NRF) is configured per function. It is up to each NRF routing a NF discovery request to another NRF if needed based on information the requesting function provides (like the S-NSSAI and DNN). This model is already assumed in the roaming case for NRF (see TS23.502 Figure 5.2.7.1-2: Nnrf_NF Discovery across PLMNs information flow).
Isolation of NRFs for a different slices across roaming boundaries or inside a PLMN per S-NSSAI can be achieved by devoting some NRFs to a certain S-NSSAI. However we do not believe that this should be a crucial aspect of any solution as which NRF to populate is a deployment and network configuration issue that needs no special handling once the general principle is agreed that a NRF can invoke another NRF based on S-NSSAI and/or DNN based routing.

## Slide 10: Possible questions to shape the way forward
Confirm (or not) that ALLOWED NSSAI is a decision that the AMF undertakes based on subscription data and other UE related information (including its current RA), i.e. the AMF does not need to export these decision data to an external function.
Do we prefer a two step approach whereby a NSI is selected via a service which is not NF instances aware (NSSF) and then a function inside the NSI is selected using another service which is NF instances aware(NRF), or a single step shall achieve both via an augmented NRF (in other words, when slicing is deployed, the service for function discovery is simply augmented with slice/slice instance awareness/scoping)? Note: using a separate NSI selection service means conceptually adding a second logical roaming interface between H-PLMN and V-PLMN.
If answer to question 2) resulted in two step approach, do we want early binding with H-PLMN, whereby the V-PLMN for every S-NSSAI which has a DNN using Home routed approach, obtains a NSI-ID from HPLMN at registration time, or we postpone this to the time when a PDU session request for a Home routed DNN in a Slice happens?

## Slide 11
THANKS