## Slide 1: Discussion on N3GPP registration from UE point of view
3GPP SA WG 2 Meeting#122
26 - 30 May 2017, San Jose Del Cabo, Mexico
Source: LG Electronics
Title: TS 23 502 Discussion on N3GPP registration
Document for: Discussion
Agenda Item: 6.5.10 Non-3GPP access specific functionality and flows
Work Item / Release: 5GS_Ph1 / Rel-15
S2-174592
LG Electronics

## Slide 2: Candidate solutions – NAS over IKEv2
Analysis on re-registration & re-authentication scenario
According to RFC 7296
“without AUTH” means initiator (UE) desires to use EAP before establishing IKE SA
According to RFC 7296
If responder is willing to use an EAP, it will add EAP payload in the response message. However, there is no “EAP” payload (Actual “EAP” is in the NAS and it is not visible in IKEv2).
Initiator think that responder is not going to use “EAP” so multiple IKE exchange is not possible.
This solution is not aligned with RFC 7296 and in order to support this solution, interaction between different layers is required
  IKEv2 needs to support multiple IKE exchange to support EAP-AKA’ authentication while there is no direct interface between IKE and EAP-AKA’ layer.
IKEv2
NAS
EAP-AKA’
Protocol stack in UE

## Slide 3: Candidate solutions – NAS over IKEv2
Possible solution to minimize impact in re-registration & re-authentication scenario
AMF duplicate EAP-AKA/Challenge and includes it both in NAS & N2 message.
N3IWF includes EAP-AKA/Challenge in IKEv2 signalling.
UE includes EAP-AKA/Challenge in NAS and IKEv2 signalling.
UE performs same authentication in each layer (i.e. IKEv2 & EAP-AKA’)
Is there an issue to duplicate EAP-AKA/Challenge message in the AMF/SEAF?
  Not sure whether this is acceptable from security point of view

## Slide 4: Candidate solutions – NAS over IKEv2
Analysis on re-registration & identity request without re-authentication scenario
  Is this valid scenario?
According to RFC 7296
“without AUTH” means initiator (UE) desires to use EAP before establishing IKE SA
EAP authentication is triggered in IKEv2 but UE doesn’t receive any EAP payload or EAP error message
This solution is not aligned with RFC 7296
Is it possible N3IWK generates EAP-Success message without any interaction with SEAF/AUSF?
  Not sure whether this is acceptable from security point of view

## Slide 5: Candidate solutions – NAS over EAP
Analysis on re-registration & re-authentication scenario
This solution is not aligned with RFC 7296 and in order to support this solution, interaction between different layers is required
  Security key needs to be changed with a shared key from EAP-AKA’ when Child SA is established while RFC mandates to use security key from EAP-5G
  Not sure whether this is acceptable from security point of view
According to RFC 7296
When EAP is used with IKEv2, a shared key from EAP authentication MUST be used to generate AUTH payload.
In this solution, IKEv2 is interact with EAP-5G to support multiple IKE exchange. So a shared key (from result of EAP-5G authentication) MUST be used for Child SA creation.
However, this solution proposes to use a shared key from EAP-AKA’ authentication when child SA is established
EAP-5G is used for multiple IKE message exchange
EAP-AKA’ in NAS message is used for authentication between UE and AUSF and it is transparent to N3IWF and IKE layer
EAP-5G
NAS
EAP-AKA’
IKEv2
Protocol stack in UE

## Slide 6: Summary
At this stage, no strong view which solution is better
However, we prefer minimizing UE & RFC impact. So we propose that
  If NAS over IKEv2 is applied
    Network provides EAP message in IKEv2 signalling by duplicating (in the AMF) or generating (in the N3IWF) EAP messages or;
    Find any other solutions
  If NAS over EAP is applied
    Find a solution that a security key of EAP-AKA’ authentication is used to establish Child SAs without any changes of RFC 7296