## Slide 1: Network Slicing Roaming Support
Tricci So
ZTE TX Inc.

## Slide 2
Open Issue: TS 23.501 related to Roaming for Network Slicing
The following EN in TS 23.501 clause 5.15.6 was proposed as the outstanding question on how the vPLMN and hPLMN are coordinated to support the roaming scenarios, especially for the consideration on the use of NSSF:
Editor's note: The details of the procedure to select specific functions in the HPLMN minimizing the interactions between VPLMN and HPLMN and the exposure of HPLMN topology are FFS.
The intent of this proposal is to address this specific issue by leveraging the Proxy Function that is described in TS 23.502 clause 4.17.5 and to identify the additional steps in the existing procedures in TS 23.502 clauses 4.2.2.2.2, 4.3.2.2.1 and 4.3.2.2.2.

## Slide 3
Considerations of the use of Proxy Function & NSSF to support roaming
What has been defined for the use of Proxy Function in case of roaming?
- As defined in TS 23.502, clause 4.17.5
According to TS 23.501, clause 6.2.14, NSSF is responsible for selecting the set of network slice instances to serve the UE. Also, according to TS 23.501, clause 5.15.6, each PLMN is responsible for selecting their respective network functions with the support of their respective NRFs.
However, based on agreement in SA2#122 (referred to meeting report), network slicing specification shall enable that NRFs know only about NFs belonging to a set of slices and NOT NFs from the whole PLMN. During the SA2#122bis, it was also agreed that NSSF can identify the serving target NRF for the given S-NSSAI(s) corresponding to the network slice instance(s), hence, during the roaming scenario, it is reasonable to have the vPLMN to also identify the home target NRF that supports the home NFs selection and discovery for the Requested S-NSSAI.
Finally, the NSSF is the same level of network function as the UDM. Hence, the discovery of NSSF is similar to the procedure to discovery the UDM (see TS 23.501, clause 6.3.8) for BOTH non-roaming and roaming scenarios.

## Slide 4
If none of the addresses of UDM, vNSSF and hNSSF are pre-configured at the serving AMF, the serving AMF obtains the addresses of vNSSF from the vPLMN NRF, and hNSSF as well as UDM from hPLMN NRF via the support of vPLMN NRF.
If Serving AMF is not operated in autonomous mode, it obtains the allowed NSSAI(vPLMN) from vNSSF after vNSSF examines Requested NSSAI (if provided) and Subscribed NSSAI from UDM. vNSSF may also provide the Target vNRF(s) as well target AMF set or candidates list of target AMFs for the Allowed NSSAI. Once the serving AMF is confirmed, i.e. after steps and ... In case of early binding (pre-configured policy in vNSSF) …..
Option-1: if there is “no” interface between vPLMN’s and hPLMN’s NSSFs, the serving AMF obtained the Target hNRF(s) directly from hNSSF over N22 by providing Allowed NSSAI(hPLMN).
Option-2: if there is interface between the NSSFs, the serving AMF obtained the Target hNRF(s) from hNSSF via vNSSF by providing Allowed NSSAI(hPLMN).
Proposal to address the Editor’s Note
- UE Initial Registration (Roaming)
UE
RAN
Serving
AMF
vNSSF
UDM
vPLMN- NRF
1
2
3
6
9
10
11
12
hPLMN- NRF
hNSSF
7
8
Proxy
Function
(see TS 23.502 clause 4.17.5)
4
5
vPLMN
hPLMN
Observation: In case of “early binding”, (a) Leveraging Proxy Function can provide the topology hiding, if needed. (b) Two viable options to support early binding without introducing additional procedures. Both (a) and (b) provide more privacy control and no more procedure steps in both non-roaming and roaming scenarios than leveraging the hierarchy NRF approach.
10
9
Option-1
Option-2

## Slide 5
UE
RAN
Serving
AMF
vNSSF
1
2
3
4
11
12
hNSSF
Proxy
Function
(see TS 23.502 clause 4.17.5)
Proposal to address the Editor’s Note
PDU Session Establishment Procedure
for Home-routed roaming scenarios
vPLMN
hPLMN
hTarget
-NRF
vTarget- NRF
vSMF
7
5
6
hSMF
Optional steps 3 and 4 are introduced only for late binding, to obtain the hTarget NRF for the support of selecting the hSMF and other slice related NFs in the hPLMN.
Option-1: if there is no interface between vPLMN’s and hPLMN’s NSSFs, the serving AMF obtains the hTarget NRF from the hNSSF by providing the Requested/default S-NSSAI(hPLMN)
Option-2: if there is interface between NSSFs, the vNSSF obtains the hTarget NRF from the hNSSF by providing the Requested/default S-NSSAI(hPLMN).
(2) For early binding case, the serving AMF would have obtain the hTarget NRF during UE registration procedure.
8
9
10
Option-1
Option-2
Observation: In case of “late binding”, (a) Leveraging Proxy Function can provide the topology hiding, if needed. (b) Two viable options to support early binding without introducing additional procedures. Both (a) and (b) provide more privacy control and no more procedure steps in both non-roaming and roaming scenarios than leveraging the hierarchy NRF approach.

## Slide 6
Conclusions
By leveraging ….
  the Proxy Function as described in TS 23.502 clause 4.17.5,
  the NSSF functionality as agreed in SA2#122bis to determine the target serving NRF to select NFs/services within the selected Network Slice instance(s) as described in TS 23.501 clause 5.15.5.2.1,
  This proposal is able to demonstrate an optimal and compatible roaming procedures as described in TS 23.502 clauses 4.3.2.2.1 and 4.3.2.2.2 to address the Editor’s
It is proposed to adopt the high-level concepts as described in this paper as described in slide-3 to 5 to resolve the following Editor’s note in TS 23.501 clause 5.15.6.
Editor's note: The details of the procedure to select specific functions in the HPLMN minimizing the interactions between VPLMN and HPLMN and the exposure of HPLMN topology are FFS.