## Slide 1
Emergency services –
System/RAT fallback
Devaki Chandramouli
Nokia, Nokia Shanghai Bell
SS2-178679

## Slide 2: Voice/Emergency services – Support for RAT/System fallback
SA2#122bis agreed to the following requirement for TS 23.501:
In order to support various deployment scenarios, the 5G System supports mechanism to direct or redirect the UE either towards E-UTRA (RAT fall back) or towards EPS (System fall back) for obtaining emergency services.
RAT fall back = NR/5GC -> E-UTRA/5GC
System fall back = NG-RAN/5GC -> E-UTRAN/EPC
Triggers to initiate fall back and the method to support fall back is FFS!

## Slide 3: Assumptions
Network indicates IMS PS Voice supported
Solution assume that the selected PLMN (or its equivalent PLMN) supports emergency services either natively in NR/5GC or NR/5GC performs emergency services fallback to another RAT/System that supports Emergency services natively.
When network indicates that emergency services is not supported natively in NR/5GC, UE autonomous selection of a certain PLMN/RAT for emergency services is possible however network assisted redirection is faster, reliable and necessary for liability reasons (allows providing target information to the UE reducing measurement/selection time (no trial and error), allows preparation in the target side etc).
Solution for redirection to another RAT shall not require PLMN search
When full blown Emergency services is not supported in the NR/5GC, any of the following could be true:
  NR/5GC do not support necessary location accuracy
  NR/5GC do not support PDU session/DRB for emergency services, GBR QoS flows for voice/emergency services
  NR/5GC do not support necessary ARP
  AMF does not support selection of appropriate SMF selection

## Slide 4: Solution option 1
Network always indicates support for emergency services
UE indicates Emergency PDU session request for Emergency services
UE performs IMS registration.
Upon UP and QoS flow setup for voice, when traffic for E911 starts, RAN detects that the traffic is for Emer. Services based on QFI=5QI=1 and ARP=1.
NG-RAN (NR) directs the UE towards E-UTRA/5GC or E-UTRA/EPC (depending on whether 5GC supports emergency services or not)
Proposed verbally by some companies during SA2#123
Pros:
UE has to always initiate only PDU session request for obtaining emergency services support
Cons:
Requires NR/5GC to support pretty much all the features of emergency services anyhow.
Redirection performed quite late.
Network indicates Emergency services support even though it is not supported natively
Requires selection of combo node. Service break would be non-seamless in absence of N26; Requires IP address service continuity
LCS initiated late thus this impacts the accuracy of network location at emergency call setup. Also, it requires LCS support in 5G System thus the need to perform fallback in this case, is questionable.

## Slide 5: Solution option 2
Network always indicates support for emergency services
UE indicates Emergency PDU session request for Emergency services
When SMF detects that the PDU session request is for Emergency services, SMF initiates request towards NG-RAN (via AMF) for redirection towards E-UTRA/5GC or E-UTRA/EPC (depending on whether 5GS supports emergency services or not). NG-RAN determines the method to perform redirection.
Proposed verbally by some companies during SA2#123
Pros:
UE has to always initiate only PDU session request for obtaining emergency services support.
Cons:
Requires AMF to support SMF selection for emergency services.
Requires SMF to know about NR and target RAT/System capabilities to determine whether redirection should be supported or Emergency PDU session can be served natively.
Network indicates Emergency services support even though it is not supported natively
Requires selection of combo node. Service break would be non-seamless in absence of N26; Requires IP address service continuity (actually unclear whether this approach assumes IP address setup in the source).

## Slide 6: Solution option 3
If the network indicates support for IMS PS voice support (= YES) and no support Emergency services (= NO), then in order to initiate Emergency call, normal UE should initiate Service request with service type emergency towards 5GC; Network will then redirect the UE to the appropriate RAT/System.
When AMF detects that the Service request is for Emergency services, AMF initiates request towards NG-RAN for redirection towards E-UTRA/5GC or E-UTRA/EPC (depending on whether 5GS supports emergency services or not). NG-RAN determines the method to perform redirection.
Based on Nokia/Intel proposal (S2-178148/S2-177961 ) to SA2#123
Pros:
Allows notifying target information, preparation in the target RAT/system to enable faster redirection of UE to provide support for emergency services
Requires no emergency related feature to be supported in NR, AMF, SMF
Cons:
Requires UE to initiate “emergency registration (limited services) and/or PDU session request for emergency services to perform emergency call” when network indicates emergency support (= YES) or initiate Service request with service type emergency when network indicates no support for emergency services (= NO) but indicates IMS voice support (= YES)

## Slide 7: Way forward proposal
Based on analysis of various solutions, we believe Solution 3 should be adopted as a way forward to support emergency services fallback in rel-15.