## Slide 1: Examples for impacted procedures for increasing the number of LTE/EPS bearers to 15
(Attachment to S2-180251)

## Slide 2: Procedures impacted - summary
 | Procedure | High level impact | Relevant stage2 TS(s) / section(s)
Auth & location management | E-UTRAN attach | UE to indicate capability, internal network signalling to confirm support from various nodes | TS 23.401, section 5.3.2.1
 | TAU procedure (Idle mode mobility within E-UTRAN) | Some bearers may not be retained if target nodes (MME, SGW) don’t support 15 bearers | TS 23.401, sections 5.3.3.1 & 5.3.3.2 (TAU with and w/o SGW change, respectively)
 | RAU procedure (Idle mode mobility from E-UTRAN to UTRAN/GERAN) | Only up to 8 bearers can be retained – but formally 11 can be handed over to SGSN. | TS 23.401, sections 5.3.3.3 (RAU to S4 SGSN); ) and D.3.5 (RAU to Gn SGSN)
 | UE & network triggered service requests | If the new eNB, where the UE connects to does not support 15 bearers, then some bearers may need to be released. | TS 23.401, sections 5.3.4.1 and 5.3.4.3
Session management | UE requested PDN connectivity | The UE’s request may be rejected, if some nodes (eNB, MME, SGW or PGW) do not support 15 bearers. Special case for this can be bearers needed for UE detectable emergency session | TS 23.401, section 5.10.2 TS 23.167, section 7.1
 | Dedicated bearer activation | The bearer activation may succeed or fail depending on the capabilities of UE, eNB, MME, SGW and PGW support for 15 bearers | TS 23.401, section 5.4.1
 | UE requested bearer resource modification | See dedicated bearer activation (which is invoked) | TS 23.401, section 5.4.5
Handover | E-UTRAN handover – X2 and S1 based handover | Some bearers may not be retained if target nodes (eNB, MME, SGW) don’t support 15 bearers | TS 36.300, section 10.1.2.1 (X2 based HO) TS 23.401 sections 5.5.1.1.2&3 (X2 based HO w/o and with SGW relocation); Section 5.5.1.2.2 (S1 based HO)
 | E-UTRAN to UTRAN/GERAN handover | Only up to 8 bearers can be preserved – but formally 11 can be handed over to SGSN | TS 23.401 sections 5.5.2.1 (HO to UTRAN with S4 SGSN), 5.5.2.3 (HO to GERAN w/ S4 SGSN), D.3.3 (hard HO & SNRS relocation), D.3.7 (HO to GERAN w/ Gn)
 | Mobility from E-UTRAN to non-3GPP access | The new limit of 15 EPS bearers and the corresponding EPS bearer IDs present | TS 23.402, section 8.1 (generic aspects for HO w/o optimisations for multiple PDNs)

## Slide 3: Procedures with modification / overview
E-UTRAN initial attach
  Goal: Ensure that the UE capability can be taken into consideration later / during mobility and session management procedures
  Required functional change: Add the handling of new UE capability indication for supporting 15 bearers: store in the MME (but no network support indication, thus no indication needed from SGW/PGW, see key decisions). MME to collect/store information on the other node’s support of 15 bearers.
  Other change / clarification needed: none identified
Tracking area update (idle mode mobility in E-UTRAN), involving MME and/or SGW change
  Goal: Ensure that the TAU procedure is successful also in a network that has uneven node capabilities for supporting 15 EPS bearers, by retaining a selected subset of bearers that can be supported by the target nodes.
    When UE has more than 8 bearers and the target eNB supports only 8 EPS bearers
    When UE has more than 11 bearers and target MME and/or SGW only supports 11
  Required functional change:
    The target MME shall indicate in the Context Request if it supports 15 bearers.
    In the lack of that, the source MME shall select bearers to be retained, provide them in a “selective list” of EPS Bearer Contexts to target MME, release the rest of the bearers at the and of the TAU procedure.
    If there is an SGW change, and the UE supports 15 bearers, the target MME may need to s
    The source or target MME may need to release bearers that it had to filter out/could not update.
  Other change/clarification needed: none identified
RAU procedure (Idle mode mobility from E-UTRAN to UTRAN or GERAN)
  Goal: Ensure that RAU procedure is successful and the maximum number of bearers is preserved
  Required functional change:
    Source MME to select EPS bearers to be retained/send restricted list of bearer contexts to SGSN; this shall be applied both for S10 or Gn interface. (The S4 SGSN is never expected to indicate support of 15 bearers). The MME shall release any bearers that used EPS bearer IDs that are reserved in GTPv1-C.
  Other change/clarification needed: The existing text about SGSN releasing bearers that can’t be supported on UTRAN/GERAN remains relevant but may need to be changed/adjusted.

## Slide 4: Procedures with modification / overview (cont.)
UE or network initiated service request
  Goal: Ensure that the procedure is successfully executed also when the eNB that the UE is connecting to does not support all the bearers that were active before the UE went into idle mode
  Required functional change: The eNB shall indicate if it supports 15 bearers and if not, the MME shall down-select the bearers to be retained/activated as ERABs and S1 bearers. The MME shall release the rest of the bearers.
  Other change/clarification needed in TS: None
UE requested PDN connectivity
  Goal: Ensure that the network supports the highest number of EPS bearers for a UE, subject to the EPC node capabilities
  Required functional change: None (with the assumption that UE has no information about the network support for 15 bearers).
  Other change/clarification needed in TS: Describe the consequences of the UE having no information about the no. of bearers supported by the network: UE may initiate PDN connectivity that is rejected by the network due to the no. of bearers exhausted on the network side.
Dedicated bearer activation
  Goal: The network shall support QoS by activating bearers beyond 8 if the UE supports it.
    It is noted that any optimisation for the node selection must have happened before this procedure, at this stage the relevant limitations from the capabilities of the selected SGW & PGW will apply.
  Required functional change: MME (which allocates the EPS bearer IDs for the new bearer) shall take into consideration whether the UE and the involved nodes (SGW, PGW, eNB) support 15 bearers. For this, the MME is expected to have information received during the attach/TAU procedure and the setup of the relevant default bearer.
  Other change/clarification needed in TS: None identified (some notes might be needed)
UE requested bearer resource modification
  Goal: Refer to dedicated bearer activation
  Required functional change: Refer to dedicated bearer activation
  Other change/clarification needed in TS: None identified

## Slide 5: Procedures with modification / overview (cont.)
Handover within E-UTRAN
  Goal: Ensure that the handover procedure is successful also in a network that has uneven node capabilities for the max. no of bearers, by retaining the selected subset of bearers that can be supported by the target nodes
    When UE has more than 8 bearers and the target eNB supports only 8 bearers
    When UE has more than 11 bearers and target MME and/or SGW only supports 11
  Required functional change:
    For X2 based HO: Source eNB to send the set of ERAB bearers to the target eNB which can be supported; release the rest of bearers if the HO is completed successfully. The HO procedure does not provide any possibility for an indication from the target eNB on its capabilities, so RAN2 / RAN3 work is needed to decide how to achieve this. TS 36.300 and several stage3 RAN specifications may need to be updated.
    If X2 handover requires SGW relocation, the MME shall ensure that those bearers as sent to the new SGW that can be supported there, if the new SGW selected does not support 15 bearers and it shall release the rest via the old SGW. As the procedure does not allow the MME to receive indication from the new SGW before the session setup to it, It needs to be agreed, how to achieve this goal.
    For S1 based HO: During the HO preparation phase, the source and target MMEs shall ensure that those bearers shall be retained that can be supported by the target MME, eNB and SGW. It needs to be agreed how to achieve this, as the procedure does not cater for capability indication from the target nodes. The MMEs then need to release the rest of the bearers if the HO is completed successfully.
  Other change/clarification needed:
    For X2 based HO, TS 23.401 should reflect the changes needed in TS 36.300.
    LSs (or joint discussion) will be needed to align TS 36.300 and TS 23.401
Handover from E-UTRAN to UTRAN/GERAN
  Goal: Ensure that the handover procedure is successful and retains a selected subset of bearers that can be supported by the target RAN and the GPRS core network
  Required functional change:
    During the HO preparation phase, the MME shall include only 11 bearers in the Forward Relocation Request. Then if the HO is completed successfully, it shall release the rest of the bearers at the end of the handover execution phase.
    While there are different variants of the procedure, depending on S10 or Gn being used, and UTRAN or GERAN being the target, these steps should be applicable for all.
  Other change/clarification needed:
    None identified

## Slide 6: Procedures with modification: E-UTRAN attach
This is section 5.3.2.1 in TS 23.401
Step1: The UE shall include a new capability of supporting 15 EPS bearers in the Attach request / the UE core network capability parameter
Step2: The eNB shall add indication of its support when it forwards the Attach Request.
  The MME can use this information later e.g. in dedicated bearer setup procedure. It should not use EPS bearer IDs that were reserved earlier – even though they were not reserved for S1AP. This could be stage3 decision
Step13-16: During the setup of the initial PDN connection, the MME shall indicate the UE + MME supporting 15 bearers and the SGW and PGW shall return the indication of their support as well
  This information shall be used by the MME later e.g. in dedicated bearer setup or UE initiated PDN connection. The MME shall not setup more than 11 bearers / use dedicated bearer ID values that were reserved earlier
Note: as per the proposal to key decision1, the MME does not provide any confirmation of the network support for 15 bearers to the UE

## Slide 7: Procedures with modification: Tracking Area Update procedure with Serving GW change
Section 5.3.3.1 in TS 23.401 has to be updated
Step2: The UE shall indicate its support for 15 EPS bearers in the TAU request / UE network capability
Step3: The eNB shall include indication of its support of 15 bearer to the TAU request.
  Note: The MME can use this in later procedures for this UE, see Attach description
Step4: The new MME shall include indication of its support of 15 bearer to the old MME
Step5: The old MME shall include more than 11 bearer context, or use any of the earlier reserved EPS bearer ID values in the Context Response only if it received this indication. If needed, it will down-select the bearers to 11 or further as needed due to backward compatibility in EPS bearer ID values
  Note: As the UE and network may establish and subsequently release bearers, it will be possible to have some bearers using those EPS bearer IDs that were reserved earlier, even if there is less than 11 bearer active at this time
  Note: If only such bearers are active that use these EBI values (1..4), the TAU will fail if some of the nodes don’t support 15 bearers – the MME shall send TAU reject.
Steps 8 -11: If the new MME supports 15 EPS bearers, it shall include indications of this in the Create Session Requests and it will receive indication from the SGW and PGW(s) on their support of 15 EPS bearers. In the lack of such indication, the new MME may need to down-select the EPS bearers for the UE, in line with step5.
  Note: if the MME sends all the Create Session Requests in parallel, those that use the EBI values that were reserved earlier, will be rejected by SGW (which does not support the 15 EPS bearers)
  Note: The MME can use the information on the SGW and PGW support later, e.g. in dedicated bearer setup procedure
  Note: all EPS bearers may be preserved even if the new eNB does not indicate support for 15 bearers; they will be only be down-selected when the UE goes to connected mode – see the UE & network initiated Service Request procedures.
New conditional steps 19A/19B (to be added to the figure): The old MME shall release those sessions PDN connections and/or dedicated bearers that it had to filter out in step 5. Alternatively, the new MME shall do the same for sessions/bearers it could not establish in steps 8-11.
  This action can be done by a combination of Delete Session Requests and Delete Bearer Commands (refer e.g. to RAU procedure later)
  Note: this should be shown logically separate steps, as in step18, the MME does set the Operation Indication flag (i.e. it is not a real deletion)
(Note: This figure is corrupt/broken in TS23.401, I could not update it)

## Slide 8: Procedures with modification: Tracking Area Update procedure with Serving GW change
Section 5.3.3.2 in TS 23.401 needs to be updated
This is similar to the previous case (TAU w/ SGW change), the same additions/changes shall be repeated, except those for the new MME (that has no new actions)
The diagram should be changed to add the steps that the old MME releases sessions and/or dedicated bearers (similar to the RAU step 17A)

## Slide 9: Procedures with modification: Routing Area Update with MME interaction and without S‑GW change
Section 5.3.3.3 in TS 23.401 needs to be updated
Step4: The MME shall execute the same type of down-selection as described for the TAU case when the new MME did not indicate support of 15 bearers
Steps 16-17: the MME processes here only those sessions that is has included in the Context Response (step4).
New conditional step 17A: the MME releases those bearers and corresponding sessions that it filtered out from the Context Response in step4.

## Slide 10: Procedures with modification: Routing Area Update (from E-UTRAN, using Gn to SGSN)
Annex D / section D.3.5 in TS 23.401 needs to be updated
Step2: The MME shall execute the same type of down-selection as described for the TAU case when the new MME did not indicate support of 15 bearers
Steps 13: the MME processes here only those sessions that is has included in the Context Response (step4).
New conditional step 14: the MME releases those bearers that it filtered out from the Context Response in step4

## Slide 11: Procedures with modification: UE triggered service request
Section 5.3.4.1 of TS 23.401 needs to be updated
Step2: eNB to indicate its support of 15 EPS bearers
Step4: in the lack of such indication, the MME shall down-select the EPS bearers (similar to / as described for the TAU procedure where the new MME does not support indicate support) and include those selected to be retained in the Context Response
Steps 8-12: Here, only those bearers are processed that have been included in the Context Response (step4)
New conditional step 13 (to be added to the figure 5.3.4.1-1, here just copied 17A from the RAU): the MME shall release those bearer that is filtered out for step4. For the release, the MME can use a combination of the MME requested PDN disconnection and the MME initiated dedicated bearer deactivation procedures
17A. MME initiated Dedicated bearer deactivation (refer to steps 2-9 of figure 5.4.4.2-1) /
MME Requested PDN Disconnection (refer to steps 2-6 of figure 5.10.3-1)

## Slide 12: Procedures with modification: Network triggered service request
Section 5.3.4.3 of TS 23.401 needs to be updated
There is no change needed, just clarification that the service request procedure may involve the release of some PDN connections and/or dedicated bearers as per 5.3.4.1

## Slide 13: Procedures with modification: UE requested PDN connectivity
Section 5.10.2 of TS 23.401 needs to be updated
New conditional/alternative step2a (to be added to the figure): The MME may reject the request depending on the support of 15 bearers by eNB, the MME itself, and the SGW
Step5a – conditional/alternative, to be added: The PGW may reject the Create Session request depending on its support of 15 EPS bearers

## Slide 14: Procedures with modification: UE Detectable Emergency Session
Section 7.1.1 of TS 23.167 needs to be updated
Step2 tells that “In the case that the UE has insufficient resources or capabilities to establish an emergency call due to other ongoing sessions then the UE should terminate the ongoing communication and release reserved bearer resources”
A note shall be added here that here, the UE shall assume that the network does NOT support 15 bearers.
This is needed as the UE will not receive network support indication, refer to key decision1.

## Slide 15: Procedures with modification: Dedicated bearer activation
Section 5.4.1 of TS 23.401 needs to be updated
New alternative/conditional step4A (to be added to the figure): the MME may accept/reject the request depending on the UE, eNB, MME and SGW support for 15 bearers
Note: the MME is supposed to have received the relevant information about the support of all these nodes – see the other procedures

## Slide 16: Procedures with modification: UE requested bearer resource modification
Section 5.4.5 of TS 23.401 needs to be updated
A note should be added (or alternative step?) that the dedicated bearer setup may succeed or fail, depending on the UE, eNB, MME, SGW and PGW support for 15 EPS bearers.

## Slide 17: Procedures with modification / X2 based handover
The handover is handled by the eNBs without core network involvement i.e. any difference between the source and target eNB capabilities must be handled by the RAN between these eNBs
Section 10.1.2.1 in TS 36.300 (maintained by RAN2) describes the X2 based HO (the figure is from there), while the X2 interface protocol, however, is defined in TS 36.423 (by RAN3).
As the Handover request (see step4 in the diagram) is the first message for the procedure, and it carries the information for all the ERABs to be setup (see 9.1.1.1 of TSS36.423), there appears to be 2 options to handle the case where the target eNB cannot handle the ERAB list containing more than 8 bearers:
  a.) Source eNB to have a priory information – would require a capability discovery for supporting 15 bearers in the X2 setup. There are no similar capability indications provided today.
  b.) Fail and retry, i.e. source eNB figuring out from a cause for failure that it needs to send max. 8 bearers. As HO is time critical, this is going to increase the HO failure rate.
RAN2 may decide to use a SIB to indicate to the UE whether the target cell (i.e. eNB) will support 15 bearers.
From the core network perspective, the outcome is that the path update (to SGW) is combined with bearer releases
Proposed action: SA2 to send LS to RAN2 and RAN3 to call out this impact.
See TS 23.401 related change for the same procedure in next slide

## Slide 18: Procedures with modification: X2-based handover without Serving GW relocation
Section 5.5.1.1.2 of TS 23.401 needs to be updated
A note should be added that during the HO in RAN, some of the bearers may need to be released – when the target eNB does not support 15 bearers and the are more than 8 bearers in use or some ERABs utilise the values that were reserved earlier (introduced only in Rel-15/for 15 bearers)
New conditional step / sub-procedure 7a shall be added to the handover completion, where the source eNB releases those bearers that it could not hand over.
Further discussion is needed, what is the best way to align the UE, RAN, EPC view of the bearers

## Slide 19: Procedures with modification: X2-based handover with Serving GW relocation
Section 5.5.1.1.3 of TS 23.401 needs to be updated
A note should be added that during the HO preparation / execution in RAN, some of the bearers may need to be released – when the target eNB does not support 15 bearers and the are more than 8 bearers in use or some ERABs utilise the values that were reserved earlier (introduced only in Rel-15/for 15 bearers)
Step2: If the target SGW does not support 15 EPS bearers, the MME may not be able to execute all the Create Session requests. The SGW may reject some of the requests (e.g. with EBI values that were reserved earlier), and/or the MME can down-select the sessions / EPS bearers in the same way as described e.g. for the TAU procedure.
  To be clarified: what happens here if a dedicated bearer can’t be supported but the default bearer is supported by SGW?
Steps 7a/b: a note should be added that these steps are relevant only for those sessions that have been successfully migrated to the new SGW
New step 7c (to be added to the figure): The MME shall release those sessions and/or dedicated bearers that have not been moved to the new SGW.
  This action can be done by a combination of Delete Session Requests and Delete Bearer Commands (refer e.g. to RAU procedure later)
  Note: this should be shown logically separate steps, as in steps 7a/b, the MME does set the Operation Indication flag (i.e. it is not a real deletion)
New conditional step / sub-procedure 7d shall be added to the handover completion, where the source eNB releases those bearers that it could not hand over.

## Slide 20: Procedures with modification: S1-based handover, normal
Section 5.5.1.2.2 of TS 23.401 needs to be updated
Step3: the MME may not be able to send all of the bearer contexts to the new MME.
  As per the key decision 6, the MME will not select target MME for the particular, i.e. it may not know if it support 15 bearers
  As per key decision 8, the MME will send the full list of bearer contexts.
  Conditional Step 3A/3B may be needed, to resend the Forward Relocation Request. This may be covered only in stage3 specifications though.
Step4: the target SGW may not support 15 EPS bearers;
  As in step4, the target MME (if it supports 15 bearers, i.e. it received the full list) shall send the full list. In this case some of the create session requests may fail / the target MME may need to down-select the sessions/bearers as described e.g. for TAU with SGW change and resend the relevant request(s).
Step5: the new eNB may not support 15 EPS bearers, and the may not have information about it
  The MME may not have information about the eNB support.
  As per key decision 8, it shall still send all the bearer contexts in the Handover Request.
  Conditional steps may be needed for the to down-select the requested ERAB list and resend the Handover command to the target eNB.
Step 16-17: a note is to be added that these steps are relevant only for bearers that could be handed over
New conditional steps/sub-procedures 17a/b is needed (should be added to the figure) where the source and/or target MME releases those sessions/bearers that could not be handed over. Refer to the TAU procedure / steps 19A/19B

## Slide 21: Procedures with modification: E-UTRAN to UTRAN Iu mode Inter RAT handover (with S4 SGSN) / preparation phase
Section 5.5.2.1.2 of TS 23.401 needs to be updated
Step3: The MME shall down-select the EPS bearer contexts, similarly to what is described for the RAU procedure and include in the Forward Relocation Request only those that can be retained Also may add a note here that those that were filtered out will be released after the successful completion of the handover

## Slide 22: Procedures with modification: E-UTRAN to UTRAN Iu mode Inter RAT handover (with S4 SGSN) / execution phase
Section 5.5.2.1.3 of TS 23.401 needs to be updated
New conditional step/sub-procedure 11C is to be added: the source MME shall release those bearers that have not been handed over / have been filtered out by the MME during the handover preparation.

## Slide 23: Procedures with modification: E-UTRAN to GERAN A/Gb mode Inter RAT handover (with S4 SGSN) / preparation phase
Section 5.5.2.3.2 of TS 23.401 needs to be updated
Step3: The MME shall down-select the EPS bearer contexts, similarly to what is described for the RAU procedure, and include in the Forward Relocation Request only those that can be retained Also may add a note here that those that were filtered out will be released after the successful completion of the handover

## Slide 24: Procedures with modification: E-UTRAN to GERAN A/Gb mode Inter RAT handover (with S4 SGSN) / execution phase
Section 5.5.2.3.3 of TS 23.401 needs to be updated
Step3: The MME shall down-select the EPS bearer contexts, similarly to what is described for the RAU procedure, and include in the Forward Relocation Request only those that can be retained Also may add a note here that those that were filtered out will be released after the successful completion of the handover
New conditional step/sub-procedure 14C is to be added: the source MME shall release those bearers that have not been handed over / have been filtered out by the MME during the handover preparation.

## Slide 25: Procedures with modification: MME to 3G SGSN combined hard handover and SRNS relocation procedure
Section D.3.3 of TS 23.401 needs to be updated
New conditional step/sub-procedure 19 is to be added: the source MME shall release those bearers that have not been handed over / have been filtered out by the MME during the handover preparation.

## Slide 26: Procedures with modification: E-UTRAN to GERAN A/Gb mode Inter RAT handover (with Gn SGSN) / preparation phase
Annex D / section D.3.7.2 of TS 23.401 needs to be updated
Step3: The MME shall down-select the EPS bearer contexts, similarly to what is described for the RAU procedure, and include in the Forward Relocation Request only those that can be retained Also may add a note here that those that were filtered out will be released after the successful completion of the handover

## Slide 27: Procedures with modification: E-UTRAN to GERAN A/Gb mode Inter RAT handover (with Gn SGSN) / execution phase
Annex D / Section D.3.7.3 of TS 23.401 needs to be updated
New conditional step/sub-procedure 15 is to be added: the source MME shall release those bearers that have not been handed over / have been filtered out by the MME during the handover preparation.

## Slide 28: Procedures with modification: Common Aspects for Handover without Optimizations for Multiple PDNs
Section 8.1of TS 23.402 needs to be updated
The new text shall describe the following:
  The UE supporting 15 bearers may have more bearers active than what can be handed over to the non-3GPP access
  It should define what the target is when handing over – but this is not very clear from the current text / from the earlier requirements
Further discussion is needed to agree, where the limitations in the non-3GPP access really are

## Slide 29: Other changes needed - summary
Aspect | High level impact | Relevant stage2 TS(s) / section(s)
Generic description of the handling multiple bearers / connected limitations | Should describe on high level the impacts coming from INOBEAR / interworking with non-supporting nodes | TS 23.401, could be somewhere under section 4.7.2 that describes the EPS bearers
MME generic description | Add MME role in handling the bearers for mobility | TS 23.401, section 4.4.2
Information storage | MME shall store information whether UE, eNB, SGW support 15 bearers | TS 23.401, section 5.7.2
UE core network capability | The UE capability for supporting 15 bearers shall be added | TS 23.401, section 5.11.3