## Slide 1: Discussion on Paging for non-3GPP access
3GPP SA WG 2 Meeting#125
22 - 26 January, 2018, Gothenburg, Sweden
Source: LG Electronics
Title: Discussion on Paging for non-3GPP access
Document for: Discussion
Agenda Item: 6.5.10 Non-3GPP access specific functionality and flows
Work Item / Release: 5GS_Ph1 / Rel-15
S2-180518
LG Electronics

## Slide 2: Network Triggered Service Request procedure
Current description on N3GPP paging
  AMF behavior in step 4b
    For 3GPP paging
      If the UE is in CM-IDLE state in 3GPP access and the PDU Session ID received from the SMF in step 3a has been associated with 3GPP access and based on local policy the AMF decides to notify the UE through 3GPP access even when UE is in CM-CONNECTED state for non-3GPP access, the AMF may send a Paging message to RAN node(s) via 3GPP access
    For N3GPP paging
      If the UE is simultaneously registered over 3GPP and non-3GPP accesses in the same PLMN, the UE is in CM-IDLE state in both 3GPP access and non-3GPP access, and the PDU Session ID in step 3a is associated with non-3GPP access, the AMF sends a Paging message to RAN node(s) via 3GPP access
  UE behavior in step 6
    For 3GPP paging
      If the UE is in CM-IDLE state in 3GPP access, upon reception of paging request for a PDU Session associated to 3GPP access, the UE initiates the UE Triggered Service Request procedure (clause 4.2.3.2)
    For N3GPP paging
      If the UE is in CM-IDLE state in both non-3GPP and 3GPP accesses, upon reception of paging request for a PDU Session associated to non-3GPP access, the UE may initiate the UE Triggered Service Request procedure (clause 4.2.3.2) which shall contain the List Of Allowed PDU Sessions that can be re-activated over the 3GPP access

## Slide 3: Paging issue for N3GPP
Scenario needs to be discussed
  UE is in CM-IDLE in 3GPP and N3GPP.
  AMF receives N3GPP PDU Session related notification first (①)
  AMF receives 3GPP PDU Session related notification later (⑤)
gNB
AMF
SMF (N3GPP PDU Session)
SMF (3GPP PDU Session)
① N3GPP PDU Session
⑤ 3GPP PDU Session
UE
③ Paging (N3GPP access)
② Paging Request (N3GPP access)
⑥ AMF decides to just wait for UE response
⑧ Paging Request (3GPP access)
④ UE decides NOT to respond to Paging
⑨ Paging (3GPP access)
Service Request
Time line
①
②
③
④
⑤
⑥
⑦
Paging supervise timer (T3513)
⑧
⑨
⑦ Paging timer expires
Very long delay for 3GPP PDU Session

## Slide 4: Candidate Solutions
Option 1: Mandating Service Request for "N3GPP" Paging
  The AMF keeps the received Namf_Communication_N1N2MessageTransfer related to 3GPP PDU Session and waits for UE response
  The UE initiate the Service Request procedure when it receives paging request indicating "non-3GPP access" even if there is no PDU Sessions can be transferred to 3GPP access
Option 2: "N3GPP" Paging override by "Both accesses" Paging
  The AMF sends another paging request indicating "both accesses"

## Slide 5: Detailed solution for Option 1
gNB
AMF
② Paging Request (3GPP access)
SMF (N3GPP PDU Session)
SMF (3GPP PDU Session)
UE
③ Paging (3GPP access)
⑤ AMF just wait for UE response
⑥ Service Request
⑦ AMF sends NAS Notification (N3GPP PDU Session ID)
Case 3: AMF receives 3GPP PDU Session related notification first and N3GPP PDU Session related notification later
④ N3GPP PDU Session
① 3GPP PDU Session
gNB
AMF
② Paging Request (N3GPP access)
SMF (N3GPP PDU Session)
① N3GPP PDU Session ID
UE
③ Paging (N3GPP access)
④ Service Request with List of Allowed PDU Sessions
Case 1: AMF receives N3GPP PDU Session related notification (i.e. Namf_Communication_N1N2MessageTransfer)
gNB
AMF
SMF (N3GPP PDU Session)
① N3GPP PDU Session
④ 3GPP PDU Session
UE
⑥ Service Request (List Of Allowed PDU Sessions = "no PDU Sessions can be transferred to 3GPP")
② Paging Request (N3GPP access)
Case 2: AMF receives N3GPP PDU Session related notification first and 3GPP PDU Session related to notification later
③ Paging (N3GPP access)
SMF (3GPP PDU Session)
⑤ AMF just wait for UE response

## Slide 6: Detailed solution for Option 2
gNB
AMF
⑥ Paging Request (both access)
SMF (N3GPP PDU Session)
SMF (3GPP PDU Session)
① N3GPP PDU Session
⑤ 3GPP PDU Session
UE
⑦ Paging (both access)
gNB
AMF
② Paging Request (N3GPP access)
SMF (N3GPP PDU Session)
① N3GPP PDU Session ID
UE
③ Paging (N3GPP access)
④ Service Request with List of Allowed PDU Sessions (Optional)
gNB
AMF
② Paging Request (3GPP access)
SMF (N3GPP PDU Session)
SMF (3GPP PDU Session)
UE
③ Paging (3GPP access)
② Paging Request (N3GPP access)
⑤ AMF just wait for UE response
⑥ Service Request
⑦ AMF sends NAS Notification (N3GPP PDU Session ID)
Case 3: AMF receives 3GPP PDU Session related notification first and N3GPP PDU Session related notification later
Case 2: AMF receives N3GPP PDU Session related notification first and 3GPP PDU Session related to notification later
Case 1: AMF receives N3GPP PDU Session related notification (i.e. Namf_Communication_N1N2MessageTransfer)
③ Paging (N3GPP access)
④ UE decides NOT to respond to Paging (N3GPP access) due to no PDU Sessions can be transferred to 3GPP
④ N3GPP PDU Session
① 3GPP PDU Session
⑧ Service Request (List Of Allowed PDU Sessions = "no PDU Sessions can be transferred to 3GPP")

## Slide 7: Proposal
For the simple UE & Network behavior
  Propose to choose option 1
    UE initiate the Service Request procedure when it receives paging request indicating "non-3GPP access" even if there is no PDU Sessions can be transferred to 3GPP access
Change Proposal (S2-180519)
  Step 4 of Network Triggered Service Request
    Clarify AMF behavior when it received both 3GPP and non-3GPP requests from SMF(s) at the same time
      If the UE is simultaneously registered over 3GPP and non-3GPP accesses in the same PLMN, the UE is in CM-IDLE state in both 3GPP access and non-3GPP access, and the AMF receives multiple requests associated with 3GPP and non-3GPP accesses at the same time, the AMF sends a Paging message with associated access "non-3GPP" to RAN node(s) via 3GPP access.
    Clarify AMF behavior when it received 3GPP request first and non-3GPP request later
      If the AMF, while waiting for a UE response to the Paging Request message for a 3GPP access PDU Session, receives an Namf_Communication_N1N2MessageTransfer message with the PDU Session ID associated with non-3GPP access, the AMF shall wait until the UE becomes CM-CONNECTED and send NAS Notification message containing the PDU Session ID associated with non-3GPP access to the UE over 3GPP access.
    Clarify AMF behavior when it received non-3GPP request first and 3GPP request later
      If the AMF, while waiting for a UE response to the Paging Request message for a non-3GPP access PDU Session, receives an Namf_Communication_N1N2MessageTransfer message with the PDU Session ID associated with 3GPP access, the AMF shall wait until the UE becomes CM-CONNECTED and perform activation of UP connection for the the PDU Session associated with 3GPP access.
  Step 6 of Network Triggered Service Request
    Clarify UE behavior when it received non-3GPP paging
      If the UE is in CM-IDLE state in both non-3GPP and 3GPP accesses, upon reception of paging request for a PDU Session associated to non-3GPP access, the UE may initiate the UE Triggered Service Request procedure (clause 4.2.3.2) which shall contain the List Of Allowed PDU Sessions that can be re-activated over the 3GPP access. If there is no PDU Session that can be re-activated over the 3GPP access, the UE includes the List Of Allowed PDU Sessions as an empty list.