## Slide 1
3GPP TSG SA WG2 Meeting #126 S2-181608
26 February – 02 March 2018, Montreal, Canada
Source: Telstra
Title: Summary of Telstra CRs for INOBEAR
Document for: Discussion
Agenda Item: 6.15
Work Item / Release: INOBEAR / Rel-15
Abstract of the contribution: The discussion paper provides a summary of how the different CRs presented in Montreal meeting address procedures and other sections of TS 23.401, TS23.402 and TS23.167 for INOBEAR.

## Slide 2: INOBEAR related CR summary: Types of changes and TSs modified
Type of change | TS | Tdoc | Comments
Adding feature definition for supporting 15 EPS bearers | 23.401 | S2-181780 | This CR adds a new section for defining support of 15 bearer as a feature, captures the main requirements, e.g. interworking between supporting/non-supporting UE and network, mobility etc.
Description of procedure impacts | 23.401 | S2-181782 | This addresses mobility management related changes – for mobility within E-UTRAN and E-UTRAN to UTRAN/GERAN
 | 23.401 | S2-181812 | This addresses changes required in handover related descriptions – for HO within E-UTRAN and IRAT HO from E-UTRAN to UTRAN/GERAN
 | 23.401 | S2-181813 | This CR contains updates for session management related descriptions – for UE request PDN connectivity and dedicated bearer setup procedures
Update for IMS emergency calling | 23.167 | S2-181815 | This CR adds clarification that the UE needs to assume that the network supports only 8 bearers. This is needed because there is no indication about the network support for 15 bearers.
Update for mobility to non-3GPP access | 23.402 | S1-181851 | The CR adds clarification about the limitations when handing over from E-UTRAN to non-3GPP access, for a UE supporting 15 EPS bearers
Other/various changes | 23.401 | TBC (may not be provided for Montreal) | The document will cover other updates needed in TS23.401, e.g. extending the UE capabilities for supporting 15 bearers

## Slide 3: Analysis of impacted procedures for increasing the number of LTE/EPS bearers (INOBEAR) Note: This analysis contains various stage3 related delibarations. It is provided as background only for SA2 / explanation for the changes in procedure related CRs S2-181782, S2-181812, S2-181813.

## Slide 4: Summary of procedure impacts and proposed changes /1 EMM mobility management and EMM connectivity mgmt
 | Procedure | Relevant stage2 TS(s) / section(s) | Sli-de # | High level impact | Conclusions for updating the stage2 TS
Auth & location management | E-UTRAN attach | TS 23.401, section 5.3.2.1 | 5 | UE to indicate INOBEAR support in UE network capability (step1) – as suggested by CT1 in LS C1-174658. As per KI1 & KI3B (c.f. S2-181208), no further signalling is needed. Note: the only time the MME makes use of this information is in dedicated bearer activation (section 5.4.1) | Step1 in the flow description shall be updated to reflect the UE capability indication
 | TAU procedure (Idle mode mobility within E-UTRAN) | TS 23.401, sections 5.3.3.1 & 5.3.3.2 (TAU with and w/o SGW change, respectively) | 6-7 | Some bearers may not be retained if target nodes (MME, in 5.3.3.1 also SGW) don’t support 15 bearers. But as bearers are not established, the eNB support is not relevant. NAS protocol extension will be needed to support the interworking between UE (+old MME) supporting 15 EPS bearers and a legacy new MME. The old MME shall prioritise the bearer contexts and GTP protocol extension using forward compatibility shall ensure any legacy (pre-Rel15) node will process only 8 bearers/the backward compatible EBI values. All lower-prioritised bearers above 8 and those that are using extended EBI values shall be sent in new/extended GTP parameters, which shall be defined by CT4. | There are several steps impacted, which will be treated entirely on the protocol level (these have to do with the encoding of bearer lists) – these shall be handled by CT groups / stage3 level However the bearer release in cases impacts the procedure, and should be indicated in stag2 flow. We propose that this is handled similarly as existing text for SGSN functionality for PDP context handling for E-UTRAN to UTRAN/GERAN mobility.
 | RAU proce-dure (Idle mode mobility from E-UTRAN to UTRAN/ GERAN) | TS 23.401, sections 5.3.3.3&6 (RAU to S4 SGSN with & w/o SGW change); and D.3.5 (RAU to Gn SGSN) | 8-10 | Only up to 8 bearers can be retained – but formally 11 can be handed over to SGSN. The MME shall prioritise/down-select the PDN connections/dedicated EPS bearers and send only those bearers that use backward-compatible EBI values (i.e. valid as NSAPI) / maximum 11 bearers to the SGSN. | The bearer prioritisation / selective release of the bearers is more deterministic here. However, similarly to the TAU procedure, the description of bearer release shall be added to the text only, as it is not part of the default / successful RAU procedure
 | UE & network triggered service requests | TS 23.401, sections 5.3.4.1 and 5.3.4.3 | 11-12 | The eNBs may not be upgraded in the whole PLMN at the same time, i.e. some will support 15 bearers before others. If the old eNB supported 15 DRABs, but the new eNB, where the UE connects to supports only 8 bearers, then some bearers contexts may not be preserved and will be released. The MME shall prioritise the E-RABs and shall need to use S1AP protocol extension to control which bearers will be released if the eNB supports only 8 bearers. | S1AP protocol extension / using existing forward compatibility mechanism should be used to handle the fallback to eNB supporting only 8 bearers. RAN3 resources will be required and SA2 should send LS to RAN plenary and RAN3 to ensure this. Text shall be added about the MME releasing the bearers that new eNB did not setup (only 5.3.4.1)

## Slide 5: Impacted procedures: E-UTRAN attach
This is section 5.3.2.1 in TS 23.401
High level impact
UE to indicate capability to support 15 EPS bearers.
As per KI1 & KI3B (see S2-181208), no further signalling is needed – network support for 15 bearers is not indicated to the UE
Impacted steps
Step1 (Attach Request) provides detailed information about the capabilities and preferences that the UE indicates. Support of 15 EPS bearers would be a similar capability to those that are listed here, therefore it shall be added.
The other steps are not changed (Note: The RAN work plan for INOBEAR does not include broadcasting eNB capability for 15 bearers / connecting to MME that supports it, therefore there is no need to add it to the text)

## Slide 6: Impacted procedures : Tracking Area Update procedure with Serving GW change
This is covered in section 5.3.3.1 in TS 23.401
High level impact
Some bearer contexts may not be preserved if target nodes (MME, SGW) don’t support 15 EPS bearers.
As agreed in KI4 (c.f. S2-181208), the old MME shall prioritise the bearer contexts and GTP forward compatibility shall ensure any legacy (pre-Rel15) node will process only 8 bearers/the backward compatible EBI values. All lower-prioritised bearers above 8 and those that are using extended EBI values shall be sent in new/extended GTP parameters, which shall be defined by CT4.
Impacted steps
In step1 (TAU request) the UE supporting 15 bearers has to indicate the bearer status. Given that the old MME may and the new MME may NOT support 15 bearers, the UE may indicate here bearer status for such bearers that the new MME does not understand.
Key observation: the NAS protocol has to be extended in order to support the interworking between such UE and the legacy new MME for the TAU procedure.
  The UE MUST NOT indicate the status of bearers with EBI=1..4 values in the EPS bearer context status IE (see sections 8.2.29 and 9.2.2.1 of TS24.301) of the TAU, as the legacy MME would reject the request. If the UE has EPS bearers with these EBI values, it shall include them into a new parameter (to be added to 24.301), e.g. “Extended EPS bearer context status”, where it would carry _only_ this information – keeping the EBI=5..15 in the existing EPS bearer context status IE.
Step5, sending Context Response is where the old MME shall ensure the prioritisation of the bearers for retaining the bearers with higher priority (e.g. ARP). This shall be done using forward compatibility of GTPv2C, the MME including the non-backward compatible part of the EPS new parameter, e.g. Extended Bearrer prioritisation will be then kept by the new MME and new SGW, if they do support 15 EPS bearers. Note that this will be handled based on GTP forward compatibility: information on bearers and the corresponding PDN connections shall be encoded into new optional parameters, e.g. “extended PDN connection” and/or “extended Bearer Context” within that IE. CT4 shall specify the way how this is extended.
Key observation: as only part of the bearers may be recognised by the new MME/new SGW, the rest of the bearer status is not updated in the PGW. Those bearers – or whole PDN connections, e.g. if the default bearer is impacted – need to be released at the end of the procedure
  CT4 or CT1 shall define how the PDN connections and/or dedicated bearers that were included in new GTP parameter(s) will be released if a node has not processed them. It seems to me that some capability indication over GTP would be needed so that a source node (old/new MME, new SGW) understands from the response that there is a fallback to pre-Rel15. While this is stage3, it should be understood as to my understanding those steps of bearer release should be added to these procedures.
Key observation: There has been a similar for this – the SGSN handling of the PDP contexts in RAU procedure for E-UTRAN to UTRAN/GERAN mobility. The text describes the relevant actions, but they are not added to the flow diagram as they are not part of the basic flow. We propose that the bearer release in this case is also only added to the text.

## Slide 7: Impacted procedures: Tracking Area Update procedure without Serving GW change
Section 5.3.3.2 in TS 23.401
High level impact
Same as in 5.3.3.1/TAU with SGW change – some bearers may be released if the new MME does not support 15 EPS bearers
Impacted steps
Same steps as 5.3.3.1, except that the sub-procedure of modifying the bearers is not impacted.
The MME’s task of releasing the bearers that were not transferred to the new MME successfully need to be added to the text

## Slide 8: Impacted procedures : Routing Area Update with MME interaction and without S‑GW change
Section 5.3.3.3 in TS 23.401
High level impact
Formally 11 bearer contexts can be forwarded to SGSN, but it will release those PDP contexts it cannot support in the destination RAN.
The MME shall prioritise/down-select the PDN connections/dedicated EPS bearers and send only those bearers that use backward-compatible EBI values (i.e. valid as NSAPI) / maximum 11 bearers to the SGSN.
Impacted steps
The MME does the down-selection in step4 (Context Response).
At the end of the procedure, the PDN connections/EPS bearers that could not be transferred to the new MME shall be released by the MME.
The old MME prioritising / down-selecting the PDN connections/bearers in Context Response and subsequently releasing those that were not preserved is to be added to the text.

## Slide 9: Impacted procedures : Routing Area Update with MME interaction and with S‑GW change
Section 5.3.3.6 in TS 23.401
High level impact
Formally 11 bearer contexts can be forwarded to SGSN, but it will release those PDP contexts it cannot support in the destination RAN.
The MME shall prioritise/down-select the PDN connections/dedicated EPS bearers and send only those bearers that use backward-compatible EBI values (i.e. valid as NSAPI) / maximum 11 bearers to the SGSN.
Impacted steps
The MME does the down-selection in step4 (Context Response).
At the end of the procedure, the PDN connections/EPS bearers that could not be transferred to the new MME shall be released by the MME.
The MME releasing of the PDN connections/EPS bearers that were not preserved is to be added to the text.

## Slide 10: Impacted procedures : Routing Area Update (from E-UTRAN, using Gn to SGSN)
Annex D / section D.3.5 in TS 23.401
High level impact
Formally 11 bearer contexts can be forwarded to SGSN, but it will release those PDP contexts it cannot support in the destination RAN.
The MME shall prioritise/down-select the PDN connections/dedicated EPS bearers and send only those bearers that use backward-compatible EBI values (i.e. valid as NSAPI) / maximum 11 bearers to the SGSN.
Impacted steps
The MME does the down-selection of bearers in step2 (SGSN Context Response).
At the end of the procedure, the PDN connections/EPS bearers that cannot be retained as PDP contexts shall be released by the MME.
This shall be added to the text

## Slide 11: Impacted procedures : UE triggered service request
Section 5.3.4.1 of TS 23.401
High level impact
The eNBs may not be upgraded in the whole PLMN at the same time, i.e. some will support 15 bearers before others.
If the old eNB supported 15 DRABs, but the new eNB, where the UE connects to supports only 8 bearers, then some bearers contexts may not be preserved and will be released.
The MME shall prioritise the E-RABs and shall need to use S1AP protocol extension to control which bearers will be released if the eNB supports only 8 bearers.
Impacted steps
Step4: The bearer prioritisation is executed by MME in this step – when sending Initial Context Setup Request. It is assumed that in S1AP protocol is extended to handle the fallback for a legacy eNB – that MME shall prioritise the E-RABs and request only the backward compatible subset of bearers in the existing “ERAB to Be Setup List” parameter. It will send those that use new (not-backward compatible) EBI values and any bearers above 8 to new S1AP in new parameters that are to be defined by the RAN3 group. E.g. an “Extended ERAB to be Setup List” parameter could be introduced.
Step7: The eNB responds with Initial Context Setup Response and it shall indicate which bearers it succeeded/failed to setup (E-RAB Setup List / E-RAB Failed to Setup List) + will need to indicate now explicitly that it processed the new parameters with the extended E-RAB list / what it failed to setup from those, if any. This could be included e.g. in an “Extended ERAB Setup List” and “Extended E-RAB Failed to Setup List”
Key observation: these aspects are handled on stage3/S1AP protocol level and do not need to be reflected on stage2 procedure / in TS23.401. However, it is absolutely important to engage RAN3 to make the S1AP changes to happen. RAN plenary in March should allocate time slots to INOBEAR for Q2/18 in RAN3 as well (not only RAN2). WE propose SA2 to send LS about the RAN3 aspects of INOBEAR to RAN3 and RAN plenary
At the end of the procedure, the MME to release those bearers that have not been setup by the eNB. Similarly to other procedures, this release shall be covered in the text. However, this is not really different from what is already described in step8: “The MME releases the non-accepted bearers by triggering the bearer release procedure as specified in clause 5.4.4.2. ” Therefore, no change is needed for this section.

## Slide 12: Impacted procedures : Network triggered service request
Section 5.3.4.3 of TS 23.401
High level impact
See UE triggered service request
Impacted steps
There is no change needed in the text, this is just referring back to the UE triggered service req.

## Slide 13: Summary of procedure impacts and proposed changes /2 Handovers
 | Procedure | Relevant stage2 TS(s) / section(s) | See Slide # | High level impact | Conclusions for updating the stage2 TS
Handover | E-UTRAN handover: X2 based HO | TS 36.300, section 10.1.2.1 (X2 based HO) TS 23.401 sections 5.5.1.1.2&3 (X2 based HO w/o and with SGW relocation); | 14-16 | SA2 currently uses the assumption that support of 15 bearers is homogenous across such nodes that have an X2 interface. Therefore, the HO itself is expected to retain all bearers. However, if the subsequent path switch involves an MME or SGW change and the target SGW does not support 15 bearers, then some bearers may need to be released after the HO. The GTPv2C protocol will need to be extended to support the graceful fall back to 8 bearers. The MME shall prioritise bearers for this. | There is no need to update TS36.300 and section 5.5.1.1.2 in TS23.401 The section 5.5.1.1.3 in TS23.401 – X2 HO with SGW change – needs to be updated to describe that the source MME may need to release bearers that were not successfully switched to the new SGW.
 | E-UTRAN handover S1 based handover | Section 5.5.1.2.2 (S1 based HO) | 17 | S1 based HO is expected to be the procedure where non-homogeneity in the RAN for supporting 15 ERABs is supported; also the HO can involve target MME and/or SGW not supporting 15 EPS bearers. Some of the existing bearers may be released during the HO, if the target eNB/MME/SGW does not support 15 bearers. The GTPv2-C and S1AP protocols shall be extended to handle such cases/fallback to 8 bearers gracefully. The source MME shall ensure that the bearers are prioritised in line with the operator preferences. | There are several steps impacted, which will be treated entirely on the protocol level (these have to do with the encoding of bearer lists) – these shall be handled by CT4 and RAN3 groups on stage3 level However the bearer release in cases impacts the procedure, and should be indicated in stag2 flow. We propose to add text description that the source MME shall release bearer that have not been preserved.
 | E-UTRAN to UTRAN/GERAN handover | TS 23.401 sections 5.5.2.1 (HO to UTRAN with S4 SGSN), 5.5.2.3 (HO to GERAN w/ S4 SGSN), D.3.3 (hard HO & SNRS relocation), D.3.7 (HO to GERAN w/ Gn) | 18-24 | The SGSN can formally support . | 

## Slide 14: Impacted procedures: X2 based handover / RAN view (Only background info for SA2)
Section 10.1.2.1 in TS 36.300 (maintained by RAN2) describes the X2 based HO, while the X2 interface protocol, defined in TS 36.423 (by RAN3).
The handover is handled by the eNBs without core network involvement i.e. any difference between the source and target eNB capabilities must be handled by the RAN between these eNBs
High level impacts
Some of the bearers may be released, if the source eNB supports 15 bearers but the target eNB does not.
The current assumption used in SA2 is that this scenario does not need to be supported, therefore it would be OUT OF SCOPE, not just in SA2, but also in RAN WGs. However, the minimum level of homogeneity for supporting 15 bearers in E-UTRAN is up to the RAN groups to be decided.
Impacted steps
Step4 (Handover request) is used to provide the list of all the ERABs to be setup in the target eNB (see 9.1.1.1 of TSS36.423). In order to support the graceful completion of the procedure, in case when the target eNB cannot interpret the full bearer list /a legacy node is not expected to receive/process more than 8 bearers for a UE), the X2AP protocol should be extended so that bearers above 8 should be carried in new optional information elements.
If not all bearers are handed over, the source eNB shall release those that failed to be handed over. From the core network perspective, the outcome is that the path update (to SGW) is combined with bearer releases
See TS 23.401 related change for the same procedure in next slide
As the assumption is that supporting X2 based HO across eNBs that support different number of EPS bearers is out of scope (subject to RAN decision), at this stage there is no change suggested in any TSs.

## Slide 15: Impacted procedures : X2-based handover without Serving GW relocation
Section 5.5.1.1.2 of TS 23.401
High level impact
As described in the previous slide, we assume that the eNBs both support 15 EPS bearers (or neither of them does), i.e. there is no impact from eNBs
With that assumption, there is no impact to this example procedure, as there is no new node involved in the core network either.

## Slide 16: Impacted procedures : X2-based handover with Serving GW relocation
Section 5.5.1.1.3 of TS 23.401
High level impact
SA2 currently uses the assumption that support of 15 bearers is homogenous across such nodes that have an X2 interface. Therefore, the HO itself is expected to retain all bearers.
However, if the subsequent path switch involves an MME or SGW change and the target SGW does not support 15 bearers, then some bearers may need to be released after the HO. The GTPv2C protocol will need to be extended to support the graceful fall back to 8 bearers. The MME shall prioritise bearers for this.
Impacted steps
In step 2, the MME shall prioritise the bearers (as per KI4) and use forward compatibility mechanism of GTPv2, i.e. include the PDN connection / bearer context information that is beyond the “legacy limits” (EBI values, >8 bearers) in new, optional IEs.
Step3a: If the target SGW is not supporting 15 EPS bearers, it will not understand the extended part of the list and it shall not include these extra bearers in the Modify Bearer Request.
Step4: The MME learns from the Create Session Response in step4 that the SGW did not setup all bearers (there will be no TEIDs for those sent in the new IEs).
The MME shall release those bearers that were not setup in the target SGW, via the source SGW – this shall happen in new steps after or in parallel with the resource release in the source SGW (7a/b).
The specification text shall be updated for the release of the bearers only – the handling of the extended bearer/PDN connection list in step3/3a is considered to be covered by stage3.

## Slide 17: Impacted procedures : S1-based handover, normal
Section 5.5.1.2.2 of TS 23.401
High level impact
Given that we cannot assume that the whole RAN in a PLMN has been updated, we have to assume that the target eNB may not support 15 bearers, while the source eNB does.
S1 based HO is expected to be the procedure where non-homogeneity in the RAN for supporting 15 ERABs is supported; also the HO can involve target MME and/or SGW not supporting 15 EPS bearers.
Some of the existing bearers may be released during the HO, if the target eNB/MME/SGW does not support 15 bearers. The GTPv2-C and S1AP protocols shall be extended to handle such cases/fallback to 8 bearers gracefully.
The source MME shall ensure that the bearers are prioritised in line with the operator preferences.
Impacted steps
In step 3 Forward Relocation request, the source MME shall prioritise the bearers (see KI4) and send those beyond 8 or using new optional IE(s) / GTPv2-C forward compatibility mechanism. The target MME will process this part only if it supports15 bearers, and the same is true for the target SGW step4.
In step 5 Handover Request, the source MME shall also prioritise the bearers/use new IEs on S1AP protocol for those above legacy limits. Note that the MME will learn from the Handover Request Ack whether the target eNB processed those in the extended bearer list.
In step 7, the target MME shall include the TEIDs in the Forward Relocation Response only for those bearers that both the SGW and the target eNB confirmed. The source MME thus learns which bearers have been dropped. Thus, it can and shall release those bearers towards the PGW that have not been handed over successfully – this will happen in new conditional steps added after the handover is completed/before the TAU procedure.
Note: There does not seem to be any option to pre-empt any bearers with backward compatible EBIs by releasing other bearers – so the KI4 cannot be really fulfilled.
There are multiple aspects that can be handled using forward compatibility capabilities in the GTP and S1AP protocols – these do not need to be covered in stage2 description. However, textual description should be added for releasing bearers that have not been handed over successfully.

## Slide 18: Impacted procedures : E-UTRAN to UTRAN Iu mode Inter RAT handover (with S4 SGSN) / preparation phase
Section 5.5.2.1.2 of TS 23.401
High level impact
Only up to 11 bearers can be sent over to SGSN.
Furthermore, during the HO, the target RNC may not acknowledge all bearers requested and these bearers shall be released. Note that this is not new for the support of 15 bearers – e.g. existing UTRAN implementations do not support secondary PDP contexts, so those are always released during HO to UTRAN.
Impacted steps
In step3, Forward Relocation Request, the MME shall send only up to 11 bearers to the SGSN – and only include those that have an EBI that can be converted to valid NSAPI values.
This shall be added to the text

## Slide 19: Impacted procedures : E-UTRAN to UTRAN Iu mode Inter RAT handover (with S4 SGSN) / execution phase
Section 5.5.2.1.3 of TS 23.401 needs to be updated
High level impact
See the previous slide
Impacted steps
After the successful completion of the HO, the MME shall release those bearers that have not been handed over. For this, it may use the MME initiated dedicated bearer deactivation and/or the MME requested PDN disconnection procedures.
This shall be added to the text

## Slide 20: Impacted procedures : E-UTRAN to GERAN A/Gb mode Inter RAT handover (with S4 SGSN) / preparation phase
Section 5.5.2.3.2 of TS 23.401 needs to be updated
For the impacts and impacted steps/required changes, refer to the Iu mode IRAT procedure on the previous slides

## Slide 21: Impacted procedures : E-UTRAN to GERAN A/Gb mode Inter RAT handover (with S4 SGSN) / execution phase
Section 5.5.2.3.3 of TS 23.401
For the high level impacts and impacted steps/required changes, refer to the Iu mode IRAT procedure on the previous slides

## Slide 22: Impacted procedures : MME to 3G SGSN combined hard handover and SRNS relocation procedure
Annex D / Section D.3.3 of TS 23.401
For the high level impacts and impacted steps/required changes, refer to the Iu mode IRAT procedure on earlier slides

## Slide 23: Impacted procedures : E-UTRAN to GERAN A/Gb mode Inter RAT handover (with Gn SGSN) / preparation phase
Annex D / section D.3.7.2 of TS 23.401
For the high level impacts and impacted steps/required changes, refer to the Iu mode IRAT procedure on earlier slides

## Slide 24: Impacted procedures : E-UTRAN to GERAN A/Gb mode Inter RAT handover (with Gn SGSN) / execution phase
Annex D / Section D.3.7.3 of TS 23.401 needs to be updated
For the high level impacts and impacted steps/required changes, refer to the Iu mode IRAT procedure on earlier slides

## Slide 25: Summary of procedure impacts and proposed changes /3 EPS session management procedures
 | Procedure | Relevant stage2 TS(s) / section(s) | See Slide # | High level impact | Conclusions
Session management | UE requested PDN connectivity | TS 23.401, section 5.10.2 | 26 | The bearer activation may succeed or fail depending on the capabilities of UE, eNB, MME, SGW and PGW support for 15 bearers As per KI4 (prioritise bearers based on QoS/ARP), the MME may re-attempt the setup of the bearer by pre-empting an existing bearer that has lower priority. The details of prioritisation should be left for implementation though. | Update the text to describe that the MME may pre-empt an existing bearer if needed, due to SGW/PGW not supporting 15 bearers.
 | Dedicated bearer activation | TS 23.401, section 5.4.1 | 27 | The MME shall attempt the bearer setup above 8 existing bearers only if the UE indicated its capability for supporting 15 bearers If the bearer setup is rejected by the eNB | 
 | UE requested bearer resource modification | TS 23.401, section 5.4.5 | 28 | See dedicated bearer activation (which is invoked) | No changes needed

## Slide 26: Impacted procedures : UE requested PDN connectivity
Section 5.10.2 of TS 23.401 needs to be updated
High level impact
The bearer activation may succeed or fail depending on the capabilities of UE, eNB, MME, SGW and PGW support for 15 bearers
As per KI4 (prioritise bearers based on QoS/ARP), the MME may re-attempt the setup of the bearer by pre-empting an existing bearer that has lower priority. The details of prioritisation should be left for implementation though.
Impacted steps
Step1: Note that the UE is not expected to send a PDN connectivity request that leads to more than 8 EPS bearers if the eNB has not confirmed at RRC setup that it supports 8 bearers. This is relevant as the bearer setup on S1AP is not expected to fail – other than for admission control reasons (i.e. cell load).
In step2, the MME allocates an EPS Bearer ID and may need to use one that is not backward compatible. In this case, it shall use forward compatibility of the GTPv2-C to indicate such EBI.
The SGW or PGW not supporting 15 bearers will still reject such request (of extended EBI) – in an alternative step ~3a/~5a.
In line with KI4, the MME may release an existing bearer with backward compatible EBI and re-allocate it to the current request/procedure.
The MME shall also use new IEs on S1AP for the extended E-RAB ID values, if needed in step 10 (Bearer setup req/PDN connectivity Accept).
The text should be updated to add that the MME may retry the bearer setup and pre-empt an existing bearer. This shall be optional.

## Slide 27: Impacted procedures : Dedicated bearer activation
Section 5.4.1 of TS 23.401 needs to be updated
High level impact
The bearer activation may succeed or fail depending on the capabilities of UE, eNB, MME, SGW and PGW support for 15 bearers
The MME shall reject the Create Bearer request if the UE has 8 bearers already and have not indicated support of 15 bearers.
The requirement KI4 (prioritise bearers based on QoS/ARP) can be met with pre-empting an existing bearer, but only if the SGW and PGW indicate support of 15 bearers.
Then, the MME may be able to pre-empt an existing bearer if the eNB does not support 15 bearers.
Impacted steps
In/before step4, the MME shall evaluate whether the request can be supported, based on the no. of existing bearers, and the indication for support of 15 bearers from the UE, SGW and PGW.
In step4, the MME may need to use extended EBI value and for that, it would use new/extended protocol IEs on S1AP.
In step7, the MME will receive a Bearer Setup Reject message if the eNB supports only 8 bearers. The MME then may decide to pre-empt an existing bearer, i.e. release it and re-allocate its EBI and re-send the Bearer Setup request to the eNB and Session management request to the UE.
The aspects of the MME evaluating the bearer setup in step4 and the option for pre-emption should be added to the text in TS23.401

## Slide 28: Impacted procedures : UE requested bearer resource modification
Section 5.4.5 of TS 23.401 needs to be updated
High level impact
See dedicated bearer activation (which is invoked)
Impacted steps
See dedicated bearer activation (which is invoked)
There is no need to update this section

## Slide 29: Summary of procedure impacts and proposed changes /4 Other procedures
Procedure | Relevant stage2 TS(s) / section(s) | See Slide # | High level impact | Conclusions for updating the stage2 TS
Emergency call setup | TS23.167, section 7.1.1 | - | The UE supporting 15 bearers has to make some assumption about the network’s capability when evaluating whether it has sufficient resources for the emergency call | The UE shall assume that the network only supports 8 bearers
Mobility from E-UTRAN to non-3GPP access | TS 23.402, section 8.1 (generic aspects for HO w/o optimisations for multiple PDNs) | - | There is no requirement to extend the capabilities for the max. no. of supported bearers on non-3GPP access – therefore, from Rel-15 onwards, not all EPS bearers may be handed over successfully, even if the non-3GPP access type supports up to 8 bearers. | The text should be extended to clarify that the number of bearers that can be handed over from E-UTRAN may depend on the access type, but 15 EPS bearers are not expected to be supported, so HO to non-3GPP access may lead to release all bearers above 8.