## Slide 1: Summary of slicing interworking drafting session
(Qualcomm)

## Slide 2: Outline
Issue 1: AMF selection, how AMF learns S-NSSAIs/PDU session IDs for PDN connections active in EPC and V-SMF selection during EPC->5GC mobility
Issue 2: Support of multiple PDU sessions to same DNN and different S-NSSAIs for EPC-5GC interworking

## Slide 3: Issue 1
AMF selection, how AMF learns S-NSSAIs/PDU session IDs for PDN connections active in EPC and V-SMF selection during EPC->5GC mobility

## Slide 4: Option 1a: Partial solution for slicing interworking in Rel-15; complete solution may be added in Rel-16
Rel-15
Idle mode
UE to include
  S-NSSAIs (with values for the Serving PLMN of the target 5GS) in Requested NSSAI in AS and NAS (if available)
  <PDU Session ID, associated S-NSSAI, PLMN ID (from which S-NSSAI was received), default EBI> for PDN connections active in EPC in Registration Request
AMF selected taking also S-NSSAIs of UE’s PDN connections into account (by RAN based on Requested NSSAI in AS or as part of re-allocation procedure)
AMF uses EBIs to correlate PDU Session IDs/S-NSSAIs with PDN contexts received via N26
AMF to select V-SMFs taking S-NSSAIs into account
Connected mode
MME selects AMF (S-NSSAIs of UE’s PDN connections not taken into account)
AMF selects default V-SMFs
AMF learns PDU Session ID and S-NSSAI for PDN connections moved from H-SMF
Rel-16: potential enhancements (*)
Connected mode
AMF selection taking S-NSSAIs of UE’s PDN connections into account
AMF to select V-SMFs taking S-NSSAIs of UE’s PDN connections into account
Assumption: Connected mode enhancements do not have UE impacts
(*) subject to input contributions; just listed as a potential option

## Slide 5: Option 1b Partial solution for slicing interworking in Rel-15;
Rel-15
Idle mode
AMF selected taking also S-NSSAIs of UE’s PDN connections into account
AMF uses F-TEIDs received via N26 to find the SMF address and S-NSSAI
AMF to select V-SMFs taking S-NSSAIs into account
AMF to select the H-SMF based on the F-TEID
Connected mode
MME selects AMF (S-NSSAIs of UE’s PDN connections not taken into account)
AMF uses F-TEIDs received via N26 to find the SMF address and S-NSSAI
AMF to select V-SMFs taking S-NSSAIs into account
AMF to select the H-SMF based on the F-TEID
AMF learns PDU Session ID and S-NSSAI for PDN connections moved from H-SMF
Rel-16: potential enhancements (*)
Connected mode
AMF selection taking S-NSSAIs of UE’s PDN connections into account
AMF to select V-SMFs taking S-NSSAIs of UE’s PDN connections into account
Assumption: Connected mode enhancements do not have UE impacts
(*) subject to input contributions; just listed as a potential option

## Slide 6: Option 2: Basic support for slicing interworking in Rel-15; complete solution may be added in Rel-16
Rel-15
Idle mode
AMF selects default V-SMFs
AMF learns PDU Session ID and S-NSSAI for PDN connections moved from H-SMF
Connected mode
MME selects AMF (S-NSSAIs of UE’s PDN connections not taken into account)
AMF selects default V-SMFs
AMF learns PDU Session ID and S-NSSAI for PDN connections moved from H-SMF
Rel-16: potential enhancements (*)
Idle mode
UE to include
  S-NSSAIs (with values for the Serving PLMN of the target 5GS) in Requested NSSAI in AS and NAS
  <PDU Session ID, associated S-NSSAI, PLMN ID (from which S-NSSAI was received), default EBI> for PDN connections active in EPC in Registration Request
AMF selected taking also S-NSSAIs of UE’s PDN connections into account
AMF uses EBIs to correlate PDU Session IDs/S-NSSAIs with PDN contexts received via N26
AMF to select V-SMFs taking S-NSSAIs into account
Connected mode
AMF selection taking S-NSSAIs of UE’s PDN connections into account
AMF to select V-SMFs taking S-NSSAIs of UE’s PDN connections into account
(*) subject to input contributions; just listed as a potential option

## Slide 7: Way forward
Option 1a: Huawei, Ericsson (2)
Option 2: ZTE, Nokia, Cisco, Intel, NTT DoCoMo, Qualcomm (6)
Tentative way forward: Option 2
  Related CRs are in S2-171541 and S2-171542.

## Slide 8: Issue 2
Support of multiple PDU sessions to same DNN and different S-NSSAIs for EPC-5GC interworking

## Slide 9: Proposals
S2-181665 (Huawei): PDU session with same DNN but different S-NSSAIs expected to be served by different APNs (no details on how to achieve this given in the paper)
S2-182007 (Qualcomm): Assume DNNs to be unique across all the S-NSSAIs that the UE is subscribed to, thus no need for additional information or mapping; DNN used in 5GC equal to APN used in EPC for the same data network
S2-181717 (NTT DoCoMo): Separate SMF address from PGW-C address; allow for multiple SMFs but one PGW-C to handle multiple PDU sessions/PDN connections to same DNN/APN and different S-NSSAIs in 5GC and EPC, respectively

## Slide 10: Issues to be discussed
Assume DNNs to be unique across all the S-NSSAIs that the UE is subscribed to?
If not and UE has more than one active PDU session to same DNN but different S-NSSAIs, move all or just one PDU session from 5GC to EPC?
If we decide to move more than one PDU session:
  whether/how to perform APN-AMBR enforcement if those sessions were handled by different SMFs (i.e. different PGW-C in EPC)?
  MME is supposed to select same PGW-C for same APN, e.g. if UE establishes another PDN connection to same APN/DNN? Which PGW-C should MME choose?
  User experience impact: Applications requiring PDU session towards specific S-NSSAI and DNN combination will work when activated in 5GC and will continue to work in EPC; however when application is activated in EPC there is no way to establish the PDN connection towards a specific S-NSSAI. This asymmetry may be confusing.

## Slide 11: Status and way forward
Initial discussions on questions 1 (“Assume DNNs to be unique across all the S-NSSAIs that a UE is subscribed to?”)
  Multiple companies indicated preference to not make this assumption.
Due to lack of time the remaining questions and issues could not be addressed
The issues listed on the previous slide need to be revisited in the next meeting.