## Slide 1
Qualcomm Incorporated
Discussion on use and configuration of Configured NSSAI
© 3GPP 2018 SA2-184944 TSG SA2#127bis Newport Beach, USA, May 28 – June 1

## Slide 2: Background
Release 15 slicing has defined:
  Configured NSSAI for HPLMN
  Configured NSSAI for (V)PLMN
  Sort of defines the Configured NSSAI for all PLMNs for which there is no dedicated C-NSSAI
    “Configured NSSAI that is not associated to any PLMN” is the term adopted by CT1 which has a more explicit definition of it
In eDECOR, the HPLMN is capable of preconfiguring (default) values of DCN ID in the UE
  Values can be configured in USIM or in the ME

## Slide 3: Background
The current assumption in Rel. 15 in SA2 is that values configured by the HPLMN (not upon registration procedures or update procedures) are “magically” configured in the UE via implementation dependent mechanism
  No specific mechanism is defined (and OMA DM is not available)
  Not even the (pre) configuration in USIM is considered
Therefore, there is no way EVER to modify such “pre-configured” values from the HPLMN

## Slide 4: Configured NSSAI Who should define and configured them?
UE provisioned with Configured NSSAI
  Configured NSSAI for HPLMN  configured by HPLMN
  Configured NSSAI for (V)PLMN  pre-configured by HPLMN also
    Rel. 15 stage 3 assumes this is possible, stage 2 has no mention of that
  Configured NSSAI that is not associated to any PLMN  configured by HPLMN
Shall the HPLMN be enabled to updated the configured NSSAIs defined by the UE? Yes, it simplifies roaming and provides the HPLMN stronger control
  At present any pre-configured Configured NSSAI for the HPLMN cannot be modified
  At present, there is no mechanism to modify the Configured NSSAI that is not associated to any PLMN

## Slide 5: Update to Configured NSSAI
Configured NSSAI that is not associated to any PLMN
  Must be defined by HPLMN
  Should not be modifiable by VPLMN
  Observation 1: HPLMN must be able to update it in the UE
  Observation 2: nothing is defined about updating such configuration in the UE
Configured NSSAI for the HPLMN
  Must be defined by the HPLMN
  Should not be modifiable by VPLMN
  Used by the UE when connecting to HPLMN, obsolete value requires inefficient procedures when UE “returns” home
  Observation 3: HPLMN must be able to update it in the UE
  At present 501 enables update of C-NSSAI for HPLMN only when the UE in in HPLMN
    “If the HPLMN performs the configuration update of a UE registered in the HPLMN (e.g. due to a change in the Subscribed S-NSSAI(s)), this results in updates to the Configured NSSAI for the HPLMN. Updates to the Allowed NSSAI and/or, if present, to the associated mapping of the Allowed NSSAI to the Configured NSSAI for the HPLMN are also possible if the configuration update affects S-NSSAI(s) in the current Allowed NSSAI.”

## Slide 6: Update to Configured NSSAI
Configured NSSAI for VPLMN
  VPLMN can provide the VPLMN defined value to the UE in NAS procedures, no need to modify this
  However, Rel. 15 stage 3 assumes that pre-configuration of such value by the HPLMN is possible (to align functionality to eDECOR), stage 2 has no mention of that
  Observation 4: stage 2 should align to stage 3

## Slide 7: Use of Configured NSSAI for Serving PLMN
A UE registering to a Serving PLMN for which it has no Configured NSSAI and no Allowed NSSAI, based on the current specifications, cannot provide any Requested NSSAI:
  “The Requested NSSAI shall be one of:
    - the Configured-NSSAI, or a subset thereof as described below, e.g. if the UE has no Allowed NSSAI for the serving PLMN; or
    - the Allowed-NSSAI for the Access Type over which the Requested NSSAI is sent, or a subset thereof and Access Type; or
    - the Allowed-NSSAI for the Access Type over which the Requested NSSAI is sent, or a subset thereof, plus one or more S-NSSAIs from the Configured-NSSAI as described below.
  The subset of Configured-NSSAI provided in the Requested NSSAI consists of one or more S-NSSAI(s) in the Configured NSSAI applicable to this PLMN, for which no corresponding S-NSSAI is present in the Allowed NSSAI. ”
UE would provide no Requested NSSAI, and AMF/NSSF would determine a Configured NSSAI for the VPLMN and provide it to the UE.
  The procedure requires a registration to be followed by a re-registration
However, why can’t the Configured NSSAI that is not associated to any PLMN be used?
  At present, it is not clear that such value can be used

## Slide 8: What is missing
Update of Configured NSSAI for HPLMN:
  New value must be provided to AMF: already possible
  New value must be provided to the UE: missing
Update of Configured NSSAI all PLMNs for which there is no dedicated Configured NSSAI:
  New value must be provided to the UE
Enable the HPLMN to provide and update pre-configured value of Configured NSSAI for VPLMN
  Similar to eDECOR mechanism and preconfiguration of DCN ID
Observation 5: we are missing a mechanism to deliver the two Configured NSSAIs to the UE

## Slide 9: Proposal
Clarify that the Configured NSSAI used for creating the Request NSSAI may be the Configured NSSAI that is not associated to any PLMN configured by the HPLMN
Clarify the use of Configured NSSAI for VPLMN in TS 23.501 may be the one provided to UE by HPLMN (default/preconfigured value)
Enable the delivery of the Configured NSSAIs from HPLMN to the UE via policy mechanisms
  Intent is to change the preconfigured values in ME, does not apply to any pre-configured values that may be stored in the USIM.
  NOTE: if the preconfigured value for a PLMN is changed, UE needs to delete everything it has for that PLMN
  Values are optional elements in the UE policy