## Slide 1: NSSAI handling in Access Stratum
SA2#127-bis May 28 – June 1 Newport Beach, USA Tdoc S2-185834

## Slide 2: Access stratum NSSAI handling: UE aspects
The AS uses the NSSAI in the Connection establishment procedure to trigger upfront C-Plane policies in the (R)AN before the CN provides the NG-RAN with the Allowed NSSAI.
  One example is the Overload control procedure.
TS 23.501 is already covering this principle: see clause 5.15.2.1 General
  “The (R)AN may use Requested NSSAI in access stratum signalling to handle the UE Control Plane connection before the 5GC informs the (R)AN of the Allowed NSSAI. “
The above is current text in TS

## Slide 3: Access stratum NSSAI handling: UE aspects
Some more work is required:
  For AS Connection Establishment triggered by a Registration procedure, the Requested NSSAI is formed as documented in clause 5.15.5.2.1 (which documents Registration procedures and slicing). No additional text required. In the current text, the Requested NSSAI is the Allowed NSSAI unless a slice set change is required by the UE.
  For Service Request, the RAN needs to know the Allowed NSSAI Upfront at RRC connection establishment (e.g. to trigger OLOAD control action or to locally manage to load).
    We need to clarify the Allowed NSSAI the UE stores is sent in RRC connection establishment triggered by Service Request.
      Very simple logic
      No need to compute anything, just include the stored Allowed NSSAI in RRC connection establishment procedure message 5.
      Ericsson: Principle of using Allowed against already used principles in the system like Establishment cause. Again, what type of slicing information RAN needs and how RAN uses it is up to RAN to decide and to specify.
Text wise we may specify that the Requested NSSAI is included in all RRC connection establishment procedures, if available, and when the UE is registered it is set to the Allowed NSSAI in all procedures except registrations that trigger a Slice Set change.
  Implement this by CRs at this meeting. (based on S2-185444 revision and S2-185317)
Majority of companies oriented to include the Requested (= allowed NSSAI) NSSAI also in the RRC connection request for SR. This to be added to Kundan’s LS s2-185832

## Slide 4: Access stratum NSSAI handling: network aspects – RAN awareness of Allowed NSSAI
TS 23.501 is already covering this principle: see clause 5.15.2.1 General
“When a UE is successfully registered over an Access Type, the CN informs the (R)AN by providing the Allowed NSSAI for the corresponding Access Type.”
  Proposal: Implement this RAN awareness of allowed NSSAI also in TS 23.502 and proceed with agreeing related CRs at this meeting (based on S2-185317)
Update 23.502 TS based on revision S2-185317 -> S2-186074

## Slide 5: Access stratum NSSAI handling: network aspects – MT procedures
For MT procedures: the Paging request from the AMF so far does not provide the RAN with information on what slices the UE is allowed to use.
Certain slices may be subject to congestion management in the RAN, but for MT procedures requiring paging the UE the RAN cannot evaluate if it is pointless to page the UE (e.g. because the related SR may lead to a release of the RRC connection as the RAN temporarily is not providing c-plane resources to certain UEs that only are allowed to use certain slices)
Proposal: to make RAN aware of slices the UE is allowed to use also at time of paging, include the Allowed NSSAI in the N2 message carrying the Paging Request to the RAN.
LS to RAN WGs to ask them what they think of this . This to be added to Kundan’s LS s2-185832

## Slide 6: RFSP handling
The Subscribed RFSP ID already takes into account the S-NSSAIs the UE subscribes to. State this in RRM clause of 23.501.
The serving PLMN CN works RFSP ID out based on subscribed RFSP-ID and other local policies in Serving PLMN AMF and if offload of policies in PCF (allowed NSSAI may be considered also in AMF and PCF). State this in RRM clause of 23.501. update procedures in 23.502. remove example of polices that PCF may use in 23.503.
The AMF sends RFSP-ID to RAN. State this in RRM clause of 23.501 and update procedures as applicable.
The RAN gets the RFSP ID from CN and determines the camping policy (RF selection priority in RRC_IDLE mode priorities and control inter-RAT/inter frequency handover in RRC_CONNECTED mode) based on operator policies which may also take the Allowed NSSAI and the related slices local information (e.g. load status) in RAN into account.
Proceed with above and use CR S2-185828 as the basis