## Slide 1: EPS SPID/RFSP extension TEI-16 Proposal
Source: Vodafone, Verizon, Telstra, Telecom Italia, Ericsson
SA WG2 Meeting #129bis November 26 - 30, 2018, West Palm Beach, USA
Agenda item: 7.1
Tdoc S2-1812020

## Slide 2: Use case: Prioritise capacity for a specific enterprise on a specific macro cell
Cell A
Cell B
Enterprise 1
Enterprise 2
Cell A RRM:
  Enterprise 1’s employees get priority access to X% (but not all) of Cell A resources.
  Handle Enterprise 2 employees and other users with default behaviour
  Cell B RRM:
  Enterprise 2’s employees get priority access to Y% (but not all) of Cell B resources.
  Handle Enterprise 1 employees and other users with default behaviour

## Slide 3: Additional Description
This is not a ‘closed access’ cell that is reserved exclusively for the use of an enterprise
Some similarity to a WiFi Access Point that has two SSIDs, one for private use and one for public use.
Cell A is configured with knowledge that it needs to give special treatment to Enterprise 1’s users.
  Requires cell A to know whether the UE belongs to ‘enterprise 1’
  For non-enterprise users, or, users from other enterprise groups <> 1, default behavior is applied. Some resources are reserved for them in order to ensure coverage.
The RRM strategy of the cells is operator/implementation specific.
  However, as indicated in the WID, RP-151827 “RAN Aspects of RAN Sharing Enhancements for LTE”, existing eNBs are able to share load between the sharing PLMNs’ customers (“Sharing is normally based on agreed quota or share ratio.“)
  In a non-shared PLMN, or a PLMN with few sharing partners, this eNB functionality could be re-purposed to serve a “Matching Enterprise user group” and a “Default user group”
Cell A generates separate counters/statistics for ‘enterprise 1’ and ‘other’ users -> enables any Service Level Agreement to be monitored.

## Slide 4: No current tools available to solve this
Current QoS information is ‘abstract’ and relates primarily to that UE, rather than the “set of UEs used by the enterprise’s employees”
RAN does not know the ‘group’ of the UE
RAN does not have visibility of the IMSI
There are too many enterprises to allocate different IMSI ranges to different enterprises.
APN is not visible to the RAN
Access Class Barring only applies to idle mode. Also, Access Classes need to be randomly allocated to devices – so all ‘groups’ are likely to have an equal proportion of devices in each Access Class.
“Low Access Priority” does not help as LAPI devices should not be rejected if their group’s load is within the eNB’s quota for that group.
SPID/RFSP has only 256 values. This can identify that the UE is an Enterprise subscriber but NOT WHICH ENTERPRISE
  there are insufficient values to identify different the enterprises within a PLMN (or MME area, or even a Tracking Area)
Use of 5GCore -> enterprise provided (or ‘bring your own’) devices are frequently not leading edge devices – e.g. they may well not be 5GCore capable devices

## Slide 5: Proposed solution: Extend SPID/RFSP
Add a 32 bit, optional, extension to the 'Index to RAT/Frequency Selection Priority' (RFSP Index) so that e.g. individual enterprises can be differentiated from each other.
Rationale:
The SPID/RFSP mechanism was specified in 3GPP Release 8
The standardised values in Annex I of TS 36.300, and e.g. the LS from GSMA in S2-178308 ,imply that it is at least somewhat implemented, rather than being an unimplemented or “yet to be implemented” feature.
RFSP functionality specified in clause 4.3.6 of TS 23.401 allows visited network policy to be applied to the RFSP Index of Roaming subscriber.
Existing MME, S1 interface, and E-UTRAN behavior provides the ability to handle a mix of supporting and non-supporting entities smoothly.
Why 32 bit extension?
  gives sufficient codespace for identification of an enterprise (16 bits is insufficient; 24 bits is borderline for large PLMN)
  CT4’s Diameter and GTP-C specifications seem to use 32 bit parameters
  if desired, could allow 1:1 mapping with a 5GCore NSSAI parameter.

## Slide 6: Alternative potential solutions:
UE Usage Type (c.f. R13 DECOR)
  This is only 8 bits long
  Not sent to RAN, nor transferred on X2
  As not sent to RAN, no concept of VPLMN policing the value from HPLMN specified As NB-IoT MME selection can be “RAT based”, probably less widely implemented than RFSP Index
DCN ID (c.f. R14 eDECOR)
  16 bits long (as indicated by NG-RAN’s use of 24 bit TACodes, 16 bits are really not sufficient for simple allocation to large numbers of different enterprises)
  Intended for very different purpose (i.e. MME selection at PLMN change)
New parameter
  Slower rollout than with existing concept
“Full 5GCore Slicing”
  Unnecessary complexity for EPC
 SPID/RFSP extension is sufficient

## Slide 7: Specification Impacts of SPID/RFSP
Stage 2: TS 23.401
  Potentially no change needed in 4.3.6
  However, probably useful to describe the added field, and update the HSS and MME storage tables
  Existing ‘fallback’ mechanisms support partial rollout in core or RAN:
  “…The MME stores the subscribed RFSP Index value received from the HSS and the RFSP Index value in use. During the Tracking Area Update procedure, the MME may update the RFSP Index value in use (e.g. the MME may need to update the RFSP Index value in use if the UE related context information in the MME has changed)…”
Interworking with 5GCore Depends whether RFSP extension is desired in 5GCore
  Can reuse S10 (= N26) functionality
  TS 23.501 clause 5.3.4.3 is close copy of clause 4.3.6 of TS 23.401.
CT 4 specifications:
  29.272 Diameter, add RFSP extension to the Subscription-Data AVP (which carries the existing RAT-Frequency-Selection-Priority-ID)
  29.274 GTP-C, add the ‘subscribed’ and ‘in use’ RFSP extension to Forward Relocation Request and Context Response messages (which carry the existing RFSP Index parameters)
RAN 3 specifications
  36.413 S1 AP, add “RFSP extension” to messages carrying Subscriber Profile ID for RAT/Frequency priority
  36.423 X2 AP: as S1-AP
  36.300 potentially add new “well known” value for Enterprise

## Slide 8: Proposals
Agree to draft TEI-16 EPC CRs for this functionality.
Decide now whether or not to replicate in 5GCore.
Allocate 0.5 TU in SA2 for this work.
Report to SA/RAN/CT on the need for limited stage 3 work.