## Slide 1
Coexistence of the AS security and slice information in the RAN during the RRC connection establishment procedure.
SA WG2 Meeting #129-Bis S2-1812156
26 – 30 November 2018, West Palm Beach, USA

## Slide 2
Requirements
Requirements:
  S-NSSAI shall be send encrypted in the AS and NAS (SA1 guidance [1]).
  S-NSSAI(s) is required during the RRC connection establishment to perform slice related overload control at NG-RAN.
  S-NSSAI(s) is required during the RRC connection establishment for following RAN related function:
    To check slice availability:
      A slice may not be deployed homogeneously in the network. Therefore a NG-RAN needs slice information to check if the slice is available at the location.  See 38.413 Slice Support List IE in the NG setup response message.

## Slide 3
Requirements
    Resource management between slices
      NG-RAN supports policy enforcement between slices as per service level agreements. It should be possible for a single NG-RAN node to support multiple slices. The NG-RAN should be free to apply the best RRM policy for the SLA in place to each supported slice.
    Resource isolation between slices
      the NG-RAN supports resource isolation between slices. NG-RAN resource isolation may be achieved by means of RRM policies and protection mechanisms that should avoid that shortage of shared resources in one slice breaks the service level agreement for another slice. It should be possible to fully dedicate NG-RAN resources to a certain slice. How NG-RAN supports resource isolation is implementation dependent.
    Optimal AMF selection procedure
      S-NSSAI(s) are required at the NG_RAN to perform optimal AMF selection at NG-RAN.

## Slide 4
Current Status of Slice availability during RRC connection establishment:
Following alternative solutions are proposed to achieve slice confidentiality at AS layer
S2-1811403: don’t send a S-NSSAI during the RRC connection procedure
S2-1811565: send S-NSSAI in clear text if HPLMN and VPLMN agrees for this otherwise don’t send a S- NSSAI during the RRC connection establishment.
SA3 Guidance regarding selecting one of the two above proposal in SA3 LS Response (S3-183659):
SA3 sends an LS response requesting the SA2 to choose on of the above solution which is most suitable
for the Rel15 5GS.

## Slide 5
Observations
Observation 1: None of the solutions provides slice confidentiality at the AS layer during the RRC connection establishment.
Observation 2: Slice information (S-NSSAI(s)) are required at the NG-RAN for the various purposes described in the requirement section of the presentation.

## Slide 6
Further analysis on this issue
To achieve the coexistence of the AS security and slice information in the RAN during the RRC connection establishment, following three possible solutions can be considered.
Solution 1: Encrypted S-NSSAI(s) shall be sent to NG-RAN after the RRC connection procedure.
Solution 2: Encrypted S-NSSAI(s) shall be sent to NG-RAN during the RRC connection procedure
Solution 3: Encrypted S-NSSAI(s) shall be sent to NG-RAN only if the NG-RAN maintains the AS security context

## Slide 7
Solution: Solution 1a
NG-RAN fetches AS security contexts from the AMF after the RRC connection establishment and provides it to the UE to encrypt a S-NSSAI(s) and send encrypted S-NSSAI(s) in next RRC message.

## Slide 8
Solution: Solution 1b
The UE and is provided with a AS security context during the registration procedure. The UE uses this security context to encrypt. The NG-RAN sends encrypted S-NSSAI to the AMF to decrypt it.

## Slide 9
Solution: Solution 2
The NG-RAN fetches the security context from the registered AMF during the RRC connection establishment.

## Slide 10
Solution: Solution 3
The UE and NG-RAN are provided with a AS security context during the registration procedure. The UE and the NG-RAN uses this security context to encrypt and decrypt S-NSSAI(s).

## Slide 11
Conclusions
In Release 15, SA2 should make a decision as guided by the SA3 LS Response (S3-183659).
In Release 16, it is proposed to work on providing slice privacy during RRC connection procedure by taking one of the solution listed in the discussion paper as baseline for Rel-16 TEI with coordination with RAN2 and SA3.

## Slide 12
References
[1] LS from SA: SP-180914 “Guidance on initial NAS message protection”
[2] LS from RAN2: R2-1816022 “Reply LS on initial NAS security agreements”
[3] LS from SA2: S2-1811568 “Reply LS on initial NAS security agreements”