## Slide 1
Handling of slice based overload control at NG-RAN
SA WG2 Meeting #129-Bis S2-1812158
26 – 30 November 2018, West Palm Beach, USA

## Slide 2
Rel-15 UE and Network behaviour
    An AMF invokes Slice based overload control at NG-RAN by sending Start Overload message containing a congested S-NSSAI(s).
    When a NG-RAN receives Requested NSAAI during the RRC connection establishment procedure and the requested NSSAI are indicated as congested by the AMF then the NG-RAN sends a GENERIC wait time in the RRC connection release to the UE.
    When the UE receives GENERIC wait time in the RRC connection Release message it will not send any AS and NAS signalling till the wait time expires. This procedure may block ALL services unnecessary at the UE.

## Slide 3
  When the AMF requests NG-RAN to perform overload control for one service/Slice (S-NSAAI) then the NG-RAN will send generic wait time to the UE. As a result all the other services (essential services e.g. V2X) at the UE are blocked till the generic wait time expires. This will create bad user experience.
  e.g. when a UE requires IoT and eMBB services and IoT related slice is congested then this mechanism block eMBB services as well. This will become more critical when some essential services will be blocked (e.g. V2X).
Drawback of the Rel-15 UE and Network behaviour

## Slide 4
    It is proposed in Rel-16 to introduce a better mechanism to handle the slice based overload control at a NG-RAN and an UE e.g. sending wait timer per slice based.
    This scenario can be part of TEI16 or eNS.
Proposal