## Slide 1: Discussion on Always-on PDU Session
3GPP TSG-SA WG2 Meeting #129bis
West Palm Beach, USA, 26 - 30 November, 2018
Source: LG Electronics
Title: Discussion on Always-on PDU Session
Document for: Discussion
Agenda Item: 6.5.7 3GPP access specific functionality and flows
Work Item / Release: 5GS_Ph1 / Rel-15
S2-1812159
LG Electronics

## Slide 2: Background
Always-on PDU Session
  S2-1811571 was agreed in SA2#129 to align with CT1 specification.
    “An always-on PDU Session is a PDU Session for which User Plane resources have to be activated during every transition from CM-IDLE mode to CM-CONNECTED state.”
  The basic assumption of always-on PDU Session is that the 5GS is not allowed to run multiple Service Request procedures in parallel.
List Of PDU Sessions To Be Activated
  S2-188734 was agreed in SA2#128bis which clarifies that
    When the UE includes the List Of PDU Sessions To Be Activated, the UE shall indicate PDU Sessions only associated with the access the request message (i.e. Registration and Service Request) is related to.
    The intention of this CR was to reduce unnecessary paging.
      For example, when a UE in CM-IDLE in 3GPP and non-3GPP, the UE may initiate Service Request over non-3GPP access when the UE moves into the WLAN coverage. If the UE is allowed to include a 3GPP PDU Session in the List Of PDU Sessions To Be Activated, the network shall page the UE to activate the PDU Session.
Issues
  Is it possible to deactivate Always-on PDU Session by the SMF?
  Is Always-on PDU Session applicable both 3GPP and non-3GPP access?
  What is the UE behavior when the UE has Always-on PDU Session in one access (e.g. 3GPP access) but the UE is tries to send Service Request over the other access (e.g. non-3GPP access)?

## Slide 3: Proposal
The SMF does not deactivate Always-on PDU Session
  Always-on PDU Session is introduced for low latency services
    If SMF deactivates Always-on PDU Session due to data inactivity, latency is increased due to user plane setup procedure
  If deactivation is allowed, the UE need to request activation whenever the UE sends Registration and Service Request.
    The SMF may deactivate Always-on PDU Session again due to data inactivity
    Such activation and deactivation increases signaling in the network
Always-on PDU Session is not supported in non-3GPP access
  Always-on PDU Session is introduced for low latency services
  However, in Rel-15, it is hard to support low latency service in non-3GPP access because
    QoS of non-3GPP access (e.g. WLAN) is not controlled by the 5GC
    If UE is in CM-IDLE (e.g. out of WLAN coverage), the UE cannot use non-3GPP access
When the UE initiates Registration or Service Request over non-3GPP access, the UE does not request to activate Always-on PDU Session of 3GPP access
  Even if the UE request to activate Always-on PDU Session of 3GPP access, it is not possible because there is on-going Service Request procedure over non-3GPP access. It can be activated only after on-going Service Request procedure is terminated.
CR in S2-18XXXXX