## Slide 1: Discussion on AMF awareness of “N2 SM information” type
3GPP TSG-SA WG2 Meeting #129bis
West Palm Beach, USA, 26 - 30 November, 2018
Source: LG Electronics
Title: Discussion on AMF awareness of “N2 SM information” type
Document for: Discussion
Agenda Item: 6.5.3 Session management and continuity functions and flows
Work Item / Release: 5GS_Ph1 / Rel-15
S2-1812169
LG Electronics

## Slide 2: Transfer of N2 SM information from SMF to AMF
According to TS 23.502
  Namf_Communication_N1N2MessageTransfer service operation
  Nsmf_PDUSession_UpdateSMContext service operation
  AMF handles N2 SM information as a container, i.e. does not know type of N2 Message (e.g. PDU Session Establishment, PDU Session Modification, PDU Session Release)

## Slide 3: Transfer of N2 SM information from AMF to NG-RAN
According to TS 38.413
  PDU Session Establishment
  PDU Session Release
  PDU Session Modification
  AMF knows type of N2 SM information and send different messages to the RAN

## Slide 4: Transfer of N2 SM information from SMF to AMF
According to TS 29.502
  Update SM Context service operation
  AMF knows type of N2 SM information based on “n2SmInfoType”
Attribute name | Data type | P | Cardinality
upCnxState | UpCnxState | C | 0..1
hoState | HoState | C | 0..1
releaseEbiList | array(EpsBearerId) | C | 0..N
allocatedEbiList | array(EbiArpMapping) | C | 0..N
modifiedEbiList | array(EbiArpMapping) | C | 0..N
n1SmMsg | RefToBinaryData | C | 0..1
n2SmInfo | RefToBinaryData | C | 0..1
n2SmInfoType | N2SmInfoType | C | 0..1
epsBearerSetup | array(EpsBearerContainer) | C | 0..N
dataForwarding | boolean | C | 0..1
Enumeration value | Description
"PDU_RES_SETUP_REQ" | PDU Session Resource Setup Request Transfer
"PDU_RES_SETUP_RSP" | PDU Session Resource Setup Response Transfer
"PDU_RES_SETUP_FAIL" | PDU Session Resource Setup Unsuccessful Transfer
"PDU_RES_REL_CMD" | PDU Session Resource Release Command Transfer
"PDU_RES_REL_RSP" | PDU Session Resource Release Response Transfer
"PDU_RES_MOD_REQ" | PDU Session Resource Modify Request Transfer
"PDU_RES_MOD_RSP" | PDU Session Resource Modify Response Transfer
"PDU_RES_MOD_FAIL" | PDU Session Resource Modify Unsuccessful Transfer
"PDU_RES_NTY" | PDU Session Resource Notify Transfer
"PDU_RES_NTY_REL" | PDU Session Resource Notify Released Transfer
"PDU_RES_MOD_IND" | PDU Session Resource Modify Indication Transfer
"PDU_RES_MOD_CFM" | PDU Session Resource Modify Confirm Transfer
"PATH_SWITCH_REQ" | Path Switch Request Transfer
"PATH_SWITCH_SETUP_FAIL" | Path Switch Request Setup Failed Transfer
"PATH_SWITCH_REQ_ACK" | Path Switch Request Acknowledge Transfer
"PATH_SWITCH_REQ_FAIL" | Path Switch Request Unsuccessful Transfer
"HANDOVER_REQUIRED" | Handover Required Transfer
"HANDOVER_CMD" | Handover Command Transfer
"HANDOVER_PREP_FAIL" | Handover Preparation Unsuccessful Transfer
"HANDOVER_REQ_ACK" | Handover Request Acknowledge Transfer
"HANDOVER_RES_ALLOC_FAIL" | Handover Resource Allocation Unsuccessful Transfer
Table 6.1.6.3.12-1: Enumeration N2SmInfoType
Table 6.1.6.2.5-1: Definition of type SmContextUpdatedData

## Slide 5: Transfer of N2 SM information from SMF to AMF
According to TS 29.518
  N1N2MessageTransfer
  AMF handles N2 SM information as a container, i.e. does not know type of N2 Message (e.g. PDU Session Establishment, PDU Session Modification, PDU Session Release)
Attribute name | Data type | P | Cardinality
n1MessageContainer | N1MessageContainer | C | 0..1
n2InfoContainer | N2InfoContainer | C | 0..1
skipInd | boolean | C | 0..1
lastMsgIndication | boolean | O | 0..1
sessionId | string | O | 0..1
ppi | Ppi | O | 0..1
arp | Arp | O | 0..1
5qi | 5Qi | O | 0..1
n1n2FailureTxfNotifURI | Uri | O | 0..1
supportedFeatures | SupportedFeatures | C | 0..1
Table 6.1.6.2.18-1: Definition of type N1N2MessageTransferReqData
Attribute name | Data type | P | Cardinality
n2InformationClass | N2InformationClass | M | 1
smInfo | N2SmInformation | C | 0..1
nrppaInfo | NrppaInformation | C | 0..1
pwsInfo | PwsInformation | C | 0..1
areaOfValidity | AreaOfValidity | O | 0..1
Table 6.1.6.2.15-1: Definition of type N2InfoContainer
Enumeration value | Description
"SM" | N2 SM information.
"NRPPa" | N2 NRPPa information.
"PWS" | N2 PWS information of PWS type.
"PWS-BCAL" | N2 Broadcast Completed Area List or the Broadcast Cancelled Area List.
"PWS-RF" | N2 Restart Indication or Failure Indication
Table 6.1.6.3.4-1: Enumeration N2InformationClass
Attribute name | Data type | P | Cardinality
pduSessionId | PduSessionId | M | 1
n2InfoContent | N2InfoContent | C | 0..1
nasPdu | N1MessageContainer | C | 0..1
sNssai | Snssai | C | 0..1
subjectToHo | boolean | C | 0..1
Table 6.1.6.2.26-1: Definition of type N2SmInformation

## Slide 6: Observation
Different assumptions in each specification and group
  In TS 38.413, AMF knows type of “N2 information”
  In Update SM Context service, AMF knows type of “N2 information”
  In N1N2MessageTransfer service, AMF does not know type of “N2 information”
  Based on overall observation, currently
    In case of PDU Session Establishment
      AMF does not know type of “N2 information”
    In case of PDU Session Modification
      UE requested case
        AMF knows type of “N2 information” based on “n2SmInfoType”
      Network requested case
        AMF does not know type of “N2 information”
    In case of PDU Session Release
      UE requested case
        AMF knows type of “N2 information” based on “n2SmInfoType”
      Network requested case
        AMF does not know type of “N2 information”
  Need to align specifications

## Slide 7: Proposals
It is not clear why stage-3 assumes that AMF need to know type of “N2 information”
  Send LS to RAN3 and CT4 to ask their assumptions
  Draft in S2-18XXXXX
  Based on feedback, choose one of options
    Option 2: AMF knows type of “N2 information”
      Need to update “N1N2MessageTransfer” service in TS 29.518
      Need to update TS 23.502
        Add N2 SM information type in following service operations
          Namf_Communication_N1N2MessageTransfer
          Nsmf_PDUSession_CreateSMContext
        Draft in S2-18XXXXX
    Option 3: AMF does not know type of “N2 information”
      Need to update “Update SM Context” service in TS 29.502
      Need to update TS 38.413 so that AMF does not know type of “N2 information”

## Slide 8: Annex.
PDU Session Establishment
N1 SM container + N2 SM Information

## Slide 9: Annex.
PDU Session Modification
N1 SM container + N2 SM Information

## Slide 10: Annex.
PDU Session Release
N1 SM container + N2 SM Information

## Slide 11: Annex.
Service Request
N2 SM Information

## Slide 12: Annex.
CN-initiated selective deactivation of UP connection of an existing PDU Session
N2 SM Information