## Slide 1
S2-1812439
NTT DOCOMO
FS_CIoT_5G
KI15 CN steering
Solution 42 options

## Slide 2: Background
In Solution 42 “NAS based Redirection between Core Networks”, the redirection is performed by rejecting the Registration/Attach/TAU request with a cause value that causes the UE to disable the N1/S1-mode, and attempt registration to the other (target) CN type.
Based on the current procedures, if the target CN is not available, the UE may re-enable the source CN mode and return back to source CN, which could lead to a ping-pong between EPC and 5GC.
In SA2 FS_CIoT_5G telco on Nov 15, 2019, some companies expressed the opinion that also the above ping-pong issue needs to be resolved during the study phase, and it should not be postponed to normative phase.
The following slides present three options to resolve the issue.
The options are documented also in the companion pCR (S2-1812438) that removes the corresponding Editor’s Note from Solution 42.
Only the direction from EPC to 5GC is covered in the slides, but the other direction uses the same principle in the pCR.

## Slide 3: Option A
The redirection policy in MME should take the 5GC coverage into account, and not redirect the UE to 5GC in areas where 5GC is not available.

## Slide 4: Option B
If the UE needs to return back to the EPC due to unavailability of 5GC, the UE indicates in the Attach/TAU request that the request is sent due to unavailability of 5GC. Based on the indication, the MME knows not to redirect the UE again to 5GC.

## Slide 5: Option C
Upon rejecting the Attach/TAU request due to redirection, the MME stores the redirection history to HSS+UDM. The redirection history may contain e.g. a timestamp when the UE was redirected. If the UE needs to return back to the EPC due to unavailability of 5GC, the target MME retrieves the redirection history from the HSS+UDM, based on the redirection history the MME knows not to redirect the UE again to 5GC.

## Slide 6: Way forward
Agree to conclude Solution 42 (S2-1812436)
with one option A, B or C (S2-1812438)
What is your preferred option?