## Slide 1: EPC Dedicated Bearers for Ethernet
Source: Vodafone
SA WG2 Meeting #129bis November 26 - 30, 2018, West Palm Beach, USA
Agenda item: 7.1
Tdoc S2-182459

## Slide 2: Rationale
3GPP’s ecosystem continues to expand to more than smartphones
Many parts of the world (see annex) might not be in 5GCore coverage
Small/Medium Enterprises in developed countries might not get dedicated in-building cells
Reasonable number of applications (machines) expected to only use Ethernet (without IP)
Many machines require QoS with some guarantees, e.g. a GBR bearer
EPC does not allow GBR bearers to be the default bearer.
 Dedicated bearer support for ‘Ethernet’ would be useful for EPC in Rel 16
Release 15 situation summary
R15 5GCore maps its Ethernet PDN type to “Non-IP” in EPC
Any 5GCore Ethernet GFBR QoS Flows are mapped onto the Default PDN connection at mobility to EPC

## Slide 3: R15 components that can be reused
TS 29.244 (clause 5.13) CUPS stage 3 provides support for a SMF to configure a UPF for Ethernet use - this would already be used by a 5G-Core capable UE needing an Ethernet PDN type that establishes PDN connectivity over EPC access.
In line with S2-1811560, not change the EPC's PCC specs, but e.g. use APN to select a PGW-C that supports "SMF+PGW-C" functionality and the N7 interface (with Ethernet support) to the PCF
Use the (Release 5) ‘container functionality’ of the EPC Traffic Flow Template to carry Ethernet header TFTs between PGW-C and UE. This could be invisible to a VPLMN that supports R13 "non-IP".

## Slide 4: More detail on R15 Status
Release 13 EPC supports “non-IP” PDN connections but there is very limited description of how these PDN connections could be used for Ethernet support.
Release 15 5GCore supports “Ethernet” and “Unstructured” PDN connections and – at mobility with EPC – maps them to non-IP.
At handover/mobility, from 5GCore to EPC, dedicated bearers are not transferred.
TS 23.401 clauses 4.3.17.8.1 and 4.7.2.1 indicate that Dedicated Bearers are not supported for the Non-IP PDN type, but do not specify that any node is required to reject them.
TS 24.301 clause 6.1.1 says that the network shall not initiate Dedicated Bearers for non-IP PDN connections -> but UE support for an Ethernet TFT would be needed.
TS 36.323 (PDCP) has SDU Type specified, but probably only for SideLink (PC5) use.
TS 36.413/38.413 indicate PDN type (Non-IP/Unstructured/Ethernet) to the RAN to disable Header Compression.
Packet filters are carried in the TFT in EPC and are specified in TS 24.008. The TFT is a container mechanism between UE and PDN-GW and e.g. is used for TS 24.229 Authentication Tokens.

## Slide 5: Proposals
Agree to draft TEI-15 EPC CRs for dedicated bearer support on EPC.
Decide whether to use Non-IP PDN type in EPC, or, new EPC Ethernet PDN type
Allocate two by 0.5 TU in SA2 for this work.
d) No RAN impact expected

## Slide 6: Annex
3GPP is rather focused on advanced parts of Asia, Western Europe and North America
But much of the mobile eco-system is outside of these markets… and is growing fast
E.g. Mobile Usage shown on sheet 12 of Vodafone’s half year results at https://www.vodafone.com/content/dam/vodafone/investors/financial_results_feeds/half_year_30september2018/H1_2019_Web_Spreadsheet_FINAL.xlsx
Not obvious that the “emerging markets” will move rapidly to 5GCore.  EPS enhancements should not be rejected merely to focus on 5GCore enhancements

## Slide 7
https://www.vodafone.com/content/dam/vodafone/investors/financial_results_feeds/half_year_30september2018/H1_2019_Presentation_DOWNLOAD.pdf

## Slide 8
Europe
Iceland
Turkey
Hungary
Spain
Italy
Poland
Romania
Serbia & Mon.
Russia
Estonia
Latvia
Lithuania
Belarus
Ukraine
Moldova
France
Albania
Macedonia
Czech Rep.
Slovakia
Germany
Bulgaria
Croatia
Slovenia
Belgium
Austria
Switzerland
Netherlands
Malta
Portugal
Norway
Finland
Sweden
Greece
Denmark
Bosnia
Vodafone Opco
Vodafone Partner Market
Georgia
Azerbaijan
Armenia
Cyprus
Ireland
UK

## Slide 9
Africa
Tunisia
Madagascar
Morocco
Egypt
Algeria
Libya
Sudan
Ethiopia
Somalia
Chad
Niger
Nigeria
Mali
Mauritania
Central African Rep
Cameroon
Kenya
Dem. Rep of the Congo
Tanzania
Mozambique
Zimbabwe
South Africa
Botswana
Zambia
Namibia
Angola
Western Sahara
Senegal
Guinea
Liberia
Cote D’Ivoire
Gabon
Congo
Burkina Faso
Ghana
Togo
Benin
Uganda
Rwanda
Burundi
Malawi
Lesotho
Swaziland
Sierra Leone
Gambia
Vodafone/Vodacom Opco
Vodafone Affiliate

## Slide 10: END