## Slide 1: Study on supporting Unmanned Aerial Systems Connectivity, Identification, and Tracking
S2-1810064
Qualcomm Incorporated

## Slide 2: UAS Study in SA1
SA1 has progressed well on the UAS study
A consolidated set of potential requirements is available, highlighting specific needs for architectural work in SA2

## Slide 3: UAS Reference Architecture
Some assumptions:
  UAVc-UAV(s) relationship is 1:N
  UE permission to act as UAS (UAVc and UAV(s)) obtained via UTM
CN

## Slide 4: UAS Identification, Authorization, and Tracking
UAS needs authentication and authorization to be allowed in the 3GPP system and to be allowed by the UTM
UAS authorization via UTM based on UAV Data and 3GPP identifiers
  UAV Data mostly defined by entities outside 3GPP and used by 3GPP (e.g. delivery of parameters)
Subscription aspects and MNO policing based on UE being an UAS are in the scope of 3GPP

## Slide 5: UAS Identification, Authorization, and Tracking
A system level study would need to identify
  The role of the 3GPP system in supporting UAS identification, authorization and tracking
  The impact on procedures and interfaces to enable this, if any
Note: It is expected that UAV Controller may have other functions, e.g. be a smartphone, not limited only to UAS operations
  Blind denial of registration for a UE acting as UAV controller may not be feasible
  Need to study how to ensure enforcing failed authorization
  Also “kicking off” UAS element will not allow further tracking

## Slide 6: UAS Context
Based on SA1 discussion:
  UTM creates and maintains “pairing” of UAVc and UAV(s) upon successful authorization/authentication
    3GPP system to enable this
  MNO creates and maintains “pairing” of UAVc and UAV(s) upon successful authorization/authentication
    3GPP system to implement this

## Slide 7: UAS Communications
Consists of
  UAS-UTM communications (UAVc-UTM and UAV-UTM)
  UAVc-UAV(s) communications
Content of “messaging” expected to be outside the scope of SA2
However, 3GPP system must enable such communications
  Ensure communications are enabled based on appropriate subscription and authorization
  UAV-specific aspects (e.g. RAN resources) are enabled and authorized appropriately
  Resource revocation is in place to support requirements

## Slide 8: The Role of V2X
Several similarities exist between UAS requirements/use cases and the V2X requirements and system design
3GPP should strive to re-use as much as possible the work done for V2X to enable the requirements for UAS

## Slide 9: Conclusions
A SID is needed in SA2 to
  Identify interaction between UAS and system and UTM to enable authentication, authorization, identification, tracking, and connectivity establishment to enable
  Identifying architecture and system aspects related to supporting UAS command and control functions according to use cases defined in SA1, including studying various solutions (e.g. control plane versus user plane) for enabling according to SA1 requirements:
    UAS identification and tracking via the 3GPP system
    UAS authorization/authentication
      Study how different levels of authentication/authorization, as identified in SA1 requirements, impact system procedures
      Identify the end result of lack of authorization (e.g. lack of resources for use plane communications to carry UAV control messages, denied registration, etc.) while considering the need for the system to keep track of UAV(s)
    Connectivity between UAV controller(s) and UAV(s)
    Connectivity to the UTM
  Identifying the role of the 3GPP system for authorization of UAS(es) and for control of UAV controller to UAV(s) communication
  Identifying relationship with V2X solutions in order to re-use existing solutions to the maximum extent possible

## Slide 10: Further Considerations Impacting Study
Security of UAS communications and identification will be analysed by SA3.
The study item will also analyze whether the mechanisms to support UAS in the 3GPP system are applicable to EPS only, 5GS only, or to both 5GS and EPS.
It is expected that UAV controller to UAV(s) communications are outside the scope of SA2.
It is expected that UAV Controller may have other functions, e.g. be a smartphone, not limited only to UAS operations