## Slide 1
NSSAI in access Stratum
3GPP TSG SA WG2 meeting#129 Tdoc S2-1810389
Dongguan, China, October 15-19 2018
Nokia, Nokia Shanghai Bell, NEC, Telecom Italia, Huawei, InterDigital, AT&T, Verizon, Sprint, Orange, China Mobile

## Slide 2
Overall Background
Network slicing is an end to end feature that requires network slicing support in the CN and in the RAN.
Operators may support slices that implement Slice Aware policies to fulfil specific SLA with their customers or for own operational reasons.
  These may include aspects that apply also before contacting the CN and retrieve allowed NSSAI to:
    take local actions to release connections that cannot be served in the RAN
    Instantly Protect the CN in cases it is overloaded by certain slices, but not others, or in cases certain slices need to be taken out of service at a certain AMF but not others (UAC is AMF agnostic)

## Slide 3
RAN awareness: 38.300 text
The text points to:
There are policies in the RAN that require awareness of the slices the UE uses
some policies may use information in RRC PRIOR to contacting the CN: for these policies to work RRC needs to include NSSAI

## Slide 4
RAN awareness: 23.501 text (see clause 5.15.2.1“General”)
The (R)AN may use Requested NSSAI in access stratum signalling to handle the UE Control Plane connection before the 5GC informs the (R)AN of the Allowed NSSAI.

## Slide 5
AMF overload control: 23.501 text
Slice aware overload control is already there in TS and works on NSSAI in the RRC connection establishment…
if some connections establishment requests do not send NSSAI they use, these cannot be treated by RAN awareness
UEs would be handled by default policy regardless of the importance of the UE

## Slide 6
Operator is in driving seat: they chose what they want in their networks
proposal

## Slide 7
Is it really so sending NSSAI in RRC is damaging performance?
Scheduling of RRC Connection establishment MSG5 MSG 5 is neutral to whether Registration or SR is sent over NAS signalling.
  No one disagrees to include NSSAI in registration messages.
Operators can tune the resources allocated to msg5 initial grant to the what they see optimal for their use cases and e.g. most frequent NSSAI size… most likely most UEs will send a standard SST value of 8 bits, some will use 2/3 S-NSSAI. almost none 8 (the maximum allowed). Operators can take their own pick and maybe in network assume optimised handling of SR with NSSAI up to 2 S-NSSAIs, for instance.
  Operators choose scheduling of msg5 according to tradeoff between functionality they want to deliver and resources they want to allocate to msg5. If an operator wants JUST to minimize msg5 size, it is free to do so with our proposal and will instruct the UEs to operate in mode C.
We cannot decide in 3GPP the only criterion for operators is minimum allocated resources for MSG 5
Hence the freedom we give to operators to choose what they want or need.

## Slide 8
For info
SR-related RRCSetupComplete message size including PDCP and MAC analysis
The following slides show a detailed analysis of overhead impact for SR message due to UL data (most frequent SR type).

## Slide 9
NAS message (TS 24.501)
A NAS message needs to include the yellow highlighted IEs before the NAS message itself.
So we have 7 octets here
IEI | Information Element | Type/Reference | Presence | Format | Length
 | Extended protocol discriminator | Extended protocol discriminator 9.2 | M | V | 1
 | Security header type | Security header type 9.3 | M | V | 1/2
 | Spare half octet | Spare half octet 9.4 | M | V | 1/2
 | Message authentication code | Message authentication code 9.8 | M | V | 4
 | Sequence number | Sequence number 9.10 | M | V | 1
 | Plain 5GS NAS message | Plain 5GS NAS message 9.9 | M | V | 3-n

## Slide 10
NAS SR message (TS 24.501)
SR for UL data is normally 15 octets. Could be 19 if PDU sync is done in current access, 23 if also on other access.
IEI | Information Element | Type/Reference | Presence | Format | Length
 | Extended protocol discriminator | Extended protocol discriminator 9.2 | M | V | 1
 | Security header type | Security header type 9.3 | M | V | 1/2
 | Spare half octet | Spare half octet 9.5 | M | V | 1/2
 | Service request message identity | Message type 9.7 | M | V | 1
 | ngKSI | NAS key set identifier 9.11.3.32 | M | V | 1/2
 | Service type | Service type 9.11.3.50 | M | V | 1/2
 | 5G-S-TMSI | 5GS mobile identity 9.11.3.4 | M | LV | 7
40 | Uplink data status | Uplink data status 9.11.3.57 | O | TLV | 4-34
50 | PDU session status | PDU session status 9.11.3.44 | O | TLV | 4-34
25 | Allowed PDU session status | Allowed PDU session status 9.11.3.13 | O | TLV | 4-34
24.501 Table 8.2.16.1.1: SERVICE REQUEST message content

## Slide 11
RRCSetupComplete message (TS 38.331)
2 bit TI,
4 bits selected PLMN Id,
6 octets S-TMSI, registered AMF between 3 octets and 9 if PLMN Id is different than the one indicated in message
without any extension, At least 10 octets are there commonly. Could be 16 also when multiple PLMN IDs are shared an AMF

## Slide 12
SR message PDCP (TS 38.323):
For SRBs, the MAC-I field is always present. If integrity protection is not configured, the MAC-I field is still present but should be padded with padding bits set to 0.
So 6 Octets are for PDCP
< Data PDU for SRB >
< 38.323 - Figure 6.2.2.1-1: PDCP Data PDU format for SRBs >

## Slide 13
SR message MAC layer (TS 38.321)
L = L: The Length field indicates the length of the corresponding MAC SDU r variable-sized MAC CE in bytes.
8 bits is suffient for SR -> 2 octets overhead

## Slide 14
Summary of SR length without NSSAI in RRC for UL data:
Item | octets | Comments
NAS signaling header | 7 | 
NAS SR | 15 | 19 or 23 if PDU sync on one or two accesses
RRCSetupComplete | 10 | Could be more if PLMN ID needs to be added to registered AMF.
PDCP | 6 | 
MAC | 2 | 
Total | 40 | 

## Slide 15
Worst case overhear analysis ABOVE PHY
NSSAI (S-NSSAI#) | OVERHEAD
1 | 0.10
2 | 0.20
3 | 0.30
4 | 0.40
5 | 0.50
6 | 0.60
7 | 0.70
8 | 0.80
This analysis assumes the operator uses a S-NSSAI of 32 bits. If some operators uses only SSTs (standardised or not)
Results change dramatically. RRC allows sending SSTs-only S-NSSAIs (basically the overhead in a SST – only PLMN would
a quarter and would reach maximum of 20% with 8 S-NSSAIs. Overhead is likely to be smaller once PHY and other headers
we did not take into account are factored in.

## Slide 16
Is it really so we need no special handling for SR as the AMF only has to protect from new entrants?
One company say that SR is generated by UEs already served by AMF so the AMF shall be always able to handle load from these UEs. So slice aware overload control is not needed.
In our view, traffic patterns can be situation dependent… e.g. a certain event may load the network in unusual manner, and also just in one slice.
UAC is not AMF aware so load a single AMF may result in rejection of all UEs attached to any AMF.
UAC is limited in its effectiveness as there are only 32 operator-defined categories allowed and just 8 UAC access categories may be broadcasted at a time, including the standardised ones, with instructions on what to do (i.e. timers and drop rate).
So: slice specific AMF overload control is still useful and we should retain it. UAC is not sufficient or even usable effectively in this case.

## Slide 17
If the RAN gets the allowed NSSAI from the CN, why do we need NSSAI from UE in RRC messages?
- TS 38.300 says this is to implement in the RAN slice aware policies prior to contacting the CN
RAN can release connections for registration messages (which we all agree include NSSAI) without the need of contacting the AMF
Note: sending NAS message to the CN would trigger signalling towards SMF etc. and then if connection is release also all the state needs to be reverted.
  if RAN does not send it to CN because the RAN is slice aware it is a far more efficient

## Slide 18
Conclusions
Operators can decide whether to apply RAN aware policies to Service Requests.
If they see the overhead outweighing the benefit in their network, they can configure their network to operate in mode C.
In networks where it is critical to apply RAN awareness to the initial contact with the RAN, PLMN wide or in specific area where critical applications are expected to run, operators can configure UEs to send NSSAI in SR according to mode A or B.