## Slide 1
R16 ETSUN / debate on objective 1
S2-1810419
OCT 2018
lth

## Slide 2: R16: FS_ETSUN (intermediate SMF and SMF-UPF scalability)
2 Objectives:
Investigate mechanisms to enable the 3GPP system to support deployments where a SMF is not able / allowed to control UPF(s) throughout the same PLMN.
  Solutions are about inserting an Intermediate SMF (I-SMF) and the discussion is on the nature of the interface between A-SMF (Anchor SMF) and I-SMF (like N16 or N4??)
  Related with AMF, ISMF and local UPF operated by another (local) administrative entity than Anchor SMF and UPF (PSA)
  Nokia remark: this kind of architecture should correspond to exceptional cases (SSC mode 2 could solve many cases where a new PDU Session is controlled by a SMF in the new region)
Study whether it is needed to enhance the capability of 5GS architecture for a UPF to be controlled by multiple SMF's (and many UPF's to be controlled by many SMFs) and, if yes, define such enhancements.
  Discussion mostly centered around IP @ allocation for the UE
SID Status: almost ready for solution evaluation (still many FFS and need to explain at high level differences between solutions that rely on the same architecture)
TR 23.726. SID SP-170743

## Slide 3: R16: FS_ETSUN / intermediate SMF ISMF controlling the local UPF(s)
The main debate is on whether the I-SMF acts as a kind of V-SMF (ASMF-ISMF Nxx interface is like or based on upgraded N16 ) or as a N4 proxy (ASMF-ISMF interface is like or based on upgraded N4).
In case of traffic offload (UL CL/ BP) how are (sol 13 or 15)
  Offload policies sent to I-SMF
  Usage monitoring reporting sent from local UPF to CHF
Other debates e.g.:
Which entity selects ISMF (ASMF or AMF)? Based on which information?
Overview/issues
Nxx like N16
sol 1/6 (+sol 13/15)
Nxx like N4
Sol 5

## Slide 4: R16: FS_ETSUN / intermediate SMF: I-SMF controlling the local UPF(s)
Nxx like N16
  I-SMF like VSMF (HR) but with deltas e.g. a newly inserted I-SMF possibly retrieves SM context from I/A-SMF or via AMF
  The interface between AMF and I-SMF is the existing N11 (I-SMF terminates of SM parts of NAS messages and N2)
  Only one CP interface between the local administration domain and the administration domain of the A-SMF and PSA
  IDLE-CONNECTED transitions and HO involve only one SMF / one interface: N11
Nxx like N4
  AMF possibly not impacted when I-SMF selected by A-SMF (another administration domain); I-SMF has no NAS knowledge
  2 CP interfaces between the local administration domain and the administration domain of the A-SMF and PSA (IOT)
  IDLE-CONNECTED transitions and HO involve 2 SMF / 2 interfaces: N11 and Nxx (signaling cost and delay)
N16 or Nxx like N4 (not discussing PCF/CHF aspects)
Nxx like N16
Nxx like N4

## Slide 5: R16: FS_ETSUN / intermediate SMF: I-SMF controlling the local UPF(s)
How : Offload policies are sent to I-SMF / Usage monitoring reporting are sent from local UPF to CHF
Transfer only via A-SMF (sol 4 OR sol1/6+15)
  Only one Npcf / one Nchf (simpler PCF/CHF likely not impacted)
  But usage reporting involves one extra hop: N4+ Nxx + N7 or Nchf
Direct interface to I-SMF (sol1/6+13)
  Multiple Npcf / Nchf (impact to PCF/CHF that are modified to support 2 interfaces and to be aware of ISMF insertion/removal).
  But usage reporting involves one less interface: N4+ N7 or Nchf
Traffic offload (UL CL/ BP)
Nxx like N16
Nxx like N4
Nxx like N16 with multiple CHF/PCF itf

## Slide 6: R16: FS_ETSUN / intermediate SMF: I-SMF controlling the local UPF(s)
When a SMF registers its services with the NRF, or when OAM provisions the NRF, the SMF Service Area is provided and stored in NRF; the NF selecting the I-SMF provides the UE location (e.g. TA) in the SMF discovery procedure towards NRF.
By AMF (fits well with Nxx like N16)
  Like VSMF selection. Done in the local administrative domain of the ISMF
By A-SMF (fits well with Nxx like N4)
ISMF selection
Nxx like N16
Nxx like N4

## Slide 7: R16: FS_ETSUN / intermediate SMF: I-SMF controlling the local UPF(s)
Need to fine tune the call flows (how does I-SMF retrieve the context at change of I-SMF) but can be done later once other decisions taken
Other points
Nxx like N16
Nxx like N4