## Slide 1: Discussion: UE registration to Non-Public NW
Samsung
S2-1810584

## Slide 2: NPN deployment scenarios
Non-public network deployment scenarios
  non-public network managed by a PLMN
    A) UEs, which can access via NPN to the hPLMN
      E.g. hPLMN manages the NPN or has roaming agreement with the PLMN which manages the NPN.
    B) UEs, which can not access via NPN to the hPLMN.
  non-public network isolated from PLMN
    C) All UEs can not access to any PLMN.
Observation:
Regarding UEs in case A), we may consider reusing UE ID/Credential of the PLMN for Non-public network.
Regarding UEs in case B) & C), we need to define new UE ID/Credentials for Non-public network
hPLMN : PLMN which manages UE credential

## Slide 3: UE registration procedure to NPN
UE context retrieval from old AMF in PLMN
UE Authentication
UE Authorization and UE_CM_Reg
Case A)
Case B&C)
N/A
PLMN credential-based authentication is not possible
non-PLMN credential based authentication
Possible, based on 5G-GUTI.
PLMN credential-based authentication is possible
PLMN entities cannot be involved.
Either PLMN entities(UDM) or NPN entities can be involved per operator’s policy
We may use the existing registration procedure except using NAI and non-PLMN credential for UE, which is performed exclusively from registration to PLMN.
Next page

## Slide 4: Proposal: For case A), UE Registration procedure to NPN
UE authentication for NPN may be performed with AUSF in hPLMN, based on PLMN credential
“NPN identification” is included for message routing or NF selection
“SUCI/SUPI/GUTI can be used as UE ID for NPN
UDM in the NPN is not used for
Based on “NPN identification”, AMF may select the appropriate UDM managing the UE Subscription Data for the NPN
Assumption: UE credential / SUPI’s are managed by PLMN
Assumption: UE subscription data/ SUPI’s are managed by NPN owner with PLMN
UE authorization and UE_CM_reg can be done via UDM in the NPN

## Slide 5: Thank you