## Slide 1: SA2#129 Summary of input papers
Partial encryption for Initial NAS message/AS signaling
Nokia, Nokia Shanghai Bell, Samsung, NEC, Telecom Italia
S2-1810804

## Slide 2: Summary of all papers for initial NAS msg protection
Parameter in the initial NAS | Qualcomm (S2-1810078, S2-1810095, S2-1810080, S2-1810081) | Ericsson (S2-1810248, S2-1810249, S2-1810250) | Samsung (S2-1810095) | Intel (S2-1810095) | Nokia/Telecom Italia (S2-1810445)
Last TAI | Encrypted | Encrypted, as not used until creating RA | Encrypted | Encrypted | Encrypted
Moving from EPC | Encrypted | Clear | Clear | Not addressed | Clear
S-NSSAI | Encrypted if there is a security context, otherwise send when SMC is completed | Encrypted, see step 9b in Registration procedure | No, send in SMC. Change 4.2.2.2.2 steps to do AMF re-allocation after SMC received) | Encrypted S-NSSAI can always be sent encrypted: In SMC when UE does not have security context With partial ciphering, when UE has security context Now, given that Intel proposes S-NSSAI to be sent as cleartext in RRC during Initial and Mobility Registration, sending S-NSSAI in SMC (when UE has no security contxt) is not needed | Clear (Can accept if it is encrypted (partial ciphering) and/or sent along with SMC although this will require change in registration procedure)
Partial Encryption solution assumed (Reference – TS 33.501) | Yes | Yes, essential IEs in clear text and rest in SMC complete. | Yes | Yes | Yes

## Slide 3
Parameter in the RRC message | Qualcomm | Ericsson | Samsung | Intel | Nokia, Telecom Italia
S-NSSAI | Addressed in separate CR where S-NSSAIs are provided in RRC based on HPLMN and VPLMN indication (per S-NSSAI) | Remove S-NSSAI from AS signaling as to address privacy on all layers (can be provided when possible to encrypt) | Not addressed | Clear for RR (no NSSAI for SR and Periodic Registration Update) | Sent in clear
Summary of all papers for S-NSSAI in AS signaling

## Slide 4: Additional statements of position
Parameter in the initial NAS | NEC |  |  |  | 
Last TAI | - |  |  |  | 
Moving from EPC | - |  |  |  | 
S-NSSAI | The S-NSSAs with privacy consideration should be sent encrypted in NAS message - send during SMC procedure or after that. |  |  |  | 
Partial Encryption solution assumed (Reference – TS 33.501) | - |  |  |  | 
Parameter in the RRC message |  |  |  |  | 
S-NSSAI | - |  |  |  | 

## Slide 5: Questions to move forward
In order to reach conclusions, following questions need to be answered:
  1. Shall the last visited/registered TAI be encrypted in NAS messages?
  2. Shall the moving from EPC parameter be encrypted in NAS messages?
  3. Shall the S-NSSAIs be encrypted in (initial) NAS messages?
    NOTE 1: Whether it makes sense to encrypt S-NSSAI in NAS if it is sent as cleartext in RRC (per question 4) is a separate debate
  4. Shall the S-NSSAI be sent in AS message (in clear text) for NAS Initial Registration and Mobility Registration request?
    NOTE 2: Whether S-NSSAI is sent in AS message (in clear text) for NAS SERVICE REQUEST and NAS Periodic Mobility Update Request is a separate debate

## Slide 6: Backup

## Slide 7: Snippet from TS 23.501/2 for “moving from EPC”
23.501: For idle mode mobility from EPC to 5GC, the UE performs mobility Registration procedure with the 5G GUTI mapped from EPS GUTI and indicates that it is moving from EPC. => “moving from EPC” indication used by AMF to determine that the 5G GUTI was mapped from EPS GUTI.
23.502: The UE sends Registration Request with registration type set to "Mobility Registration Update", including 5G-GUTI mapped from EPS GUTI as the old GUTI, the native 5G-GUTI (if available) as additional GUTI and indicating that the UE is moving from EPC => “moving from EPC” indication used by AMF to determine that the 5G GUTI was mapped from EPS GUTI.