## Slide 1: Discussion on SMF Delegated Discovery and Selection for HR scenario
Oracle
SA WG2 Meeting #132 S2-1903397
April 8 - 12, 2019, Xi’an, China

## Slide 2: Background/purpose
In Rel-15, in the PDU Session Establishment procedure, the AMF performs SMF Selection (which is further broken down into NSSF interaction & NRF interaction). Below are the corresponding 23.502 figures for the Non Roaming/LBO scenario and for the HR roaming scenario.
SMF Selection for non-roaming/LBO (23.502 Rel-15 Figure 4.3.2.2.3.2-1)
SMF Selection for HR-roaming
(23.502 Rel-15 Figure 4.3.2.2.3.3-1: Option 1)
In Rel-16, it’s been specified how delegated SMF discovery and selection works via the SCP for the non-roaming case. However, it’s still FFS how SMF discovery and selection works in the HR case as per the following editor’s note in subclause 6.3.2 of TS 23.501:
  Editor's note: It is FFS how the SCP handles the selection of the vSMF and hSMF in the HR roaming case and it is also FFS how the vSMF is informed of the selected hSMF in the case of delegated discovery and HR case.
This paper discusses how the Rel-16 ‘SCP delegated mode of discovery and selection’ may fit into the PDU Session Establishment procedure for the HR roaming scenario based on the TR 23.742 conclusions for KI #3 and based on the already updated sections in Rel-16 23.501.

## Slide 3: Rel-16 Current Non Roaming/LBO scenario for SMF selection
SMF Selection for non-roaming (23.502 Figure 4.3.2.2.3.2-1)
SMF Selection for non-roaming delegated via SCP (Integrated with the PDU Session Establishment service request and response)
Serving PLMN
NOTE: NSSF interaction is assumed to be outside of the scope of SCP.
Rel-15 (No SCP)
Rel-16 (SCP delegated mode)
Below is the current non-roaming ‘Rel-16 SCP Delegated mode version’ of the PDU Session establishment procedure. This includes the initial service request followed by the SMF selection (performed by the SCP).

## Slide 4: Home Routed SMF selection alternative 1a Visited SCP based Delegated Discovery of the H-SMF
Rel-15 (No SCP)
Proposed Rel-16 SCP delegated mode
V-SCP performs Discovery and Selection of both V-SMF and H-SMF.
AMF-NSSF and vSCP-vNRF interactions not optimized, i.e. they are done first for VPLMN and only then for HPLMN as currently defined for the AMF in 23.502
V-SMF discovery & selection
H-SMF discovery & selection

## Slide 5: Home Routed SMF selection alternative 1b Optimized Visited SCP based Delegated Discovery of the H-SMF
Rel-16 SCP delegated mode.
V-SCP performs Discovery and Selection of both V-SMF and H-SMF.
Optimized NSSF Selection & Optimized NRF Discovery
Local NSSF selection and remote NSSF selection are done by the AMF in ONE shot
vSCP retrieves vSMF and hSMF in one shot from vNRF (requires a slight input/output parameters adjustments to both NSSF and NRF Rel-15 services))
Rel-15 (No SCP)
V-SMF discovery & selection
H-SMF discovery & selection

## Slide 6: Home Routed alternative 2 Home SCP based Delegated Discovery of the H-SMF
Rel-16 SCP delegated mode
V-SCP performs Discovery and Selection of V-SMF only.
H-SCP performs Discovery and Selection of H-SMF.
Rel-15 (No SCP)
V-SMF discovery & selection
H-SMF discovery & selection

## Slide 7: Summary and Proposals
Summary
Alternative 1a simply requires the AMF to skip the discovery steps, while providing the results of slice selection to the SCP (V-NRF id and H-NRF id).
Alternative 1b is an optimization of 1a with the slice selection and discovery steps each collapsed into one, however, it requires changes to multiple existing procedures (slice selection, discovery, etc.)
Proposal 2 delegates H-SMF discovery and selection to the H-PLMN/H-SCP, leveraging delegated discovery end to end. It does however require knowledge at the V-PLMN of the capabilities of the H-PLMN to perform delegated discovery.
Go forward alternatives
Alternatives 1a and 2 are aligned with the current delegated discovery with the burden being respectively placed on the V-PLMN and H-PLMN.
On the other hand, while alternative 1b provides optimizations, its impact to the current procedures is quite large.
Our proposal is to define alternatives 1a and 2 as potential solutions to SMF delegated discovery in HR scenario based on operator configuration and policies. These changes are documented in the following accompanying CRs
  S2-1903400 for TS 23.501
  S2-1903401 for TS 23.502