## Slide 1: Source: Ericsson Title: Handling of Emergency Session during Handover Document for: Discussion/Agreement Agenda Item: 6.5.9, 6.5.10 Work Item / Release: 5GS_Ph1
SA WG2 Meeting #133 Reno, Nevada, USA, 13-17 May 2019
Tdoc S2-1905083

## Slide 2: Background
During SA2#132
  S2-1903829 (Rel-15) and S2-1903830 (Rel-16) “Correction of ePDG-5GS emergency session handover” were discussed
A holistic approach should be taken to cover other emergency handover scenarios, e.g. EPS to 5GC/N3IWF and EPS to 5GS mobility without N26.

## Slide 3: Discussion - Handover Scenarios of Emergency Service
Between N3GPP and 3GPP
  Scenario-1 EPC/ePDG -5GS
  Scenario-2 EPS -5GC/N3IWF
  Scenario-3 5GC/N3IWF – 5GS
MME
AMF
SGW
PGW-C
HSS+UDM
ePDG
NG-RAN
eNB
N3IWF
WLAN AP
EPC/ePDG
EPC/LTE
Scenario-1 5GS <-> EPC/ePDG
Scenario-2 5GC/N3IWF-EPS
AAA
S5/S8
S2b
N11
5GC
Scenario-3
UDM
SMF
Between 3GPP accesses
  Scenario-4 EPS-5GS without N26
Scenario-4 EPS-5GS without N26

## Slide 4: Discussion- Information needed for emergency handover
Scenario-1a EPC/ePDG -> 5GS
Scenario-2a EPS -> 5GC/N3IWF
AMF
UDM
Emergency Indication and
PGW-C FQDN
Emergency-Info
HSS
Scenario-1b: ePDG,
Scenario-2b: MME
AMF
UDM
Emergency-Info
HSS
Emergency Indication,
PGW-C FQDN
SMF
Scenario-1b 5GS -> EPC/ePDG
Scenario-2b 5GC/N3IWF -> EPS
Scenario-3 5GS <-> 5GC/N3IWF (no update needed)
AMF
UDM
SMF
Emergency Indication
SMF ID
Scenario-1a: ePDG
Scenario-2a: MME
Scenario-4 EPS-5GS without N26
Refer to Scenario-1a and -1b for update on 23.502
Update to 23.401 that MME notifies the HSS about the PGW-C FQDN for the emergency PDN connection.
The same AMF is always used for emergency session, and the AMF use Nsmf_PDUSession_UpdateSMContext, and there is no need to use Emergency Info.
Update to 23.502 needed

## Slide 5: Proposal
[Proposal-1] Add Emergency Information in UE Subscription data type “UE context in SMF data” in clause 5.2.3.3.
[Proposal-2] Update Nudm_SDM_Notification service operation in clause 5.2.3.3.3 to clarify UDM notifies also the Emergency-Information containing FQDN of PGW-C to the AMF.
[Proposal-3] At handover of emergency session to 5GC (i.e. PDU Session establishment with request type “Existing Emergency PDU Session” is received), the AMF uses Emergency Info (provided by UDM) to locate the PGW-C+SMF.
3 sets of CRs are proposed for different handover scenarios:
  CR set 1: Scenario-1 EPC/ePDG -> 5GS
    [Proposal-1] and [Proposal-2];
    [Proposal-3]
    23.502 CR1330 (S2-1905084), CR1331 (S2-1905085)
  CR set 2: Scenario-2 EPS -> 5GC/N3IWF
    [Proposal-1] and [Proposal-2] (captured in CR set 1)
    [Proposal-3]
    23.502 CR1332 (S2-1905086), CR1333 (S2-1905087)
  CR set 3: Scenario-4 EPS->5GS without N26
    [Proposal-1] and [Proposal-2] (captured in CR set 1)
    [Proposal-3] +Update on 23.401
    23.502 CR1335 (S2-1905089), CR1336 (S2-1905090)

## Slide 6
THANK YOU !