## Slide 1: Source: Ericsson, AT&T, FirstNet Title: Rx and Npcf support and documentation approach Document for: Discussion/Agreement Agenda Item: 6.14 Work Item / Release: eIMS5G_SBA
SA WG2 Meeting #133 Reno, Nevada, USA, 13-17 May 2019
Tdoc S2-1905347

## Slide 2: Discussion on IMS functionality and supported reference points (PCF - P-CSCF)
EPC Rel-16
5GC pre-Rel-16
SBI interfaces
(Rx to Npcf (N5))
Rx kept to non-SBI AF (IMS)
5GC Rel-17 and onwards
SBI interfaces
(Rx to Npcf (N5))
Rx kept to non-SBI AF (IMS)
5GC Rel-16
Any AF deployed as part of the 5GC in R16 and beyond, is expected to be Type 2

## Slide 3: Discussion on IMS functionality and supported reference points (PCF - P-CSCF)
5GC Rel-17 and onwards
5GC Rel-16
Same functionality (if supported by the Access Network (5G)
Rx reference point:
.-Transfers application level session information for policy and charging control.
-Sponsored data connectivity
-Notifications to the AF
-Support for RAN UP control
Features (Support for in Rx)
- IMS Emergency
- RLOS service
- MPS
- MCPTT
- Resource sharing
- Data off services
EPC Rel-16
Rx reference point:
Same as in EPC Rel-16
Npcf Reference Point:
Same as in Rx except RAN UP control
Features (Support for in both N5 and Rx)
- IMS Emergency - MPS
- MCPTT
- Resource sharing
- Data off services
Npcf Reference Point:
Same as in Rx except RAN UP control
Features (Support for in N5)
- IMS Emergency
- MPS
- MCPTT
- Resource sharing
- Data off services
Same functionality (if supported by the Access Network (5G)
Notes: 2018-02-21
3

## Slide 4: Proposal
Support for IMS functionality while UE in EPC network (non interworking case) remains , evolve Rx if require for IMS functionality changes.
Support for IMS functionality while UE in 5GC network (with(out) interworking within EPC) remains , evolved if required and as such Npcf and Rx may also evolve to cover those requirements.
      Rx and Npcf are both updated in Rel-16, and then Npcf is updated from Rel-17 onwards
  Motivation: Standardization effort to maintain the same functionality over multiple interfaces.
How to document support for Rx and Npcf:
  23.503 Rel-16:
    Support for IMS functionality over Npcf and Rx.
    Move Support for Rx to a normative Annex. Indicate that no new functionality will be added over Rx in future Releases other than Rel-16.
  23.203 Rel-16:
    Support for IMS functionality over Rx.
Notes: 4

## Slide 5
Notes: 2018-02-21
5