## Slide 1: Multi-access over 5GC and EPC
Huawei , Hisilicon
3GPP TSG-SA WG2 Meeting #133 S2-1905699
13 - 17 May 2019, Reno, Nevada, USA

## Slide 2: Background
In SA2#132 meeting, the multi-access over 5GC and EPC case is proposed to be resolved by S2-1903135 and S2-1904135.
The targeted scenario is defined in S2-1903135, i.e. UE/RG is connected over LTE in EPS and non-3GPP/wireline access in 5GS, including both UE and 5G-RG cases.
A solution is also proposed in S2-1904135.
As this solution is not studied in TR 23.793, there is no evaluation on it. So in this paper:
  Evaluation on this soluton, named as solution 1 in this paper.
  Propose the other alternative solutions.
  Proposal.

## Slide 3: Evaluation on solution 1
Restriction on the system level:
  Operator deployment ensures that all PGW-C+SMF(s) shall support the extended PCO for EPC access and ATSSS function for 5GC, resulting in all PGW-C for the specific APN shall support the extend PCO and all combined SMF(s) shall achieve ATSSS functionality as mandatory feature.
  The UE shall always request PDN connection with the MA PDU session indication as proposed by S2-1903135
Impact on the PGW-C+SMF(s)
  For the EPC side, the PGW shall support this new type of PDN connection as an additional leg for MA PDU session, including the new PCO parameters, the new PDN connection authorization mechanism, especially:
    Two UE IP address with the same IP type allocated to this PDN connection, when the MPTCP functionality is activated. One UE IP is for the MA PDU session, the other is for MPTCP.
  For the 5GC side, the SMF shall distinguish the MA PDU session for EPC and 5GC, or the normal MA PDU session only for 5GC, resulting in the system complex. The two solution differences include at least the following aspects:
    Different parameters handling and different procedure triggered by different scenario.
    node selection solution, need to further consider the support of PGW-U for MA PDU session via EPC and 5GC.
    The different MA PDU session authorization mechanism, one is based on the local configuration and the other is based on the PCF decision.
  The internal interaction between the PGW-C and SMF per IP flow (for ATSSS-LL function) granularity or per packet (MPTCP function) granularity.
Impact on the terminal, i.e. 5G-RG
  For the LTE accessing, the new PCO extension has impact on the 4G NAS module. This new 4G NAS module shall be specially implemented. Additionally, for the user plane, the TFT may include the UE IP address for MPTCP not matching the UE IP allocated to this PDN connection.
  No solution for the UE to decide the access availability via LTE, except the NBIFOM solution.
  For the fixed access network, this new MA PDU session solution establishment procedure with the different NAS parameters and different trigger condition results in the different 5G NAS module comparing with the 5G NAS applied by UE, if this solution 1 is only used by 5G-RG.
  In sum, the special customized NAS module for both 4G and 5G will increase the 5G-RG equipment cost.
Impact on the MME,SGW
  No impact on MME.
  For the SGW, this is a special PDN connection allowed to transport the packets encapsulated by the MPTCP’s UE IP address, which is different from the UE IP allocated by this PDN connection. As this is a new case for EPC, not sure if it will impact the SGW implementation or not.

## Slide 4: Evaluation on solution 1
Other issues unclear:
  Whether this solution 1 will impact PCF or not? It is related with the identification of RAT type in finer granularity, such as LTE, NG-RAN, WLAN or fixed access network, etc.
  As defined by solution 1, this MA PDU session is authorized based on the local policy configured in PGW-C+SMF, why not decided by PCF? What will happen if the request is rejected? Is the PDN connection or MA PDU session released or accepted but fallback to the normal PDN connection or normal MA PDU session?
Impact on the UE, if the same solution is applied to the UE, further consideration on the UE mobility, the roaming case and the relationship with NBIFOM solution.
  In roaming case, the SGW shall identify the UE based on the UE IP address in order to perform the charging control. So there will be a problem if the packets are encapsulated by the UE’s MPTCP IP address, different from the UE IP allocated by PDN connection. If to solve this problem, some impact on the SGW cannot be avoided.
  For the EPC side
    As analysis before, the solution 1 will impact the NAS message, so the current 4G NAS module shall be upgraded.
    The UE may also support the NBIFOM solution. So what is the relationship between the NBIFOM solution and solution 1?
  For the 5GC side
    When the UE is moving, e.g. out of the LTE coverage, how to update the MA PDU session when the other leg PDN connection is released?
    What will happen if the UE leave the 5GC coverage, and the MA PDU session via 5GC is released?
Observation 1: The solution 1 has more impact on the 5GC and terminal side.
Observation 2: It is unclear whether solution 1 can be used by UE. If not, it will be more complicated for the 5GC to distinguish the UE and 5G-RG with the different solution.

## Slide 5: Alternative solutions
Solution 2:
  Reuse the MPTCP functionality in the UE and UPF.
  Establish a separate PDN connection and a single-access PDU session via EPC and 5GC.
  Notify the UE via 5GC to bind the PDN connection and single-access PDU session together with the MPTCP functionality.
  Evaluation on solution 2:
    Pro: totally no impact on the EPC side, especially no impact on 4G NAS.
    Con: new solution, need further study on Rel 17. Only support the ATSSS for IP/TCP traffic based on the MPTCP functionality. Cannot support the ATSSS-LL functionality.
Solution 3:
  Similar with solution 1, except for the EPC side, reuse the NBIFOM solution. Then access availability can be decided based on the RAN rule as supported by NBIFOM.
  Evaluation on solution 3:
    Pro: no impact on the 4G NAS, reuse the RAN rule to decide the access availability.
    Con: new solution, need further study on Rel-17. Impact on SGW in roaming case if MPTCP functionality is activated.
N4
HSS+ UDM
PCF
AMF
AGF / TNGF / N3IWF
eNB
MME
SGW
UPF+ PGW-U
SMF+ PGW-C
UE / 5G-RG
Non-3GPP / wireline
S11
S6a
S1-MME
S1-U
S5-U
S5-C
N10
N15
N11
N3
N2
N7
DN
MPTCP
PDN connection
PDU session
PDU session
PDN connection
Solution 2
MPTCP
Bind the PDN and PDU session with MPTCP function
Observation 3: There are other possible solutions which can support the multi-access via EPC and 5GC, but not analysed yet.

## Slide 6: Proposal
It is proposed to postpone the multi-access via 5GC and EPC case to Release 17.
  The scenario is out of the scope of ATSSS WID, and for now there is only one SA2 meeting for Rel-16.
  No solution is discussed from both UE and 5G-RG point of view.
  Other possible solutions are not studied.