## Slide 1
What is ATSSS Interworking with EPC in Rel-16
&
What is the way forward?
ZTE
3GPP TSG-SA WG2 Meeting #133 S2-1905767
May 13 - 17, 2019, Reno, USA

## Slide 2
The intent of this discussion paper is NOT to champion one proposal over the other, but rather to solicit feedback and agreements to drive the way forward.

## Slide 3
What is ATSSS Interworking with EPC?
What has been defined for ATSSS today?
According to TS 23.501, clause 5.32.1……
“ The ATSSS feature is an optional feature that may be supported by the UE and the 5GC network.
The ATSSS feature enables a multi-access PDU Connectivity Service, which can exchange PDUs between the UE and a data network by simultaneously using one 3GPP access network and one non-3GPP access network. The multi-access PDU Connectivity Service is realized by establishing a Multi-Access PDU (MA PDU) Session, i.e. a PDU Session that may have user-plane resources on two access networks.
The UE may request a MA PDU Session when the UE is registered via both 3GPP and non-3GPP accesses, or when the UE is registered via one access only.”
Observation#1:
Current scope for supporting ATSSS MA PDU session “simultaneously” over 3GPP and non-3GPP accesses is within 5GS.
Question:
Are we going to expand the support for ATSSS MA PDU session beyond 5GS system in Rel-16? More specifically, are we going to expand the support for ATSSS MA PDU session for two different access types spans across two systems – i.e. EPS and 5GS in Rel-16?
Do we may need to expand the TS 23.401 to support the MA PDN connection

## Slide 4
How to deliver the ATSSS rules when the UE establish MA PDN connection in EPC
Observation#1:
When 5G-RG establishes the PDU connection in the EPC, the 5G-RG may have not registered with 5GC yet This implies that, the 5G-RG may not have any URSP rule nor ATSSS rule given the UE has not been registered with 5GC.
Question:
How does 5G-RG decides whether to establish MA PDN Connection or single access PDN connection when the 5G-RG is in EPS. Should the decision be aligned with URSP rules used in 5GS?
How does the 5G-RG obtain the ATSSS rules during the MA-PDN Connection establishment over EPC? If TR-69 is used, are we going to define interface between PCF and ACS server so as the SMF can receives corresponding PCC rules from PCF?

## Slide 5
Miscellaneous Considerations
How to assign two IP addresses to UE to support ATSSS-HL (i.e. MPTCP) if the MA PDN connection is established first in the EPS?