## Slide 1: Way Forward on emergency calls from CAG
Qualcomm Inc.
SA WG2 Meeting #133 S2-1905814
13 – 17 May 2019 Reno, USA

## Slide 2: Background – CAG support per PLMN
TS 23.501 clause 5.30.3.2 & clause 5.30.3.4:
5.30.3.2 Identifiers
The following is required for identification:
- A CAG is identified by a CAG Identifier which is unique within the scope of a PLMN ID;
- A CAG cell broadcasts one or multiple CAG Identifiers per PLMN;
NOTE 1: It is assumed that an NG-RAN node supports broadcasting a total of twelve CAG Identifiers. Further details are defined in TS 38.331 [28].
[…]
5.30.3.4 Network and cell (re-)selection, and access control
The following is assumed for network and cell selection, and access control:
- The CAG cell shall broadcast information such that only UEs supporting CAG are accessing the cell;
NOTE: The above also implies that cells are either CAG cells or normal PLMN cells.
[…]

## Slide 3: Observations
Observation 1: CAG identifier is per PLMN (unlike CSG that is per cell)
Observation 2: A cell can either be CAG cell for all sharing PLMNs or normal cell for all sharing PLMNs

## Slide 4: Background – barring non-authorised UEs
TS 23.501 clause 5.30.3.1 & clause 5.30.3.4:
5.30.3.1 General
[..]
CAG is used for the Public network integrated NPNs to prevent UE(s), which are not allowed to access the NPN via the associated cell(s), from automatically selecting and accessing the associated cell(s).
[…]
5.30.3.4 Network and cell (re-)selection, and access control
The following is assumed for network and cell selection, and access control:
-The CAG cell shall broadcast information such that only UEs supporting CAG are accessing the cell;

## Slide 5: Observations
Observation 3: Only UEs “supporting CAG” are allowed to access the CAG cell

## Slide 6: Background –CAG support is optional in rel.16
C1-192481 CR to TS 23.122 (agreed at CT1#116) :
3.y CAG selection (N1 mode only)
The MS may support CAG.
If the MS supports CAG:
[…]

## Slide 7: Observations
Observation 4: CAG support is optional even for rel.16 UEs
But treating a CAG cell as acceptable cell could be possible for rel.16 UE since new behaviour can be defined

## Slide 8: Proposals
Proposal 1: CAG cell is considered “barred” for rel.15 UEs. Therefore CAG cell cannot be considered acceptable cell for such UEs (i.e. no support for emergency calls)
Proposal 2: CAG cell is considered acceptable cell for all rel.16 UEs that support CAG but are not authorised to access the specific CAG cell or do not support CAG
Proposal 3: Other than AS idle mode behaviour (see proposals 1,2) the rest of the procedures for emergency calls (i.e. domain selection) remain unaffected for PNI-NPN

## Slide 9: Way forward
SA2 to expect that related AS idle mode procedures will be documented in TS 38.304
SA2 to send LS to RAN2 with expected behaviour BUT NOT hinting use of specific encoding (leave up to RAN2 to decide) i.e. send LS communicating SA2 requirements (see proposal 1,2,3)
SA2 to document text in TS 23.501 (& TS 23.502 if needed) assuming a “forward looking” reference to TS 38.304