## Slide 1: Principles for delegated SMF discovery
NTT DOCOMO
SA WG2 Meeting #133 S2-1906514
13 – 17 May 2019 Reno, USA

## Slide 2: Generic principles (everyone agrees?)
Principle 1: Avoid 3GPP specific functionality in SCP.
Principle 2: Similar procedures are used for I-SMF and V-SMF delegated discovery

## Slide 3: Option A (NTT DOCOMO)
Principle A.1: AMF and V-SMF/I-SMF both use the same discovery model, i.e. either delegated discovery or regular discovery.
Principle A.2: When AMF uses the delegated discovery, the V-SMF/I-SMF does not receive the H-SMF address in the SMcontext create request.
Principle A.3: When AMF uses the delegated discovery, the AMF obtains the SMF Service Area from the respective SMF

## Slide 4: Option A
Procedure (see CRs for more details)
AMF sends Nsmf_PDUSession_CreateSMContext Request to SCP. The request indicates UE location to be used as a selection parameter for the SCP. HR roaming: The request indicates target PLMN ID for the H-SMF (HPLMN ID).
SCP selects the I-SMF/V-SMF from the serving PLMN.
I-SMF/V-SMF sends Nsmf_PDUSession_Create Request to SCP.
SCP discovers the H-SMF/SMF
V-SMF/SMF report the Service Area to AMF using the SMF event exposure service (if the AMF has cached the Service Area, the AMF does not need to obtain it from the SMF) This change to the CR is to address the comment from Laurent, how to avoid sending the Service Area in every PDU session setup.

## Slide 5
AMF
1. Request (selection and discovery parameters
3. Request
4. Response
5. Response
2. Discovery of V-SMF
Option A
SCP
V-SMF
8. Request
9. Response
7. Discovery of H-SMF
SCP
H-SMF
6. Request

## Slide 6: Option B (Ericsson)
Principle B.1: The AMF should retain the same roaming logic and configuration in Rel-16
Principle B.2: The AMF should not need to know if V-SMF has discovery or not.
Principle B.3: The AMF retains the same logic and configuration for communication modes A-D when deciding if a H-PCF and/or H-SMF are needed and indicates this to SCP (when used).

## Slide 7: Option B (Ericsson)
Discovery and Selection rules (see CRs for more details)
For roaming, AMF decides if H-PCF is needed, indicates this to SCP, SCP sends H-PCF and V-PCF ID to AMF in the response. AMF add H-PCF ID in the discovery and selection parameters sent to SCP.
For roaming, V-PCF adds the H-PCF ID to the discovery and selection parameters sent to SCP.
For non-roaming (and no H-PCF needed), AMF establishes the AMF and UE policy associations in sequence starting with AM policy. SCP add the PCF ID of in response to the AM policy association request, AMF adds the PCF ID in the discovery and selection parameters sent to SCP in the UE policy establishment request.
If H-SMF is needed AMF indicates this to SCP in the request to establish a PDU session.
SCP adds the H-SMF in the message body of the Request and sends it to selected V-SMF

## Slide 8
AMF
1. Request (selection and discovery parameters (H-SMF is needed)
3. Request (Insert H-SMF address)
4. Response
5. Response
2a. Discovery of V-SMF
2b. Discovery of H-SMF
Option B
SCP
V-SMF
8. Request
9. Response
SCP
H-SMF
6. Request

## Slide 9: Option C (Huawei)
Principle C.1: AMF does not use delegated discovery in HR roaming, or if the PLMN is configured to support ETSUN

## Slide 10: Option D (Huawei, Ericsson)
SCP rejects the request with the H-SMF’s address. If AMF gets a reject with the H-SMF’s address, the AMF adds the H-SMF’s address to the message body

## Slide 11
AMF
1. Request (selection and discovery parameters for H-SMF)
4. Request
6. Response
3. Error Response (insert H-SMF ID)
2. Discovery of H-SMF
Option D
SCP
V-SMF
8. Request
7. Response
SCP
H-SMF
5. Request
9. Request
10. Response

## Slide 12: Proposed way forward
Initially the AMF follows the procedure in Option A
If the SCP cannot find a V-SMF/I-SMF that uses a delegated discovery, either a) SCP reports an error to AMF. If the AMF receives the error, AMF falls back to non-delegated discovery procedures, i.e. discovers the SMFs from the NRF, or b) SCP discovers a V-SMF/I-SMF that does not use delegated discovery. SCP discovers a H-SMF, and inserts the H-SMF ID to the request the SCP sends to the V-SMF/I-SMF