## Slide 1
5G-GUTI re-assignment for 5G MT-EDT
Hannu Hietalahti
24.2.2020
S2-2002260r1

## Slide 2: 5G MT-EDT challenges
SA3 requires that the same 5G-S-TMSI value shall be used for paging only once
5G-GUTI re-assignment is designed for UE NAS level acknowledgement to ensure the UE has received the newly assigned 5G-GUTI
  Re-use of 5G-S-TMSI violates SA3 requirement by opening up a privacy threat
  Re-assignment of 5G-GUTI without NAS acknowledgement is not acceptable, as it risks out of sync situation between UE and AMF.
Recovery via fallback to old 5G-GUTI is technically possible, but it wastes paging resources
  Paging with 5G-GUTI_1 in previous serving cell (incl. paging repetitions)
  Paging with 5G-GUTI_1 in neighbor cells and eventually across all cells supported by AMF (including paging repetitions in all steps)
  Paging with 5G-GUTI_2 in previous serving cell (incl. paging repetitions)
  Paging with 5G-GUTI_2 in neighbor cells and eventually across all cells supported by AMF (including paging repetitions in all steps)
MT-EDT followed by immediate 5G-GUTI re-assignment and NAS level acknowledgement eliminates the signaling optimization of MT-EDT

## Slide 3: MT-EDT using pre-assigned 5G-TMSI values
5G-GUTI assignment requires NAS acknowledgement from the UE
Re-assignment during MT-EDT should be avoided for efficient one-shot data
Multiple 5G-GUTI values could be pre-assigned using the normal NAS negotiation procedure with UE acknowledgement
5G-GUTI structure:
  <5G-GUTI> = <GUAMI><5G-TMSI>
  <GUAMI> = <MCC><MNC><AMF identifier>
Assignment of 5G-TMSI offset to derive new 5G-TMSI values associated with the same GUAMI part that was assigned as part of 5G-GUTI
Different 5G-TMSI is used with the same GUAMI to construct 5G-S-TMSI for each paging
New 5G-S-TMSI is adopted only when UE responds to paging, so no out of sync situation can occur

## Slide 4: Registration with 5G-TMSI offset assignment
(5G-GUTI, 5G-TMSI offset)
(UE capability)
UE indicates its 5G-GUTI offset capability in Registration Request (as in S2-2000264)
If UE has indicated 5G-GUTI offset capability, the AMF may assign 5G-GUTI and 5G-TMSI offset as part of Registration Accept
Registration Complete acknowledges that the UE has received both 5G-GUTI and 5G-TMSI offset
Use of 5G-TMSI offset
  UE and AMF use the assigned 5G-TMSI to derive 5G-S-TMSI for the first paging
  Service Request procedure confirms the derivation of the next 5G-S-TMSI using the assigned 5G-TMSI offset
  Paging failure does not change 5G-S-TMSI in UE or AMF
  The AMF may re-assign new 5G-GUTI (and 5G-TMSI offset) at any time

## Slide 5: MT-EDT and 5G-TMSI update
Pre-requisite 5G-TMSI offset assignment during 5G-GUTI allocation
Main principles of S2-2000264 are followed for MT-EDT
When 5G-TMSI has been used once for 5G-S-TMSI paging, both UE and AMF step up the 5G-TMSI as follows:
  New 5G-TMSI = 5G-TMSI + offset
  AMF increments 5G-TMSI by 5G-TMSI offset upon receiving CP SR in step 6
  NG-RAN sends msg4 only after 6 & 7
  UE increments 5G-TMSI by 5G-TMSI offset based on lower layer indication of successful delivery of CP SR across the radio interface in step 8
  UE condition to update 5G-TMSI follows the Registration call flow step 22 logic
AMF pages for MT-EDT using one 5G-S-TMSI

## Slide 6: 5G-GUTI re-allocation in S2-2000264
S2-2000264 proposes to change the criteria to start using newly assigned 5G-GUTI
UE does not acknowledge 5G-GUTI reception
AMF receives no NAS level acknowledgment to new 5G-GUTI
The condition to take new 5G-GUTI is weaker than in Registration and UCU:
  AMF criteria: AMF starts using 5G-GUTI based on RRC ack on the sending side of radio interface
  UE criteria: UE starts using new 5G-GUTI if it has received it
Paging does not initiate
the use of new 5G-GUTI
5G-GUTI is assigned only
in the last DL NAS message
No NAS acknowledgement
from UE

## Slide 7: 5G-GUTI re-assignment in Registration vs. 5G-TMSI offset (please view in slide show mode)
Corresponding reliability levels:
AMF indicates new 5G-GUTI
UE ack in NAS level
AMF starts using new 5G-GUTI after NAS response from UE
UE starts using new 5G-GUTI after RRC ack to NAS response sent by UE
AMF indicates new 5G-GUTI to UE and
MT-EDT triggers the need for
5G-GUTI generation
AMF takes new 5G-GUTI in use after
NAS acknowledgement from UE
UE and AMF know new 5G-GUTI is needed but it’s not confirmed yet
UE sends NAS acknowledgement
UE takes new 5G-GUTI in use after
RRC ack to RRC msg containing NAS ack
Both 5G-TMSI delivery methods are
Equally secure

## Slide 8: Error handling during 5G-TMSI generation
Whichever side takes the lead in three-way negotiation, the last step is always acknowledged in RRC layer
Secure delivery of new temporary identity follows the three-way negotiation principle used in Registration procedure
Possible loss of the last RRC message in step 8 cannot be prevented, but it is no more likely than in Registration procedure
AMF error recovery if RRC message in step 8 is lost
If step 8 fails, then lower layers attempt to re-transmit the same message for 100 – 2000 ms
UE NAS level criteria to adopt new 5G-GUTI is not met until step 8 is completed
Based on UE re-transmitted CP SR with old 5G-GUTI (step 6a), the AMF falls back to the previous 5G-GUTI when responding in step 7a with SR
If the re-transmission is completed successfully (as in step 8a), the AMF knows that the procedure was successful and starts using new 5G-GUTI
AMF must handle error recover in any case, but:
Error recovery during 5G-GUTI assignment is more efficient than paging fallback using multiple 5G-GUTIs
Lower layers detect
missing ACK
AMF error recovery:
AMF falls back to old 5G-GUTI until the re-transmission procedure is completed successfully
In step 8a
Lower layer
re-transmission

## Slide 9: Conclusion
Registration / UCU assign 5G-TMSI offset to UE along with new 5G-GUTI
  No change in 5G-TMSI assignment reliability
New 5G-TMSI value is first indicated in DL NAS message
  Explicitly assigned 5G-GUTI value (Registration/UCU)
  Indication of generate new 5G-TMSI value using already received 5G-TMSI offset (MT-EDT)
Reception / generation of new 5G-GUTI value does not take it in active use yet
Adoption of new 5G-GUTI requires UE NAS level acknowledgement
AMF starts using new 5G-GUTI in use after UE NAS level acknowledgement
UE starts using 5G-GUTI after RRC ack to UE NAS level acknowledgment
5G-TMSI offset is as reliable means to deliver new 5G-GUTI as Registration and UCU procedures in TS 23.502