## Slide 1: Correcting UPF selection for 5G TSN Bridge (read me first) Background information on submitted S2-2003044, S2-2003083, S2-2003101, S2-2003105
Intel

## Slide 2: Problem statement
TS 23.501 clause 5.28.1 currently states that the UPF hosting a specific TSN bridge is selected as follows:
  The UPF is selected for a PDU Session serving TSC based on subscribed DNN, traffic classes and VLANs.
“traffic classes” and “VLANs” are obviously not usable and need to be removed. Only DNN makes sense
However, using DNN alone for selecting the UPF that hosts a specific TSN bridge implies that the DNN meaning needs to be overloaded with the TSN bridge identity
  E.g. if the 5GS supports 100 TSN bridges, it will have to support 100 different DNNs

## Slide 3: Solution 1: subscription based
In this solution the Bridge Name (an existing parameter) is used as a unique TSN bridge identity and allows for UPF selection along with the DNN
  The Bridge Name is stored in the session management subscription data
  This solution is implemented in S2-2003044 and S2-2003083 (for 23.501 and 23.502, respectively)

## Slide 4: Solution 2: DS-TT based
In this solution again the Bridge Name (an existing parameter) is used as a unique TSN bridge identity and allows for UPF selection along with the DNN
  The Bridge Name is provided by DS-TT/UE upon PDU Session establishment
  This solution is implemented in S2-2003101 and S2-2003105 (for 23.501 and 23.502, respectively)

## Slide 5: Proposal
It is proposed to agree either of the two solutions, not both

## Slide 6: Other
Why use the Bridge Name as unique TSN bridge identity?
  The current specification has three TSN bridge identities:
    Bridge Name
    Bridge MAC address
    Bridge ID (derived from Bridge MAC address)
  If NW-TT supports multiple ports, the Bridge MAC address may become obsolete
  On the other hand, Bridge ID is currently signalled from UPF to SMF/PCF/AF in during the TSN bridge reporting phase. Using Bridge ID (instead of Bridge Name) as the unique TSN bridge identity may require more extensive specification changes